## Slide 1
eRD104 Powering Update
09/05/2022
Notes: The abstract pattern can be removed or repositioned if required. Be careful to ‘Send to Back’ so that it does not obscure any important information.

## Slide 2
Background
eRD104 Deliverables
  Intermediate Report on Serial and DC-DC Powering
  Final Report on Serial and DC-DC Powering (FY22) report
Previous Work
  Powering Options for an EIC Silicon Tracker – A. Collu and L. Greiner (https://www.eicug.org/web/sites/default/files/Powering-options-for-an-EIC-silicon-tracker.pdf)
  Studied external DC-DC converters, and in-silicon serial powering
  Conclusions:
    DC-DC converter: Low risk, reduced material budget if kept to the sides, many additional components (barrel 210 – 1700, disks 125-1000)
    Serial Powering: Higher risk, lower material budget
  Talk by Peter Philips at previous meeting - https://indico.bnl.gov/event/14948/contributions/60508/subcontributions/1796/attachments/40039/66750/20220228_ITkStripPower.pdf

## Slide 3
Goals
Powering Scheme - General
  Begin detailed studies in RAL PPD on the EIC powering scheme
    What would a powering scheme for the EIC look like? Can we keep the same configuration (esp. on large area sensors/modules)?
    What current are we looking at per sensor/module?
    Will vertex layers, staves, disks be powered in the same way? Depends on stave/disk design - possibly fits well with work in eRD111.
Serial Powering
  Once ER1 is submitted, start work on a shunt regulator (probably based on existing work done for ATLAS and CMS)
  Will allow the feasibility of this approach to be evaluated