## Slide 1: Evaluating barrel ECal options discussion
erhtjhtyhy
This work was partially supported under grant DE-AC02-06CH11357 from the US Department of Energy, Office of Nuclear Physics

## Slide 2: Our Task
From the Calo WG’s charge:
  For each non-trivial difference working groups will then work to prepare a pro/con list accounting for technical performance, risk and cost. The resolution of non-trivial differences should be discussed in close consultation with the Global detector/integration WG, physics working groups, the EIC project, relevant detector consortia and R&D efforts.
Evaluation of options based on:
Performance
Risk
Cost
Integration

## Slide 3: Potential physics channels to benchmark barrel ECAL performance
Summary of YR requirements: | 
Parameter | Driven by
Pion suppression: 104 | Inclusive ALL and PV asymmetries
separation | p < 15 GeV/c DVCS?? I need to find this.
Minimum E: 50 MeV | Exclusive diffractive vector meson production in eA
Hermiticity | inclusive diffraction (ep→eXp) using the rapidity gap method
Energy resolution: 10-12/√E + (1-3)% | deemed sufficient by all working groups (except ‘exclusive’, who had no comment)
Spatial Resolution | 
Summary of YR requirements: | 
Parameter | Driven by
Pion suppression: 104 | Inclusive ALL and PV asymmetries
 | p < 15 GeV/c DVCS?? I need to find this.
Minimum E: 50 MeV | Exclusive diffractive vector meson production in eA
Hermiticity | inclusive diffraction (ep→eXp) using the rapidity gap method
Energy resolution: 10-12/√E + (1-3)% | deemed sufficient by all working groups (except ‘exclusive’, who had no comment)
Spatial Resolution | 

## Slide 4: Performance
Imaging/SciFi
Hermicity
  Good
  Stave edges in may have some gap due to support structure
    Is there a study on these effects?
Energy Resolution:
  Easily meets energy resolution requirements
Minimum Energy
SciGlass Pros:
Hermicity
  Good
  Cracks due to limited module type
    Is there a study on these effects?
Energy Resolution:
  Easily meets energy resolution requirements
Minimum Energy
My Fault, I ran out of time to find this.

## Slide 5: Performance
Imaging/SciFi
Pion Rejection
SciGlass Pros:
Pion Rejection
This must be studied as part of an integrated detector simulation as pion rejection can be done with other elements of the spectrometer as well
  p > 1 GeV/c:
    R > 1000 in realistic simulation while maintaining efficiency > 85%. (In ideal case its R > 3000 and eff > 95%)
  0.6 < p < 1 GeV/c:
    R > 300 with efficiency > 82% in realistic simulation (Ideal: R> 400 and eff > 95%)
My Fault, I ran out of time to find this.

## Slide 6: Performance
Imaging/SciFi
Pion Rejection
SciGlass Pros:
Pion Rejection
  p > 1 GeV/c:
    R > 1000 in realistic simulation while maintaining efficiency > 85%. (In ideal case its R > 3000 and eff > 95%)
  0.6 < p < 1 GeV/c:
    R > 300 with efficiency > 82% in realistic simulation (Ideal: R> 400 and eff > 95%)

## Slide 7: Integration
Imaging/SciFi
Construction based on ”wedges” in
Can match DIRC geometry
Compact
  Could move radially outward, providing more room for tracking
  Needs simulation
Can work as Inner Barrel HCal
Imaging/SciFi Con:
Production time
SciGlass Pros:
homogenous calorimeter
  Single readout electronics
Mechanical construction based on ”wedges” in
Production easily fits within Project timeframe.
SciGlass Cons:
Individual wedges can be removed

## Slide 8: Cost
 | In M$ | M&S | Labor |  |  | Totals |  | In M$ | M&S | Labor | Totals
Detector | Pb SciFi Detector | $ 7.7 | $ 4.5 |  |  | $ 12.2 |  | SciGlass | 14.2 | 0.8 | 15
 | Imaging Detector | $ 6.3 | $ 4.8 |  |  | $ 11.1 |  |  |  |  | 
 | Total Detector | $ 14.0 | $ 9.3 |  |  | $ 23.3 |  |  |  |  | 
Readout | Pb SciFi Readout | $ 1.8 | $ 0.3 |  |  | $ 2.1 |  | SciGlass Readout | 1.5 |  | 1.5
 | Imaging Readout | $ 0.4 | $ 1.8 |  |  | $ 2.2 |  |  |  |  | 
 | Total Readout | $ 2.2 | $ 2.1 |  |  | $ 4.3 |  |  |  |  | 
Totals | Total Pb/SciFi | $ 9.5 | $ 4.7 |  |  | $ 14.2 |  | Total SciGlass | 15.7 | 0.8 | 16.5
 | Total Imaging | $ 6.7 | $ 6.6 |  |  | $ 13.3 |  |  |  |  | 
 | Grand Total |  |  |  |  | $ 27.5 |  | Grand Total |  |  | $ 16.5
Notes on readout | Notes on readout | PbScifi | includes SiPMs, Digitizer and FEE. |  |  |  |  |  |  |  | 
 |  | Imaging | readout include up to first aggregator |  |  |  |  |  |  |  | 
 |  | SciGlass | readout includes only SiPM. |  |  |  |  |  |  |  | 
Additional Notes | Additional Notes | PbScifi | budget is for 410 cm long. This could be reduced to 360 cm. |  |  |  |  |  |  |  | 
 |  |  | can use 1 or 4 SIPMs/channel \delta = $0.8M |  |  |  |  |  |  |  | 
 |  |  | Budget can vary based on density of sampling and commodity (Pb or W) prices |  |  |  |  |  |  |  | 
 |  | Imaging | first layer may replace MPGD layer |  |  |  |  |  |  |  | 

## Slide 9: Labor Rates
Labor Skill Set |  | Cost per hour for each skill set |  | Labor Skill Set |  | Cost per hour for each skill set
Scientist |  | $157.05 |  | Mechanical Tech |  | $101.01
PostDoc |  | $70.99 |  | Electrical Engineer |  | $153.17
PhD Student |  | $20.00 |  | Electrical Designer |  | $116.10
Undergrad |  | $20.00 |  | Electrical Tech |  | $101.01
Mechanical Engineer |  | $153.17 |  | Software Expert |  | $178.24
Mechanical Designer |  | $116.10 |  | Other |  | $0.00

## Slide 10
Barrel Electromagnetic Calorimeter Questions
Revised 09 June 2022 #2
What is the pion subtraction factor at 90%, and 95% electron efficiency with a 1.5 T magnetic field for the calorimeter in Detector I geometry (Detector I material in front of the calorimeter sitting at r=80 cm)?
What is the 2 gammas merging probability ( discrimination) for the normal incident angle for the calorimeter at r=80 cm in Detector-I geometry, as a function of the distance from the edge of a calorimeter module? If the separation in eta/phi has a different dependence, please quote them separately, and quantify the ability isolate the energy of the two clusters.
What are the efficiency, and purity (background subtraction) of for DVCS photons as a function of eta in the required for the EIC phase-space with the proposed Barrel ECAL?
What is the impact on inclusive DIS measurement with the achieved e/ separation for your calorimeter?
In discussions comments have been made about technology choices prioritizing a specific physics subset. Was such a prioritization made in each technology choice? If so, please clearly describe the tradeoffs that were made?
What are the expected energy and spatial resolution? Are there beam test or in-experiment data confirming these numbers?
Both technologies are requested to develop an estimated cost that includes material, labor, electronics and in-kind contributions, at the same level as the estimate for the DPAP review.