## Slide 1: ITS3_EIC contribution plan
EIC_SC
presented: G.W.Deptuch
05/12/2022

## Slide 2: plan for contributing to ITS3 + developing EIC (1)
(1) It is expected that the ALICE ITS3 sensor will fulfill the requirements of the EIC tracking layer as self-supporting layers and on staves for the inner and outer tracking layers, respectively (assuming that the required pixel pitch and other requirements are not changed),
(2) Also, the ALICE ITS3 sensors will be suitable for the staves and disks in the EIC, where the responsibility of the EIC developers will consist in adapting the ALICE ITS3 development to the form of the EIC Large Area Sensors (LAS),
In both above cases (1, 2), the major circuital blocks are much probably to be imported from the ALICE ITS3 and the design efforts will be organized around the tasks, such as:
  reorganizing the design into the forms suited for staves and disks,
  setting on stitching methodology, organization of the readout (TDM or DATA concentrating), low noise powering and power distribution, etc.
  unless important changes with respect to the ALICE ITS3 development are to be entailed by the EIC physics that needs to be shown,

## Slide 3: plan for contributing to ITS3 + developing EIC (2)
It is expected that the EIC groups contribute to the ALICE ITS3 developments in a significant enough (although what is enough is not quantifiably measurable) degree that the ALICE ITS3 database could be shared for the purposes of the development of the EIC MAPS detectors (vertexing, stave and disks),
In this moment, the ALICE ITS3 developments are significantly advanced and prior proposals from the US EIC groups for the design contributions seem to be obsolete and, knowing the CERN submission schedules, it is hard to consider developments of independent, small blocks that could be prototyped first on the MLRs runs and then used in the final ALICE ITS3 chips,
The development needs to be discussed and negotiated with the ALICE ITS3, targeting things that are not covered yet and (best if) needed for the EIC later,
The EIC groups are in effect (with emphasis on the US side) need to turn to the CERN ALICE ITS3 - EP group to discuss the list of contributions – to identify the immanent needs,

## Slide 4: plan for contributing to ITS3 + developing EIC (3)
At least three areas can be considered as the EIC groups contribution to the ALICE ITS3 development:
  (1) Studies on serial powering and development of the required circuits for the serial powering with the development of shunt-LDOs and power distribution management features (to handle e.g. powering down and overvoltage/overcurrent emergencies) with an impact on AC-coupling of interconnects, data transfer etc., as an alternative to DC-DC converters for reduction of mass inside the detector,
  (2) Taking on verification for the ALICE ITS3 detectors, as this area is not covered by the ALICE ITS3 efforts so far but is needed for assuring successful development of the detectors and integration them in the readout/supply systems. The efforts would consist in:
    developing of the full model of the sensor chips code using SystemVerilog – UVM (or SystemC),
    architecting data flows pathways, defining standards and interfaces in the system,
    developing data flow models starting with the physics-level simulation database interfaces (to vertexing and tracking layers with MAPS),
    covering data formation for transfer (transmission encoding, error protection boundary scan for testability) - data flow channels - data acquisition upstream slow control downstream, connecting different databases from Geant4, through Python to SystemVerilog (SystemC) UVM, build UVM components (drivers, monitors, sequencers, agents, env, scoreboards and subscribers) of the system plugged into operational ecosystem of the ALICE experiment,
    developing plans for regressions testing with coverage and random stimulus, verification stimuli data, coverage regression and scoreboards results, etc.,
  (3) Live function monitoring (medium resolution, slow ADC) of the internal operation of the ALICE ITS3 chip, including digitization of bias settings of currents and voltages, temperature readouts etc.

## Slide 5: plan for contributing to ITS3 + developing EIC (4)
The serial powering is less appealing for the ALICE-ITS3 development, whereas ALICE-3 (certainly) and EIC (probably) will be the targets,
The first two mentioned activities will be transferable to the major conceptual EIC efforts as equally needed also they serve for the eRD104 resource reduction,
Involvement into the verification is challenging as it is a sizeable effort, requires suitable composition of the workforce, but is a natural pathway for very close relation with the ALICE ITS3 efforts and familiarity with the ALICE ITS-3 database (towards the EIC development),
Other areas of contribution to the ALICE ITS3 efforts can be identified upon meeting with the CERN ALICE ITS3 - EP group.

## Slide 6: Plan for the EIC ERs (MLRs) submissions
CERN ITS3-EP submission plans of MLRs and Ers do not go beyond the ALICE-ITS3 scope,
CERN ITS3-EP and TPSCo must be informed about submission plans for the EIC ERs and PRs for LAS:
  at least two ERs in 2023 and 2024,
  and one PR 2025.

## Slide 7: Agreements (1)
The TPSCo NDA has been signed by all institutions contributing to the ALICE ITS3 (access to PDK),
Under the TPSCo NDA, design work can be carried out locally and the design results can be exchanged with CERN in a form of GDSII files suitable for fabrication, like for an MPW service – what is good for being part of MLRs but not ERs,
Inclusion of the developed objects in a commonly (to be) designed chip requires more than TPSCo NDA,
Also, there are no MPWs runs available under the TPSCo NDA through CERN, except the two past MLRs,
US EIC groups do not require any CAD/EDA licensing agreements to contribute a the full-functionality chip design in contrast to the groups associated with Europractice due to the different license scheme for the design tools in the US,
The US EIC groups (RAL as well) do not have formalized background at which contributions to the ALICE ITS3 development could be provided, this is related to either:
  (1) physically designed circuits in a form of libraries or cells (such as OA databases),
  (2) hardware description language code, such as RTL for synthesis (GIT repo, etc.), or
  (3) Verification code (SystemVerilog, UVM, SystemC), verification stimuli data, coverage regression and scoreboards results, etc.,
this stills needs to be addressed.

## Slide 8: Agreements (2)
For the US EIC, and generally for the EIC, groups, an overarching agreement between the EIC-SC ASIC groups and the CERN ITS3 (ALICE) is needed to regulate scopes of the contributive work and permitted usage of the developed material (1, 2, 3). Such an agreement is needed in order to:
  open access to the ITS3 MAPS databases (and related to this, other libraries, including for example DFM improved standard cells libraries that are enhanced with respect of the original PDK, modified models, yield data, etc.) by ALICE ITS3,
  provide contributions (1, 2, 3) to the common database by the US EIC groups (and also other EIC groups),
The efforts should not wait for the agreement, but ultimately it will be needed.
Ultimately, after having the overarching agreement in place, the EIC groups should:
  target getting access to the common ALICE ITS3 Cliosoft (or other DM) repository,
  generate own EIC Cliosoft (or other DM), and
  share it with ALICE ITS3 for carrying our contribution to the ALICE ITS3 efforts and to carry out the EIC efforts in the most efficient way (BNL can offer hosting the repository for the EIC efforts),
The Detector-1 collaboration needs to push DOE to arrange the overarching MoU with CERN, which would be the starting point for the specific sharing “agreements” described above.