## Slide 1: GENERAL D1 tracking / PID comments
Original ECCE tracking / PID setup does not fit the YR request.
-- “Fast” simulations were dome using unrealistic material thickness and hit smearing parameters with a misleading conclusion.
-- BaBar magnet, 1.4 T B-field is not good enough for high precision momentum reconstruction.
-- Very small number hits / track is extremely “sensitive” to background.
-- PID (ToF) proposed R-position does not work up to 0.3 GeV/c (~30% of all particles in +/- 1.5 rapidity).
2. A lot of barrel tracking simulation were done for (1. – 20.) GeV/c. The optimization should be done for (0.1 – 1.0) GeV/c (>85% of all (hadron) particles).
3. It should be checked / simulated the option of the barrel (+/- 1 rapidity) with miniTPC on (low mass, very good PID up to 0.7 GeV/c, ~3000 hits / track – exactly fits all demands for low momentum particle track finding and reconstruction ),
and “projective” setup for +/- ( 1. – 1.5) rapidity. (Alexander’s original idea; see next slide).
4. Expedite the production of the “spare” magnet with ~(2. – 2.5) T B-field.

## Slide 2: Cartoon, as an idea for possible D1 setup
MPGD
Si / MPGD
µiniTPC
DIRC
AC-LGAD
Si
Si
 = +1.
 = +1.5
 = -1.
50 100 150 200
-200 -150 -100 -50
50
100
AC-LGAD
pfRICH
dRICH
AC-LGAD
ToF
ToF
 = -1.5

## Slide 3: Cartoon  (KG modif), as an idea for possible D1 setup
MPGD
Si / MPGD
µiniTPC
DIRC
AC-LGAD
Si
Si
 = +1.
 = +1.5
 = -1.
50 100 150 200
-200 -150 -100 -50
50
100
AC-LGAD
dRICH
AC-LGAD
ToF
MPGD
 = -1.5
pfRICH or mRICH