## Slide 1: Reinforcement Learning applied to Optimization of LHC beams in the CERN Proton Synchrotron
Presenter: Joel Wulff
Date of presentation: 2/11/2022
Acknowledgements: A. Lasheen,
CPS operation crew
Special thanks to the Center for Bright Beams for the student grant to attend this event

## Slide 2: Part 1: Introduction and motivation

## Slide 3: The CERN accelerator complex
A complex combination of accelerators and experiments.
Particles used for the LHC go through a cascade of 4 separate accelerators before injection.
  The nominal bunch spacing of 25 ns is created in the Proton Synchrotron (PS) through a series of RF manipulations.
  These manipulations need to be carefully optimized to create good quality beams for the LHC.

## Slide 4: RF manipulations in the PS
The PS has a large number of RF systems covering a wide range of RF harmonics, allowing for plenty of RF manipulations.
All RF voltage programs and RF manipulations for the BCMS cycle, an LHC type beam.
The relevant parameters are the RF amplitude and phase, that can be adjusted for each harmonic to produce the desired bunch characteristics.

## Slide 5: RF manipulations in the PS
Ongoing project at CERN: automate setup and optimization of RF manipulations in the PS
Presently, settings are adjusted manually, which
  Takes time,
  Relies on operator experience,
  Risks performance inconsistency due to qualitative judgements of when the beam is “good enough”.
Initial focus on RF splittings,
  Quadruple splittings
  Triple splittings
Promising results in both cases, however focus on triple splitting for this presentation!
Bunch evolution, Quad. splitting
turn/185
t [ns]
Bunch evolution, triple splitting
turn/400
t [0.5ns]

## Slide 6: The triple splitting: Parameters, Observables and Goal
RF voltage program
Three main parameters to optimize (chosen):
  Phases and voltage,
, and .
Goal:
  All bunch-by-bunch observables equal after splitting.
  Quality measured through Mean Square Error (MSE) between bunches after splitting.
    + : Single metric that judges overall splitting quality.
    - : Many local minima…
Observables:
  Final bunch profiles,
final bunch-by-bunch length + intensity.
turn/185
t [ns]
Bunch evolution
Final profile
bins
Three simultaneously active cavities with different voltages
→ Non-linear interactions, difficult to optimize...
Figures from simulations

## Slide 7: Part 2: Automation through ML
Applying Reinforcement Learning to efficiently optimize the triple splitting

## Slide 8: Overview of the setup: Two main ML components
Feature extractor (CNN)
RL-Agent(s)
Based on supervised learning and computer vision approach to process more information and downscale it to simple, actionable parameters.
Based on deep reinforcement learning to train an agent to complete a task by taking correct actions, i.e. actually optimizing a splitting.

## Slide 9: The feature extractor
A supervised Convolutional Neural Network (CNN)
Data: series of bunch profiles over time. Similar to an image.
Simulated dataset using the BLonD tracking code
→ Necessary to acquire enough labeled data
Predicts .
Works in simulation, with small prediction errors!
Notes: For quadsplit around ~14.6k different settings simulated.
For triple splitting, ~ 55k different settings.

## Slide 10: The RL-agent
  Implemented through stable baselines 3.
  Trained in an environment of simulated data
  Acting on .
Several versions tested.
  In this presentation only the final triple splitting setup is presented.
Agent-environment interaction loop
Model-free: Soft-Actor Critic (SAC)
Bunch profile, or final bunch-by-bunch length/intensity
Adjust
phase/volt
Example
Based on end bunch by bunch profiles
For training,
simulation.
NOTE: all models (CNN/RL Agents) used have been trained on simulated data only!
Notes: For quadsplit around ~14.6k different settings simulated.
For triple splitting, ~ 55k different settings.

## Slide 11: Trial and error: different attempted approaches
1. Optimize directly
RL Agent,
{𝝓14 , 𝝓21, V14}
Sim.
2. Provide more info.
Feature extractor (CNN)
RL Agent,
{𝝓14 , 𝝓21, V14 }
Final bunch lengths/intensities
✔
Sim.
Op.
3. Simplify through segmentation
RL Agent,
{𝝓14 , 𝝓21, V14 }
RL Phase Agent,
{𝝓14 , 𝝓21}
RL Volt Agent,
{V14 }
Required decoupling of phases and voltages in loss function…
Feature extractor not accurate enough on real data…
Optimize sequentially, phase → voltage
Failed already in simulation. Why?
Perhaps not enough information…
Input:
BLs, Int.
Input:
Extract final bunch lengths/intensities
Final profile

## Slide 12: The phase and voltage losses
Figure: Scan of profile loss as a function of voltage factor for small residual phase errors.
1. Phase Loss:
Compare only the outer two bunches. From beam dynamics, we know that for almost all combinations of phase offset and voltage factor we will observe a difference in their shapes.
With optimal phase, they should always be identical! Gives a semi-voltage agnostic loss.
2. Voltage Loss: Assume phase is already optimized,
→ Optimization reduced to a univariate problem.
Reuse original three-bunch comparison,
→ Provides a nice, approximately parabolic loss curve!
Note: See the extra slides for a scan of phase losses for phase errors at different fixed voltages.
Figure: Illustration of phase loss. Isolated outer bunches are compared through MSE.

## Slide 13: Segmented RL-Agents: Setup and sim. results
Voltage Agent
Phase Agent
Training: ~20k steps (60k to best performance)
Performance: ~3 steps in simulation
Training: ~2k steps
(20k to best performance)
Performance: ~1-2 steps in simulation
Work great in simulation, what about operation?

## Slide 14: Segmented RL-Agents: direct application
Initial test: Apply the pre-trained RL-Agents directly to the output from the PS, optimizing
Phase → Voltage.
Unreliable → Succeeded most of the time, but not always. Why? An example…
In few special cases, the information contained in final profile sometimes not enough to solve the problem. Could more information be leveraged to find a better initial condition?
→ Yes, by using the pre-trained feature extractor!
Phase loss looks good on step 11,
Final profile looks in phase
Bunch evolution shows large phase error!

## Slide 15: Segmented RL-Agents: Add initial guess from CNN
Feature extractor predicts phases from bunch profiles over the entire splitting (more info.)
→ can identify errors earlier in the bunch splitting otherwise not visible in the final profile,
→ is usually within 3-10 degrees of the true offset when predicting phase,
→ can provide an initial guess leading to a better initial condition for the RL agents!
Feature extractor (CNN)
Prediction,
Action,
RL Phase Agent,
{𝝓14 , 𝝓21}
RL Volt Agent,
{V14 }
First acquisition: Initial phase guess based on CNN
Adjustments through RL agents

## Slide 16: Segmented RL-Agents: Final setup
Does it work?
First:
→ Initial phase step from feat. extr.
Provides good initial condition.
Followed by:
→ SAC-phase optimizes phase
→ SAC-Volt optimizes voltage.
CNN
Reinforcement Learning

## Slide 17: Part 3: Operational results
Applying simulation trained agents to the PS

## Slide 18: Results: SAC-Phase/Volt-Sim2Real + Feat. extr.
Example episode:
Approx. initial offset: 𝝓14 = 10, 𝝓21 = -20, Vf = 1.08
Init
Final
Phase opt. steps: 3
Volt opt. steps: 4
Total iterations required: 7

## Slide 19: Results: SAC-Phase/Volt-Sim2Real + Feat. extr.
26 Full episodes collected
  15 using LHC25ns 72b beam at 1.3e11 int/bunch (nominal beam),
  2 using LHC25ns 72b beam at 1.6e11 int/bunch (higher intensity),
  4 using LHC25ns 72b beam at 2.6e11 int/bunch (intensity for HL-LHC),
  5 using BCMS 48b beam,
    All episodes successful!
Steps required for optimization:
  Minimum: 2
  Maximum: 18
  Mean: 8.46
    Note: number of steps required influenced heavily by initial state and restrictions on actions by agents.

## Slide 20: Conclusion: Triple splitting agents
Consistent good performance for
  varying bunch intensities (1.3e11-2.6e11)
  different beam types (72b, BCMS)
Consistently rivals operators/experts in optimization steps
  Averaging ~8.5 steps per optimization (with difficult initial conditions).
Future work
  Inclusion of multi-bunch information.
  Finetune/retrain on real data
  Other RF manipulations?
  Investigate Hierarchical RL
Feature extractor (CNN)
RL Phase Agent,
{𝝓14 , 𝝓21}
RL Volt Agent,
{V14 }
Current setup:
Three networks + ext. logic
Optimized
beam
Super agent?
Other optimizations?

## Slide 21: Thank you for listening! Questions?
More examples of splittings after optimisation:
Trisplit episode: Init {15,-5,0.96}. Optimised in 10 steps.
Trisplit episode: Init {10,-5,1.04}. Optimised in 8 steps.

## Slide 22: Links and contact information
Additional information available in:
Progress with RL for controlling RF manipulations in the PS, J. Wulff, 2022 ML community forum
Reinforcement learning applied for RF manipulations in the PS, J. Wulff, 2021 ML Coffee
Summer student technical note
Optimization of RF manipulations in the PS, A. Lasheen and S. Johnston, 2020 ML Coffee
Contact information
Authors: Joel Wulff, joel.wulff@cern.ch or joel.wulff@hotmail.com,
Alexandre Lasheen, alexandre.lasheen@cern.ch

## Slide 24
Extra slides
Following this slide you will find many extra slides containing additional information for the interested individual. The order of them may be a bit confusing, but they could contain some interesting information for those of you who are extra interested.
For example, you can find some results from the agents used on the more simple quadruple splitting.
Cheers,
Joel Wulff

## Slide 25: Extra results: 11 sample episodes
Episode | Init settings [p14,p21, v14_offset] | Phase opt. | Voltage opt. | Success
1 | 20, 20, -0.08 | 5 | 7 | Yes!
2 | -20, -20, 0.10 | 8 | 3 | Yes!
3 | -20, 20, 0.10 | 8 | 3 | Yes!
4 | 20, -20, -0.01 | 9 | 5 | Yes!
5 | 15,-5,-0.05 | 3 | 6 | Yes!
6 | 15, -5, 0.05 | 1 | 1 | Yes!
7 (2.6e11) | 10, -10, -0.10 | 8 | 10 | Yes!
8 (2.6e11) | -10, 10, 0.10 | 2 | 2 | Yes!
9 (2.6e11) | 10, 10, -0.05 | 5 | 10 | Yes!
10 (BCMS) | 10, -10, 0.05 | 3 | 2 | Yes!
11 (BCMS) | -10, 10, -0.05 | 2 | 3 | Yes!
Figure: Start and end criterion for episodes 1-11. Computed using full profile loss, i.e. comparing all three bunches.
Notes: Only mention the figure and that the data is available for future reference

## Slide 26: Extra: Examples of poor/optimized triple splitting
Poor splitting:
Uneven bunch characteristics, large variations along final bunch train
Optimized splitting:
Even bunch characteristics, small variations along final bunch train

## Slide 27
Extra: Judging splitting quality, the loss function
Scan of the three-bunch loss values while varying phase errors at fixed voltages
  Shows how the “optimal” phase varies with the voltage setting.
  Compare with phase loss on next slide!
Note: the “true” minimum over these different settings is still located in voltage factor 1.0 and phases 0, 0, as expected.
Voltage factor = 0.90
Voltage factor = 0.95
Voltage factor = 1.0
Voltage factor = 1.05
Voltage factor = 1.10
Figure: Clipped losses for different fixed voltages: when voltage is changed, optimal phase also changes.

## Slide 28: Extra: The phase loss, scanning phases for set voltages
With the phase loss function, we no longer see the same variation in the loss landscape when varying voltage: as expected, the loss is (semi-) voltage agnostic.
Figure: Clipped phase losses for different fixed voltages: when voltage is changed, optimal phase also changes.
Note: The quality of the triple splitting is much more dependent on the p14 phase setting than the p21.
Voltage factor = 0.95
Voltage factor = 0.975
Voltage factor = 1.0
Voltage factor = 1.025
Voltage factor = 1.05

## Slide 29: Extra: Plots of phase/voltage optimization in example episode
Phase optimisation
Voltage optimisation
Final parameters after phase opt. : tomo/profile/relative bunch lengths/intensities
Logbook entry with some initial/final states: http://elogbook.cern.ch/eLogbook/eLogbook.jsp?shiftId=1120696
Example episode:
Approx. initial offset: p14 = 10, p21 = -20, vf = 1.08
Phase path: actions taken
Phase loss during steps
Volt loss during steps
Final parameters after volt opt. : tomo/profile/relative bunch lengths/intensities
Voltage path:
actions taken
NOTE:
First step no action taken.

## Slide 30: Example: Segmented RL-Agents only (no init. guess from CNN)
Episode | Init settings [p14,p21, v14_offset] | Phase opt. | Voltage opt. | Total steps | Comment | Success
1 | -15,5, -0.07 | 12 | 3 | 15 |  | Yes!
2 | 20,-20,-0.10 | 22+ | - | n/a | Did not finish. Failed to optimise phase to a good degree. | No.
3 | 10,-10,-0.10 | 10 | 12 | 22 |  | Yes!
Three initial episodes ran with the setup described in slide __
  Two successes, one failure.
  Generally slower than desired (>10 steps).
Figure: Init and end tomoscope acq. of ep. 1.
Why did the agents fail in this episode?
→ Explored in next slide

## Slide 31
Phase loss during optimisation: We will look closer on steps 0 and 11.
Initial acquisition: Start offset 20, -20, -0.10. Initial tomo looks very poor, final profile looks less poor.
Step 11: Phase loss below criteria, final profile has similar outer bunches. Rel. bunch lengths/intensities also similar. But, tomo acquisition shows large phase error remains → Error in observable!
Agent believes it is close to the minimum, but is actually far from it. A special case where the agent can get stuck!
Example: Segmented RL-Agents only (no init. guess from CNN)

## Slide 32: Example: Segmented RL-Agents only (no init. guess from CNN), conclusion
From this example, we know that the phase loss is not perfect:
If the initial condition is too poor, the information contained in the final profile may not be enough to solve the problem → The Agents may converge to a local minima.
Could we exploit the information in the full tomoscope acquisition in some way to achieve a better initial condition, where the final profile contains adequate information for the agents optimisation?
→ Yes, by using the pre-trained feature extractor!

## Slide 33: Extra: Approach for Quadruple splitting
The inputs were designed to be taken from a tomoscope acq. (as the simulated data for this was already available).
Calculates inputs and losses from profiles at different timings
  h=42 agent uses the profile after the first splitting is complete, but the second has yet to start.
  h=84 uses the final profile. We only care about differences caused by the second splitting, so we average together the first + third and the second + fourth bunches respectively to get only two bunches, representing the quality of the second double split.

## Slide 34: Extra: Quadruple splitting: Training and simulation results
Both new models perform well in simulation
SAC-p42 converged to good policy in ~1.5k steps (3k before best model)
  Optimising splitting in ~ 3.2 steps
SAC-p84 converged to good policy in ~2k steps (6.5k before best model)
  Converging splitting in ~ 3.01 steps
Two positives about new setup:
Training fast enough to potentially train directly in the PS during MDs.
No intrinsic need for full tomoscope acquisition (if the two profiles can be collected in some other way).

## Slide 35: Extra: MD setup: Quadsplit, SAC-p42/p84
Figure: Flowchart of MD setup. Optimisations of p42 and p84 run in parallel. Optimisation finished when both splittings are optimal (at the same time)

## Slide 36: Extra: MD Result: SAC-p42/p84 (Quadsplit)
Example episode
Approx. initial offset: p42 = -30, p84 = 20
Init
Final
Phase 42 opt. steps: 6
Phase 84 opt. steps: 8
Total supercycles required: 8

## Slide 37: Extra: MD Result: Quadsplit, SAC-p42/p84
Loss p84
Example episode:
Despite a very large initial error, optimised in < 10 steps.
No need for feature extractor
→ No need for tomoscope!
Phase path: actions taken
NOTE:
First step no action taken.
Final parameters after phase opt. : tomo/profile/relative bunch lengths/intensities

## Slide 38: Extra: MD Result: SAC-p42/p84 (Quadsplit)
11 Full episodes collected
  All using LHC25ns 72b beam at 1.3e11
    9 episodes reached criterion, 2 failed
      During the two failures the agents did not manage to reach the preset loss criterion. However, in both cases the splitting looked close to perfect on amp. spread → Criterion may be set too low, not the agents!
Mean steps required for optimisation:
  SAC-p42: 4.0 steps.
  SAC-p84: 4.64 steps.
Number of supercycles required (for both phases to be optimised):
  Mean: 5.27
  Min: 2
  Max: 9
    Note: Steps required influenced heavily by initial state and restrictions on actions by agents.
      Maximum step size for the agents is 20 degrees.

## Slide 39: Extra: MD Result: SAC-p42/p84 (Quadsplit)
Episode | Loss criterion | Init settings, [p42, p84] | p42 opt. | p84 opt. | Success
1 | 0.0008 | -10, 10 | 3 | 4 | Yes!
2 | 0.0008 | 10, -10 | 2 | 2 | Yes!
3 | 0.0005 | 15, -15 | 1 | 2 | Yes!
4 | 0.0005 | -15, 15 | 3 | 3 | Yes!
5 | 0.0005 | -10, -10 | 4 | 3 | Yes!
6 | 0.0005 | -10, -10 | (3) n/a | (2) n/a | No.
7 | 0.0005 | 20, -5 | (2) n/a | (4) n/a | No.
8 | 0.0005 | -12.5, 30 | 6 | 9 | Yes!
9 | 0.0005 | -30, 20 | 5 | 8 | Yes!
10 | 42: 0.0006 84: 0.0008 | 5, -5 | 3 | 5 | Yes!
11 | 42: 0.0006 84: 0.0008 | -5, 5 | 5 | 9 | Yes!
Figure: Start and end criterion for episodes 1-11. P42 and P84 losses shown separately.
Reached criterions after (_) steps, but forced to continue until 5 steps. Then, did not reach criterion within 10 steps. Splitting looked good.

## Slide 40: Extra: Conclusion: Quad splitting agents
Good performance so far
  Investigate criterion value for optimal splitting
  Test consistency across beams/intensities
Averaging ~5.27 steps per optimisation (of both phases, depending on initial conditions).
Future work
  Test using feature extractor
  Benchmark against mathematical optimisation
    Setup constructed simple enough for easy implementation in GeOFF.
    Is RL overkill in this case?
  Offline RL?
  Collection of labeled data
  Hyperparameter tuning of RL agents.
Init {15,-15}. Optimised in 2(!!) steps.

## Slide 41
Feature extractor performance on real trisplit data
Problem: CNN fails to generalise and is not accurate on real data.
  Error is however most often only ~3 degrees, which means it can improve on large phase errors.
  However, finetuning of phase becomes difficult. The agent is pre-trained with an almost perfect CNN, and trusts it too much.
Compare with simulation accuracy <1 degree.

## Slide 42: Extra: Feature extractors, gathering data
No dataset of real labeled acquisitions with available
→ One had to be simulated. Cern developed code BLonD was used.
When creating this simulated data, much care was taken to resemble live acquisitions to reduce the sim/real domain gap:
Adapting the resolution (ns/pt), number of traces, and timings to match those of the normal Tomoscope references for the quadsplit/trisplit.
Updated voltage programs of simulation by acquiring the latest ones from the LSA settings (quadsplit) or acquiring a reference of the design voltage (trisplit).
Added several data augmentation steps during training to:
  Normalise the data: the absolute values of the simulation and the detectors don’t line up, so the data is normalised before being used as input.
  Add noise to the data. This is done by approximating the noise of the machine by adding some Gaussian noise to the simulated data.
  Moving the initial injection center of the bunch +- a few ns. This is done as sometimes the beam jitters slightly compared to the tomoscope position, and we want the feature extractor to be agnostic to this.

## Slide 43: Extra: Feature extractors, the datasets
The Quad dataset:
  Scan of absolute phase errors in range
𝜙h=42, 𝜙h=84 = [-30,30].
  A total of 14641 samples in dataset.
The Tri dataset:
  Scan of absolute phase errors in range
𝜙h=14, 𝜙h=21, = [-20,20], and voltage factors for h=14 in range vh=14 = [0.95, 1.05].
  A total of 59541 samples in dataset.
Each sample stores the entire datamatrix of traces along with the label of the offset used to simulate it.
A 9:1 training/validation split was used.
Note: These same datasets are used for training of RL agents later, but then only extracted features such as end bunch-by-bunch length/intensities are given to the agents.
Datamatrix (150x200)
Label = [0, 0]
Train
Val
Datamatrix (150x400)
Label = [0, 0, 1.0]