## Slide 1
Machine Learning for Improved SRF
Operation at CEBAF
Chris Tennant | Jefferson Lab

## Slide 2: Outline
Introduction and Motivation
C100 Cavity Fault Classification
C100 Cavity Fault Prediction
Other
  Field Emission Management
  Legacy Cavity Instability Detection
Data Sources
Summary

## Slide 3: Acknowledgements
A. Carpenter, R. Suleiman, D. Turner, L. Vidyaratne*
Jefferson Laboratory
K. Ahammed, H. Ferguson, Md. M. Rahman, K. Iftekharuddin, J. Li
Old Dominion University
*now at Hitachi USA

## Slide 4: Continuous Electron Beam Accelerator Facility
CEBAF is a CW recirculating linac utilizing 418 SRF cavities to accelerate electrons up to 12 GeV through 5-passes
it is a nuclear physics user-facility capable of servicing 4 experimental halls simultaneously
the heart of the machine is the SRF cavities

## Slide 5
we have the ability to record high-fidelity data from 12 cryomodules
5
5
1
Question #1
Which of the 8 cavities faulted first?
Question #2
What kind of trip was it?
17 signals/cavity × 8 cavities = 136 signals
17 signals
1 cryomodule = collection of 8 cavities
Fault Classification: Defining the Problem
train a model to correctly classify the cavity and type of RF fault given waveform data

## Slide 6: Motivation for Machine Learning
laborious for subject matter expert to hand label thousands of events
Post-Run Analysis
use aggregate statistics for data-driven guidance for maintenance and/or upgrade activities
  analysis of fall 2018 data indicated three cryomodules in the South Linac were prone to microphonic-based faults  provided justification to perform microphonics hardening (installing tuner dampers)  reduced microphonics-based trip rates  gradients could be increased in those cryomodules
Post-Fault Analysis
provides critical feedback to control room operators
fault types get mapped to actions for the operators
  “if Trip A happens X times within Y minutes, drop gradient in the cavity by Z MV/m”

## Slide 7: Data: Waveform Harvester
…
…
fault event
streaming data
8,192 samples × 0.2 ms/sample = 1.64 seconds
waveform harvester was developed to capture RF time-series signals after a fault and write them to file for later analysis
  each of the 17 harvested waveform signals is 8,192 points long
  trigger set such that 94% of the recorded data precedes the fault and 6% after
  pre-fault data provides valuable information about the root cause of the trip

## Slide 8: ML Model Performance
models were applied to data collected from March 10-24, 2020
  physics run was prematurely ended due to COVID-19
312 fault events were analyzed by the models
summary of model performances compared to labeled data
cavity model accuracy: 84.9%
  testing accuracy: 87.9%
fault model accuracy: 78.2%
  testing accuracy: 87.7%
 | Agree | Disagree | Total
Cavity Model | 265 | 47 | 312
Fault Model | 244 | 68 | 312

## Slide 9: Visualization and Communication
for ML models to be effective, information must be communicated clearly and concisely
visualize spatial and temporal nature of model predictions
operator’s attention

## Slide 10: Machine Learning  Deep Learning
benefits
  avoid feature extraction
  computationally faster (needful for fault prediction)
  allow for uncertainty quantification
architectures explored
  recurrent NN
  CNN
  LSTM + CNN
incorrect
correct

## Slide 11: Dimensionality Reduction: Visualize Runs
cryomodule 1L22
cryomodule 1L25
cryomodule 1L24
cryomodule 1L26

## Slide 12: Maintaining Model Performance
most critical challenge is to maintain model performance from one operational run to the next (work in progress)
Feature Extraction
  Remove the output layer and use the entire network as a fixed feature extractor for the new dataset
Fine-Tune a Pre-Trained Model
  Fine-tune the weights of the pre-trained network (all layers)
Train Some Layers While Freezing Others
  Freeze weights of earlier layers and fine-tune the weights of later layers
train the model from scratch
fine-tune the pre-trained model
fine-tune lower layers of the pre-trained model
fine-tune the output dense layer of the pre-trained model
size of dataset
data similarity
https://tinyurl.com/yck4kzuk

## Slide 13: Fault Classification  Fault Prediction
small portion of waveforms around fault event are used for training classifiers
  uses static datasets
modifications to LLRF system will allow us to continuously stream data
investigate if data prior to fault contains enough information to predict event
C100 cryomodule
LLRF
storage
partial
Model A
prediction
discard
offline training
Model B
Model A: fault prediction (discriminate between “stable” and “impending”)
Model B: fault-type prediction (classify fault)

## Slide 14
Model A: Binary Classifier
slow vs fast fault types
“real” vs “quasi”-normal
fault signal window
dataset date

## Slide 15: Model A: Binary Classifier
normal
Normal
Faulty
-5 ms
faulty
100 ms
Normal
Faulty
-1435 ms
quasi-normal
-5 ms
faulty
100 ms

## Slide 16: Model B: Fault Classifier
can data prior to event accurately predict the fault type?
  use saved waveforms
t = -1400 ms
t = -1200 ms
t = -800 ms
t = -1000 ms
t = -400 ms
t = -600 ms
t = -200 ms

## Slide 17: Model B: Fault Classifier
0 ms prior to fault

## Slide 18: Model B: Fault Classifier
20 ms prior to fault

## Slide 19: Model B: Fault Classifier
50 ms prior to fault

## Slide 20: Model B: Fault Classifier
100 ms prior to fault

## Slide 21: Model B: Fault Classifier
initial results suggests that for some fault types, prediction is possible
Microphonics
Electronic Quench

## Slide 22: Field Emission Management
Goal: maintain low levels of FE radiation without invasive interruptions to physics
Description: use ML to model radiation levels and allow for off-line optimization of gradient distribution, identify cavities where FE onsets have changed
Solution: optimize surrogate model to minimize radiation via gradient reduction
damaged beamline valve
radiation area
damaged magnet and cables

## Slide 23: Field Emission Management: Proof-of-Concept Demonstration
set CEBAF to same gradient distribution as September 7 baseline
apply model-based optimized gradients to CEBAF
12 rem/hour decrease for 5 MV/m reduction in gradient
before optimization
after optimization
(courtesy A. Carpenter)

## Slide 24: Cavity Instability Detection
Goal: improve beam availability by automating process of identifying unstable RF cavities
Description: SRF cavities can become unstable without presenting faults, identifying these unstable cavities with present diagnostics is difficult and time-consuming
Solution: (1) develop and install a new fast DAQ system for the legacy SRF cavities, and (2) apply ML to identify unstable cavities
RF Analyzer Tool

## Slide 25: Importance of Having the Right Data
accelerators produce a lot of data
  CEBAF continuously archives 300,000+ signals
however, it’s not all useful for ML applications
ML projects at JLab only possible because of newly available data
C100 cavity fault classification  digital LLRF + waveform harvester
C100 cavity fault prediction  digital LLRF + streaming data
field emission management  NDX detectors*
cavity instability detection  fast DAQ
data reliability is critical!
*P. Degtiarenko, US Patent 10,281,600

## Slide 26: Summary
JLab has several active ML projects addressing SRF operation at CEBAF, which are at various stages of maturity
have – or will have – sources of high quality data to enable continued work in this area for the foreseeable future
  for systems in place: maintaining reliability of data is a challenge
  for systems in production: challenges with supply chain issues
getting buy-in from all groups involved is still a challenge
cavity instability detection
encouraging results on “slow” data
field emission management
how to update model?
fault prediction
encouraging initial results on saved waveforms
fault classification
how to maintain performance over time?
proof-of-concept
deployed system
maintained system

## Slide 27
Thank You.
tennant@jlab.org

## Slide 28: Mobile Diagnostic for Accelerator Operations
Goal: develop a remotely controlled, semi-autonomous, mobile diagnostic that can be integrated into accelerator operations
the mobile diagnostic system would provide potential benefit by:
  reducing accelerator downtime by enabling remote inspection of beamline components and reducing the need for short, controlled accesses to the accelerator tunnel, and reducing the time required to perform standard radiation surveys
  reducing machine tuning-time by acquiring dynamic measurements, e.g. beam loss and radiation measurements, under operational conditions at arbitrary locations along the beamline