## Slide 1: Data-Driven Chaos Indicators for Beam Dynamics
Nov. 1-4, 2022
3rd ICFA Beam Dynamics Mini-Workshop on Machine Learning Applications for Particle Accelerators
Robert Rainer
NSLS-II, BNL

## Slide 2: Contributors
Yongjun Li – Brookhaven National Lab, Upton, NY
Jinyu Wan – Inst. High Energy Physics, Beijing
Allen Liu – Purdue University, W Lafayette, IN
Yi Jiao – Uni. Chinese Academy of Sciences, Beijing
Rob Rainer – Brookhaven National Lab, Upton, NY

## Slide 3: Outline
Predictability vs. chaos
Proof-of-principle with Hénon map
Application on accelerator design
Summary
*Brief* Q & A

## Slide 4: Chaos vs. Predictability
Less chaotic, prediction is accurate (interpolate/extrapolate)
Prediction performance appears to be directly related to level of chaos
Is it possible to use the predictability as a chaos indicator?
Less chaotic
Prediction is accurate
More chaotic
Prediction is inaccurate

## Slide 5: Proof-of-Principle with Hénon Map
Blackbox
Hénon map
Xin
Xout
At resonances, motion is chaotic and even unstable

## Slide 6: Cheap vs. Expensive Computations
Cheap: fewer initial conditions, short time
Expensive: more initial conditions, long time
-0.6 < X,P < 0.6, 20 iterations
-1.2 < X,P < 1.2, 2048 iterations
Red box is area of interest
Blue points are stable, survived
Xin
Xout

## Slide 7: Surrogate Model’s Performance
Training data constructs surrogate model: polynomial, NN, SVM, etc.
Testing data checks the prediction performance
X
P
Original test data
Model prediction

## Slide 8: Tune Scan for Hénon Map
We see:
Nonlinear resonances
Stopband widths
Consistent with (expensive) tracking
Blue line: data-driven chaos indicator
Red line: long-term tracking
Black dashed lines: stopband width

## Slide 9: Applied to Particle Accelerator Design
NSLS-II ring lattice

## Slide 10: ANN for Surrogate Model
4-Later Artificial Neural Network
I/O: 4-D phase space coordinates
SCIKIT-LEARN & KERAS Packages
6 “Families” of Harmonic Sextupoles
Symplectic Particle Tracking: ELEGANT
4 X 12 X 12 X 4
Tuning “Knobs”

## Slide 11: DDCI for the NSLS-II Accelerator
Not well-optimized nonlinear lattice
Well-optimized nonlinear lattice

## Slide 12: DDCI as Optimization Objective
Tuning nonlinear magnets in an accelerator
Compute DDCI for each configuration
Using multi-objective genetic algorithm to minimize DDCI

## Slide 13: Testing with Real Beam at NSLS-II
Dynamic aperture
Momentum acceptance

## Slide 14: Summary
DDCI is independent of model type (polynomial, NN, SVR, etc.)
Computation cost of DDCI is low
Used as the objective of population-based optimization
A new perspective of nonlinear dynamics is provided
Publication: https://doi.org/10.1016/j.nima.2021.166060

## Slide 15: Acknowledgements
Funded by DoE under Contract No. DE-SC0012704
NSLS-II colleagues and external collaborators
ML workshop Committee
Questions and comments are welcome