## Slide 1: DUNE CE ASIC R&D & QA
Carl Bromberg, Kendall Mahn, Dean Shooltz
Michigan State University

## Slide 2
“Foam insulated kitchen sink”
...quote from FNAL safety review
LN2 Dewar
Load/Unload
Lid removed
Fan off
Heat off
no LN2
Purge and Dry
Fan on
Heat on
no LN2
Supply N2 gas
Cooldown
Fan on
Heat off
1 cm LN2
Immerse
Fan off
Heat off
10 cm LN2
Warmup
Fan on
Heat on
no LN2
Supply N2 gas
Cryo Testing Station
– Cycle time is roughly one hour (plus electronics testing time)
– Fans and heaters are located inside test chamber
– Slight pressure in Dewar used to raise LN2 into test chamber
– Relieve pressure and LN drains back into Dewar
– CTS cycle keeps DUT dry throughout the cycle
CTS
Cycle
Heater
4 ASICs or 1 FEMB

## Slide 3
Robotic ASIC Handling
– SCARA 4-axis robot
– End-Of-Arm-Tooling designed to load/unload LQFP-128 and LQFP-208 ASIC test sockets
Includes a camera system
– Positioning refinement
– ASIC optical inspection
– Bent pin detection

## Slide 4
Scaling up to a full-size dual-chamber RTS
The membrane-style test chamber
is easy to scale up to fit the 26”
by 13” BNL DAT board.
Two chambers just fit within the
operating envelope of a SCARA
robot with 550 mm reach.
The system needs to be mounted
to a stiff working table.
Current table design is welded from
3” square steel box beams with a
steel top plate. This follows common
designs found in industry.
The table is designed to be movable
with a standard pallet jack.
We will also explore options based on
aluminum strut systems (“80/20” or
Similar).

## Slide 5
Straw-Man design for DUNE CE testing boards
– Topology follows FEMB design (18 ASICs)
– All 18 ASICs (8 LArASIC, 8 ColdADC, 2 ColdData) are located on one side of the PCB
– PCB is spread out enough to allow ASIC mezzanines (soldered or socketed) at each position
– Spacing derived from previous BNL testing hardware (quad-socket LArASIC tester)
– BNL (Shanshan) seems to think that this is a reasonable starting point for designing new CTS
The “DAT”

## Slide 6
Modular Design for RTS cryo system
A standard LN2 Dewar has become an integral part of the RTS cryogenic design.
– Common in many Physics labs
– Can be filled locally from on-site supply
– Also available from commercial vendors (delivered full)
– At MSU we can get 250 liters delivered for $100, with no rental fee
(which is half the price of using our own on-site LN2 supply)
– These Dewars are self-pressurizing, simplifying RTS (-vs- CTS)
– Eliminates need for placing heaters in the Storage Dewar
– Use this “Vendor Dewar” (VD) to:
(1) Refill SD before each RTS cycle (auto-refill while we change ASICs)
(2) Supply N2 gas under pressure to operate the CTS cycle
– Swap to a full “Vendor Dewar” as necessary (once per week?)
VD = Vendor Dewar
LN2 Dewar 160-250 liters

## Slide 7
Modular Design for RTS cryo system
Inputs
LS1, LS2, PT1, PT2, User
Outputs
Valves V3, V4, V5, V6, V7
Logic (PLC)
State Machine
Control system is simply a state machine with 6 states

## Slide 8
DUNE CE Robotic Testing Station (RTS) Status
– Robotics in hand and ASIC loading tested
– Preliminary review at FNAL of Cryogenic system design saw no show-stoppers
– Cryogenic valving & piping components in hand and being assembled
– Pan and supports for DAT board have been prototyped and LN2 tested
– DAT board layout at BNL being reviewed to be followed by fabrication
Socket test is the current focus at MSU
– Mockup board with multiple sockets prepared
– Loaded with 16 dummy chips (128 pins) with internal pair-connection – then daisy-chained
– Run robotic load/unload with full cryogenic cycle to determine socket mean-time to failure.
– Sockets on DAT board are replaceable (socketed) – but with robotic handling this may be rare