## Slide 1: 60% Design/Engineering for EIC Detector Solenoid Magnet Valerio CALVELLI (CEA/IRFU) On Behalf of EIC Detector Magnet team
2D / 3D MARCO Preliminary Magnetic Design
Mid-Project Review
2022-06-28

## Slide 2: Outline
MARCO Design Strategy
Upper limits on the Interaction Length
MARCO Dimensions
MARCO Magnetic Design

## Slide 3
MARCO Specifications
Specifications related to the magnetic design
Discussed in R. Rajput-Ghoshal talk

## Slide 4
Strategy followed to achieve the specifications
Strategy
Fix the overall dimensions as BaBar's ones
Fix the coils axial length / inner radius as BaBar
Respect the same interaction length
Conductor with Al stabilizer is not an option today due to the lack of manufacturers.
Choose to design a conductor with Cu stabilizer
Reduce the overall coil + mechanical structure thickness to respect 3
Increase the current density
Propose a simplified design (cost effective) and check if it satisfies the requirements
BaBar Solenoid

## Slide 5
BaBaR Dimensions / Marco Dimensions
We adopted these dimensions for MARCO as reference
BaBar Dimensions
Dimensions / n° of turns as-built differ from the ones reported into papers
Dimension | Value | Units
Rin coil | 1509.5 | mm
Coil Axial length | 3492 | mm

## Slide 6
Interaction length limits
Mean range
(Bethe equation)
Stabilizer material for conductor
Copper
Aluminium
3x less stopping power with the same coils dimensions and NbTi fraction in the cable
TRANSPARENCY for the transverse momentum
THUMB RULE
Overall coil thickness have to be around 1/3 of BaBar’s coil
23.88 mm Cu+40 mm SS in New
136.72 mm Al in BaBar
0.42 interaction length in New
0.36 interaction length in BaBar
1.26 interaction length in SOCRATE
First calculations
By R. Rajput-Ghoshal

## Slide 7
Marco Dimensions (v.4.3.1.0.0)
Dimension | Value | Units
Rin magnet | 1420 | mm
Rout magnet | Tbd | mm
Rin coil | 1509.5 | mm
Rout coil | 1531.9 | mm
Rin mechanical structure |  | mm
Rout mechanical structure | 1535 | mm
Rout magnet | Tbd | mm
Coil Axial length | 3492 | mm
Magnet Axial length | 3850 | mm
22.4
22.5
R =1509.5
Z = 3492
R =1557.4
Dimensions are in mm
They may slightly vary according to the design progress
R =1420
Coil + mechanical structure thickness = 48 mm vs 110 mm (+30mm inner structure for BaBar)

## Slide 8
Marco Magnetic Design
1 layer solenoid
4 layers solenoid
R
Z
R
Z

## Slide 9
Marco Magnetic Design
1 layer solenoid
4 layers solenoid
Same magnetic results
In terms of energy/peak field
4 layers solenoid reference solution
(See F.Stacchi talk)

## Slide 10
3D Magnetic Preliminary Design Results
Parameter | Parameter Value | Units | Validation
Coil Rin | 1509.5 | mm | OK
Coil Rout | 1532.0 | mm | OK
Coil Length | 3492.0 | mm | OK
3D RESULTS |  |  | 
B @ (0,0,0) | 1.502 | T | OK
Bpeak+self field | 2.226 | T | 
Stored Energy | 25.076 | MJ | 
B @ (0,0,-5300) | 29 | G | Tbd
B @ (0,0,7200) | 18 | G | Tbd
B @ (3400,0,0) | 17 | G | Tbd
Projectivity | 1.63 | T/Amm² | OK
Homogeneity | 12.342 | % | Validated by physics group
3D Results are the same as 2D
Chart: Z (mm)
Homogeneity region
RICH Projectivity
B field along Z axis
1.38 T
1.56 T

## Slide 11
Yoke effect on the fringe field
Chart: Barrel Yoke increased thickness (mm)
| 0 | 50 | 100 | 150 | 200
B3400 | 1.68 | 1.56 | 1.46 | 1.37 | 1.29
B5300 | 2.9 | 2.71 | 2.55 | 2.4 | 2.26
B7200 | 1.86 | 1.73 | 1.61 | 1.5 | 1.4
Increased thickness
Small effect
Do not satisfy the requirement (0.5 mT)
Very expensive
Discussions needed with the accelerator group

## Slide 12
What’s Next
Discuss possible solutions about the fringe field
Validate the Magnetic Design
Detailed Yoke Geometry and materials
Forces on the magnet and on the Yoke at nominal operation and during ramp-up/down

## Slide 13
Summary
Today the magnetic design respects almost all the specifications:
B = 1.5 T @ IP
Homogeneity = 12.3% validated from the Physic Group
Projectivity = 1.63 T/Amm²
Coil dimensions within the specs
The fringe field is between 17 G / 29 G

## Slide 14: Back up Slides

## Slide 15
2D Magnetic Preliminary Design Results
Parameter | Parameter Value | Units | Validation
Coil Rin | 1509.5 | mm | OK
Coil Rout | 1532.0 | mm | OK
Coil Length | 3492.0 | mm | OK
2D RESULTS |  |  | 
B @ (0,0,0) | 1.500 | T | OK
Bpeak+self field 4.3.1.0.0 | 2.226 | T | 
Stored Energy | 24.952 | MJ | 
B @ (0,0,-5300) | 2.88 | mT | To be discussed
B @ (0,0,7200) | 1.84 | mT | 
B @ (3400,0,0) | 1.66 | mT | 
Projectivity | 1.63 | T/Amm² | OK
Homogeneity | 12.342 | % | Validated by physics group