## Slide 1
Ahead of DAQ/Electronics review:
What are the General DAQ/Side Requirements for FEEs / ASICS
DAQ side requirement for FEE:
  Must do zero suppression sufficient to reduce data readout per fiber output to (Quote number! Current FELIX ~6.5Gb/sec or Future FELIX/Current COTS ~40Gb/sec)?
  Must use DAQ defined header of (Quote number! 64bits?) including (partial) time frame, user bits etc arising from timing system.
  Must provide/transmit i2c configuration commands to configure FEE / any ASICS or other contained chips
  Must Support DAQ defined flow control commands
  Time frames? (Do we need FEE’s to supports specified frames, or do we let FEE’s define frames and have DAQ adapt?)
  Do the FEEs have to have their operation clock tied to the collider in any way?
    Obviously, there would be a clock signal tied to the phase and frequency of the BX
    Signal times will have to be tagged using these BX values
    The FEEs need to assign time windows based on the BX signal
    Is there any actual need or even advantage for this signal to be equivalent to the FEE clock?
Other requirements?
DAQ side requirement from ASICS / Front End readouts:
  Chips either require
    No trigger
    Can support a trigger on a clock signal that can repeat on a deterministic readout duration (with no deadtime subject to detector specific occupancy limits)

## Slide 2
Discussion of Streaming Model Alternatives:
What do we mean by streaming? “Final” Decisions are not needed for many years…
Haven’t really discussed this yet, but we do need to work at least to some generic consensus about the scheme
  We need a common stance in order to have successful discussions with Software Groups & Simulation Groups
  We need a shared idea of DAQ Features
    Online QA capable of multi-detector correlation
    Feedback to collaboration / collider regarding beam quality and suitability for our physics
    “Scalers”
    What kind of monitoring do we need
    What general components/support do we need in DAQ and at what level
      Data features created and written out (clusters, track segments, tracks, identified particles?)
      Data filtered after the FEEs (non-track hits? Tracks only? …)
      Software triggering
      ML/AI integration into the data files
      Structure for defining available information at different stages (when can we correlate detector info)
    How do we incorporate Slow Controls/Collider information with the DAQ data?

## Slide 3
Goals:
Capability
  Efficiently remove noise if/when needed
  Determine performance of detectors and of collider in real time
  Framework for extensions
    Support AI/ML use & development
    Support workarounds for inevitable issues (Say disable readout on signal from collider)
  Tracking of data files and running conditions
Simplicity
  DAQ system
  Application of DAQ supplied data additions (Scalers, data feature readout, clusters, tracks, Pt, output from AI/ML)
  Application of DAQ supplied data filtering (Software Trigger, Tracking based filtering, AI/ML filters)
  Software reconstruction
  Online QA
  Calibration
Efficiency
  DAQ system
  Application of DAQ supplied data additions (Scalers, data feature readout, clusters, tracks, Pt, output from AI/ML)
  Application of DAQ supplied data filtering (Software Trigger, Tracking based filtering, AI/ML filters)
  Software reconstruction
  Online QA
  Calibration

## Slide 4
Notes on Assumed Limitations
The more data files required to process a single “time” offline the worse
  HPSS makes correlation of many required files a disaster
  Current software scheme of “No Tape” reconstruction may mitigate this. However, if we did ever need to go “back to the tape” we would regret having large numbers of data files per “time”
FEEs & to an even larger extent DAMS will likely assemble time frames with many chucks of time ordered data.
  Moving to BX level time ordering would require unraveling this in DAQ.
  Staying at Frame level time ordering would require unraveling this in reconstruction
  Many “complexity” arguments will have the same tradeoff, so the criteria should be overall complexity if that can be determined.

## Slide 5
Hierarchy of Decisions Needed
Geographical structure of the data files
  How many data files do you need to process to obtain all of the information from a single BX?
  How are data files linked together
Time Granularity of data files
  Standard Frames
  Detector by Detector Frames
  BX
Time Coherency of data files. Do files contain coherent time sequences or time sequences with gaps?
  File #1: tm0 tm50 tm100…
  File #2: tm1 tm51 tm101…
Do we have lookaside data files?
  File with a list of potential BX corresponding to events
  Separate file for detectors with multi-bunch crossing
  Scaler files?
  QA generated files?
What role for databases. Are they required for interpreting collision data?

## Slide 6
My Strawman:
Build events so that all detectors from a time frame are in a single file
  Advantages:
    Easy to correlate detectors for QA/reconstruction
    Efficient for reconstruction
    No real efficiency loss in DAQ (assume algorithmic load balancing)
    No data replication due to readout time window differences
  Disadvantages:
    Forces same time frame periods for all detectors
    Time frames per file will not be consecutive (we will need to generate multiple files at one time)
    Scalers, SC, or trigger information from one data file would be incomplete
    Still some untangling of data files to reach BX time levels
Use lookaside file(s) or primary DB for Scalers, SC and/or trigger hypothesis.
If time frames can’t be consistent among all detectors, consider a small number of files, one for each time frame definition.