## Slide 1: GridPIX (aka MiniTPC): Brief Introduction
TK Hemmick
Main discussion in PID group of ATHENA.
Selected as “upgrade path” for ATHENA.
Will be proposed to EIC Generic R&D Program*.
Provides:
  PID (pi-K-p) from 100 MeV/c to 800 MeV/c
  ROBUST tracking (enormous number of hits per track)
DD4HEP
Gas Volume
Readout
High Voltage (-10kV)
Low radiation Length
T2K gas (low diffusion)
Silicon Pixel Readout
4% radiation length
(dominated by cooling)
Field Cage
1% radiation length, entrance and exit
*Stony Brook, Yale, Bonn

## Slide 2: GridPIX Overview
Ultimate dE/dx device.
  Avalanche grid in front of 55 x 55 mm2 pixels.
  >90% efficiency for single electrons.
  Goals:
    Enough diffusion to get every electron into a different hole.
    Count electrons one-by-one.
  Three generations of development and continuing.
Large area VERY expensive, small area not so much.
  1800 chips (order/produce/test 3600) = $716k
  Careful: 1.2-5.4 kW of power (occupancy dependent).
Pros:
Known/Proven Technology
Active further development (Bonn)
Best possible (~count each electron)
Affordable for a small area
High resolution tracking
Low mass in electron arm
Continuous (aka streaming) readout
Cons:
3 kW of power:
Must find a low pass way to handle.
Services “bulky” (compared to just Si)
  Gas
  HV membrane
  Cooling
  DC power lines (3kV goes in too)
3D e-by-e tracking

## Slide 3
Overview:
Segmentation:
  70% active area  3150 “rows”
2400 primaries in 25 cm for a MIP.
  Thousands of hits per track.
Extremely robust patterns.
June 2021

## Slide 5
Delta Rays can be removed very often by Topology.

## Slide 6
Garfield & Cooling
These are not lines! They are dots!
Temperature Profiles: 3 kW
4% Radiation Length
Coolant above the dew point
Laura Gonella: I can do MUCH MUCH better than this!

## Slide 7
NOTE:
Initial implementation = “Layers of Gas Cylinders”
One hit per layer “under-values GridPIX”
Probably still very robust w.r.t. pattern finding.

## Slide 8: Anticipated dE/dx Resolution
Lehraus Plot
Using 5.4 as a standard TPC
  5.4*(0.25)-0.37 = 9.0
Measured for GridPIX (truncated Mean)
  4.1% at 1 meter
  4.1*(0.25)-0.37 = 6.85
    This was the prior assumption quoted by us.
Roughly 20 sigma at 0.5 GeV/c
Useful range overlaps with DIRC
9.0%
K-p
p-K
6.85%
K-p
p-K
Momentum
Momentum
#s
#s
easy
hard

## Slide 9: Overly Simplified Momentum Resolution
Figure of Merit:
Can be compared to Silicon with detailed Monte Carlo
Here is simple-minded estimate
  Gas:
    Including efficiency ~3000 electrons (minimum!) per track
    Each suffers digitization (s = 55 mm/sqrt(12) = 16 mm)
    Diffusion(Length) =
      D(2cm) = 35 mm  FOM = 0.70 mm
      D(25cm) = 125 mm  FOM = 2.3 mm
      D(50cm) = 176 mm  FOM = 3.2 mm
      D(100cm) = 250 mm  FOM = 4.6 mm
  Although ignoring many significant effects, initial result is on the order of the layers of silicon.

## Slide 10: Summary
GridPIX is silicon-base gas chamber readout.
Makes for the “ultimate” TPC:
  Ultimate in pattern recognition: electron-by-electron
  Ultimate in dE/dx resolution.

## Slide 13
June 2021