## Slide 1: Hardware opportunities for PO
E.C. Aschenauer (BNL)

## Slide 2: Scope Experimental Equipment
hadronic calorimeters
e/m calorimeters
ToF, DIRC,
RICH detectors
MAPS tracker
MPG trackers
Solenoidal Magnet
Moved from WBS 6.06,
incl. lepton, hadron polarimetry and luminosity monitor
25 Subdetectors
incl. Polarimeters
provides coordination that
2nd detector remains possible

## Slide 3: The Path to CD-2/3A
Form collaboration and define subsystem responsibilities
   in-kind contributions need to be identified and agreements need to be in an advanced state (close to final)
   Integrate collaboration in WBS – structure of detector
Finalize scope of EIC Project Detector
  all subsystem technologies defined by end of CY2022
Continuous refinement of subsystem requirements and interfaces
Refine cost, schedule and labor needs for each subsystem
  detailed documentation of basis – of – estimates
  Long Lead Procurement (LLP) items of the detector will be further refined
  define scope contingency items
Bring level of design on average to 50-60% @ CD2/3A, with LLP items needing to be at final design stage (~90%)
Produce pre-TDR*: 1st version of by May 2023
 final version by October 2023
Technologies need to be defined by end of CY22

## Slide 4: What can we do and what we must do
The must do for BNL not necessarily PO:
Hadron polarimetry
Integration in the IR for the all the ancillary detectors and the main detector – some shared with Jlab
  building pot-less roman pots will be a really new novel design in a high current beams, as the EIC hadron beams
  Silicon in the electron vacuum (low-Q2 tagger) will be a novelty as well
Infrastructure
Involvement in the DAQ

## Slide 5: What can we do and what we must do
The should do for PO / BNL
BNL is a national lab so we should do detector design and construction, which goes beyond what a university group can do.
PO is a large group, so maybe more than one subdetector involvement is possible
 PID -- pfRICH:
involves new photon sensors  LAPPDs
currently BNL is ahead on this R&D  we should build on this
can integrate 2 functions in one detector low (ToF) and high momentum PID
in collaboration with Japan (Chiba University), built on our transition from RHIC could
push R&D on Aerogel
Barrel tracking:
It might soon become clear that the tracking needs significantly more planes to deal
with beam backgrounds in the track finding
 Many years of R&D in MPGDs
 MAPS tracker:
First MAPS tracker in collider experiment was operated at RHIC
IO is involved in designing the chips
collaboration with IO could make BNL a real powerhouse for MAPS
PO could look into service reduction, cooling, integration, ……
new tracking methods could be developed  synergy with NPPS

## Slide 6: What can we do and what we must do
The should do for PO / BNL
Barrel ECal: if imaging ECal will be chosen complex calorimeter with interesting physics opportunities  collaboration with Argonne

## Slide 9: Experimental Equipment Technical Progress
Consolidation of ECCE and ATHENA in full swing, make integration of all groups as welcoming as possible
Combined Leadership Team formed
Combined Physics and Technical WG formed
rolling out R&D contracts
Updating P6 & integrate milestones
Contract with Saclay to continue design for a 1.5 T BaBAR like Solenoid as Risk mitigation
Eased design as can use Cu-stabilized conductor
Update risk assessment of BaBAR Solenoid
Defined and documented system requirements down to L4
develop a technical solution to bake-out beam pipe with m-vertex in-situ
develop beam pipe support to allow 1st m-vertex layer as close to the IP as possible
detail all the requirements for the next phase of the technical design
investigate a pressurized Argon based RICH can be realized
work on next phase of technical design on eEndcap ECal in collaboration with Orsay technical team
work on next phase of technical design of barrel SciGlass ECal
Define ASIC needs based on ECCE as reference detector
Next Streaming readout workshop to develop requirements based on community input
Document the existing infrastructure at 1006, i.e. water, electricity, grounding
Full 3d layout of extended IR region including all auxiliary detectors
Technical Subsystem Review April 27th
Move in parallel on 2nd IR layout and ensure all the experimental equipment can fit
ePol: Compton polarimeter is integrated in IR and layout and technical definition are further refined
HPol: new location at IP-4 integration underway

## Slide 10: MAPS mVertex
For primary and secondary vertex reconstruction
Low material budget: 0.05% X/X0 per layer
High spatial resolution: 10 mm pitch MAPS
 ref. Alice ITS3
Compromise:
  20 mm (or smaller) pixels and ~0.3% X/X0 per layer
Configuration: Barrel+ Disks for endcaps

## Slide 11: Micro Pattern Gas Detectors
To improve momentum resolution at large rapidities.
Spatial resolution well below 100 mm
Large-area detectors possible
Cost efficient compared to silicon
EIC R&D: large 2D GEM module
~900mm
MPGDs

## Slide 12: Areas of Possible Synergy: Detector
Tracking:
Silicon – MAPS
  already ongoing R&D collaboration with CERN/ALICE ITS
  development
    low mass EIC ITS-3 based forward disks
    new development
  existing ALPIDE alternative
  EIC European Groups from UK and Italy
AC-LGAD
  EIC triggered the formation of consortium between HEP and NP groups
    Goal: push technology and readout development for many applications (tracking, ToF, …)
  EIC European Groups from France
MPGDs – GEMs
  GEM foils typically come from CERN for QA
  clear synergy with CERN RD-51 and
  ALICE new TPC GEM readout and COMPASS
  EIC European Groups from Italy
EIC R&D: large 2D GEM module
~900mm

## Slide 13: Particle ID
In general, need to separate:
Electrons from photons  4p coverage in tracking
Electrons from charged hadrons  mostly provided by calorimetry
Charged pions, kaons and protons from each other  Cherenkov detectors
  Cherenkov detectors, complemented by other technologies at lower momenta
Challenges:
photon sensors in high magnetic field  SiPMs impact on streaming DAQ
high performance aerogel radiator
P [GeV]
Pythia MC
Physics requirements:
Illustration of PID detectors achievements:
Need more than one technology to cover the entire momentum ranges at different rapidities
Rapidity | π/K/p and π0/γ | e/h | Min pT (E)
-3.5 − -1.0 | 7 GeV/c | 18 GeV/c | 100 MeV/c
-1.0 − 1.0 | 8-10 GeV/c | 8 GeV/c | 100 MeV/c
1.0 − 3.5 | 50 GeV/c | 20 GeV/c | 100 MeV/c

## Slide 14: Far forward (hadron going) region
IP
p/A
Detector | Angular accept. [mrad] | PT coverage
ZDC @ ~30m | <5.5 ( | pT<1.3 GeV
Roman Pots | 0*<<5.0 ( | *Low pT(t) cutoff (beam optics)
Off-Momentum Detectors | 0.< < 5.0 ( | Low-rigidity particles from nuclear breakups
B0 forward spectrometer | (4.6< | High pT(t)
Detector | Angular accept. [mrad] | PT coverage
ZDC @ ~30m |  | pT<1.3 GeV
Roman Pots |  | *Low pT(t) cutoff (beam optics)
Off-Momentum Detectors |  | Low-rigidity particles from nuclear breakups
B0 forward spectrometer |  | High pT(t)