## Slide 1
Tracking Detector Specific Requirements | Spec | DAM Boards
Tracking | 7 m^2 MAPS ITS-2 & ITS-3 sensors | 
3 layers silicon for vertex | ITS-3 curved silicon | 
2 layers silicon for sagitta | ITS-2 type staves but ITS-3 improvements | 
4 layers silicon disks backward |  | 
5 layers silicon disks forward |  | 
3 layers of MPGD |  | 
MAPS | 5GB/sec total throughput | 
 | 32B pixels | 
 | 5.2k MAPS sensors | 
 | ~300 data fibers | 6
MPGD |  | 
 | 100k channels | 
 | <10Gb/sec total zero-suppressed data volume | 
 | Assume 512 channels per FEE (with 8 ASICs) | 
 | 200 FEEs / data fibers | 4
 | 10Gb/sec -> .05Gb/sec per fiber | 
 | Iraqli estimate -> 1.9Gb/sec per fiber | 
Use Reconstructed clocks to avoid fiber proliferation |  | 

## Slide 2
Calorimeters Specific Requirements | Spec | DAM Boards
Forward ECAL (PbWO (+SiGlass)) | 3000 channels | 
Backward ECAL | 3000 channels | 
Barrel ECAL | 8000 channels | 
Imaging Barrel ECAL (If used) | 10,000 Pb/SciFi | 
 | 50M channels Astropix “2 level data aggregation inside detector, 1 data link per stave Count of Staves? | 
Barrel HCAL (ECCE version) | 3,000 channels | 
(Athena version) | 26,600 channels (off detector electronics) | 
Forward pECAL (Athena Version) | 25,000 channels (off detector electronics) | 
Forward FHCAL (Ecce Style) | 60,000 channels | 
High granularity HCAL inset | 8k channel | 
Except for the Imaging barrel all SiPM | ~110k channels | 
 | Assume 64 channels / FEE -> 1600 fibers | 34
Backward HCAL uncertain. |  | 
Use Reconstructed Clock to reduce fiber |  | 

## Slide 3
Far Forward Specific Requirements | Spec | DAM Boards
B0 |  | 
3 MAPS layers | 300M Pixel (3x20x20cm @ 20x20 um pitch. ~300 sensor) | 
1 AC-LGAD | 150k (500x500um pitch assumed) | 
Photon Tagger | (1) 50 -70 PbWO4 crystals; or (2) 300k channels AC-LGADs | 
2 RP and 2 OffM |  | 
4 x 500k AC-LGAD layers (2 each) | 4M total channels | 
ZDC |  | 
Crystal | 400 channels APD | 
32 x 2600 ch silicon pad | 11,520 HGCROC as per ALICE FoCal-E pad layers | 
4 x 40,000ch silicon pixel | 160k | 
2 boxes scintillator | 72 | 
Far Backward Specific Requirements | Spec | DAM Boards
Low-Q tagger 1: 2 layers of (40x40cm) (500umx500um pitch) | 1.3M | 
Low-Q Tagger 2: 2 layers of (30cmx20cm) (500umx500um pitch) | 480k | 
(or smaller…) |  | 
2 Calorimeters | 700 Channels total | 

## Slide 4
Cherenkov PID Specific Requirements | Spec | DAM Boards
dRICH | 300k channels | 
 | Max dark current rate 1830 Gb/sec | 
 | 40Gb/sec fiber | 
 | Dedicated Timing fiber for timing window application | 
 | ~310 fiber (assuming 64 channel FEB + 16 FEB x ROB) and 6.5Gb/sec fiber | ~24
pfRICH (if used) (assume 75% of dRICH) | 225k | 
mRICH | ? | 
DIRC | 100k channels | 
TOF Specific Requirements | Spec | DAM Boards
Channels |  | 
Depends on strip size (.5mm x 1cm or .5mm x .3cm) and/or pixel size (.5mm x .5mm) | 3-50M channels | 
fibers | 240 - 500 | 5 – 10
Rate per fiber | .5Gb/sec – 5 Gb/sec | 
Rates to tap | 4-6 Gb/sec | 
Dedicated fiber for high resolution clock |  | 

## Slide 5
Detector System | Channels | Fibers | DAM Boards |  | Notes
Tracking |  |  |  |  | 
MAPS | 5,200 | 270 | 6 |  | 32B pixels, 5.2k MAPS sensors
MPGD | 100,000 | 200 | 4 |  | Assume 512 ch / FEE (w/ 8 ASICs)
Calorimeters |  |  |  |  | 
Forward ECAL (PbWO (+SiGlass)) | 3,000 | 47 | 1 |  | 
Backward ECAL | 3,000 | 47 | 1 |  | 
Barrel ECAL | 8,000 | 125 | 3 |  | 
Imaging Barrel ECAL (if used) | 50,000,000 |  |  |  | data aggregation; 1 data link per stave; count of staves?
Barrel HCAL (ECCE version) | 3,000 | 47 | 1 |  | 
Forward pECAL (Athena version) | 25,000 | 391 | 9 |  | off detector electronics
Forward FHCAL (Ecce Style) | 60,000 | 938 | 20 |  | 
High Granularity HCAL inset | 8,000 | 125 | 3 |  | 
Far Forward |  |  |  |  | 
B0 |  |  |  |  | 
3 MAPS layers | 300 |  | 26 |  | 300M Pixels (3x20x20cm @ 20x20 um pitch. ~300 sensors)
1 AC-LGAD | 150,000 |  | 3 |  | (500x500um pitch assumed)
2 RP and 2 OffM |  |  |  |  | 
4 x 500k AC-LGAD Layers (2 each) | 4,000,000 |  |  |  | 
ZDC |  |  |  |  | 
Crystal | 400 |  |  |  | APD
32 x 2600 ch silicon pad | 11,520 |  |  |  | HGCROC as per ALICE FoCal-E layers
4 x 40,000ch silicon pixel | 160,000 |  |  |  | 
2 boxes scintillator | 72 |  |  |  | 
Far Backward |  |  |  |  | 
Low-Q tagger 1: 2 layers of 40x40cm (500x500um pitch) | 1,300,000 |  |  |  | 
Low-Q tagger 2: 2 layers of 30x20cm (500x500um pitch) | 400,000 |  |  |  | 
2 Calorimeters | 700 |  |  |  | 
Cherenkov PID |  |  |  |  | 
dRICH | 300,000 | 310 | 24 |  | assuming 64 ch FEB + 16 FEB x ROB and 6.5Gbps fiber
pfRICH | 225,000 |  |  |  | assume 75% of dRICH
mRICH |  | 288 | 7 |  | assume info from ECCE table
DIRC | 100,000 |  |  |  | 
TOF |  |  |  |  | 
AC-LGAD | 50,000,000 |  |  |  | depends on strip size and/or pixel size
Barrel |  | 160 | 4 |  | 
e Endcap |  | 30 | 1 |  | 
h Endcap |  | 50 | 2 |  | 
Total | 1,013,192 | 2,788 | 108 |  |