## Slide 1
Discussion of Streaming Model Alternatives:
Architecture from the DAM board through the Storage facility
  This will all be implemented in COTS computing connected via ethernet (I’m expecting 100Gb/sec as minimum speed)
  Both protocollab’s underestimated. The project has significantly higher estimate for computing
  The project has ~$1.6M allocated for COTS computers + ~$150k for networking. The types / numbers of machines were a lot different, Must be defined better as the specific architecture is developed!
  Although streaming model isn’t highest priority because software development is later in schedule & because details are easier to change than for hardware, we do need to work at least to some generic consensus about the scheme
Project (EPIC) | ECCE | Athena
108 Type 3 (DAM Interface $8k) | 115 DAM Interface ($5.7k) | 48 DAM Interface ($4k)
6 File Servers ($53k) | 6 File Servers ($53k) | 22 SDCC Interface ($7k)
44 Type 2 ($3k) | 26 Online Event Servers ($2.7k) | 38 Analysis Nodes ($9k)
48 Type 1 ($8k) |  | 
$1.6M | $1.1M | $700k

## Slide 2
We need to iterate on the details of the hardware purchase plan. They won’t be made for many years, but we want the project’s schedule/plan to reflect the actual situation as best we can!
We need a common stance in order to have successful discussions with Software Groups & Simulation Groups
We need a shared idea of DAQ Features
  Online, realtime, QA capable of multi-detector correlation
  Feedback to collaboration / collider regarding beam quality and suitability for our physics
  “Scalers”
  Real time monitoring
  Logging Support
  Common communication protocols, component identification
  What general components/support do we need in DAQ and at what level
    Data features created and written out (clusters, track segments, tracks, identified particles?)
    Data filtered after the FEEs (non-track hits? Tracks only? …)
    Software triggering
    ML/AI integration into the data files
    Structure for defining available information at different stages (when can we correlate detector info)
  Data Format
  How do we incorporate Slow Controls/Collider information with the DAQ data?
  Run Log
  [ Do aspects of online computing fall under DAQ? shift logs, web servers maintenance, DBs server maintenance, detector/user computing, shift signup etc… ]
We do need a shared concept of the model:

## Slide 3
Competing Goals:
Capability
  Efficiently remove noise if/when needed
  Determine performance of detectors and of collider in real time
  Framework for extensions Support AI/ML use & development
  Support workarounds for inevitable issues (Say disable readout on signal from collider) (If we use externally developed frameworks we need “In Group” control and expertise of the low-level protocols)
  Tracking of data files and running conditions
  Enabling / Disabling detectors and detector components, and communicating this to analysis
Simplicity
  DAQ system
  Easy to add DAQ supplied data additions (Scalers, data feature readout, clusters, tracks, Pt, output from AI/ML)
  Easy to impliment DAQ supplied data filtering (Software Trigger, Tracking based filtering, AI/ML filters)
  Ability to incorporate unforeseen features
  Natural incorporation of online QA
  Simple, general scheme for calibration needs over many detectors
Efficiency
  Avoid unneeded overhead
    E.g. 64 bit times can’t be used at the hit level, have to be spread out to the frame level
  Avoid multiple copying
  Avoid multiple sets of data pools

## Slide 4
Notes on Assumed Limitations
The more data files required to process a single “time” offline the worse
  HPSS makes correlation of many required files a disaster
  Current software scheme of “No Tape” reconstruction may mitigate this. However, if we did ever need to go “back to the tape” we would regret having large numbers of data files per “time”
FEEs & to an even larger extent DAMS will likely assemble time frames with many chucks of time ordered data.
  Moving to BX level time ordering would require unraveling this in DAQ.
  Staying at Frame level time ordering would require unraveling this in reconstruction and even during QA
  Many “complexity” arguments will have the same tradeoff, so the criteria should be overall complexity if that can be determined.

## Slide 5
Hierarchy of Decisions Needed
Geographical structure of the data files
  How many data files do you need to process to obtain all of the information from a single BX?
  How are data files linked together
Time Granularity of data files
  Standard Frames
  Detector by Detector Frames
  BX
Time Coherency of data files. Do files contain coherent time sequences or time sequences with gaps?
  File #1: tm0 tm50 tm100… (possible to have all detectors in same file)
  File #2: tm1 tm51 tm101…
  Or else: File #1 tm0 tm2 tm… tm 100 (would require subdetectors in different files)
  File #2 tm100… tm200
Do we have lookaside data files?
  File with a list of potential BX corresponding to events
  Separate file for detectors with multi-bunch crossing readout (MAPS)
  File with a list of BX rejections for triggered data….
  Scaler files?
  QA generated files?
What role for databases. Are they required for interpreting collision data? Is this the implementation for lookaside files?

## Slide 6
My Personal Strawman:
Build events so that all detectors from a time frame are in a single file
  Advantages:
    Easy to correlate detectors for QA/reconstruction
    Efficient for reconstruction
    No real efficiency loss in DAQ (assume algorithmic load balancing)
    No data replication due to readout time window differences
  Disadvantages:
    Forces same time frame periods for all detectors
    Time frames per file will not be consecutive (we will need to generate multiple files at one time)
    Scalers, SC, or trigger information from one data file would be incomplete
    Still some untangling of data files to reach BX time levels
Use lookaside file(s) or primary DB for Scalers, SC and/or trigger hypothesis.
If time frames can’t be consistent among all detectors, consider a small number of files, one for each time frame definition.