## Slide 1: Nuclear Data needs for the future of space exploration
8 September, 2022
BNL mini Town Hall on NSAC Long Range Plan for Nuclear Science
Gustavo P. A. Nobre (gnobre@bnl.gov)
On behalf of Dave Brown
National Nuclear Data Center
Nuclear Science and Technology Department

## Slide 2
The GCR background spans a huge mass and energy range covering virtually all of Nuclear Physics
Galactic Cosmic Rays include nuclei as heavy as 56Fe and E/A up to 50 GeV
  For reference, Ebinding(56Fe) ≈ 0.5 GeV
  The range of 1 GeV proton in Al is > 1 m.
It’s even worse near the gas giants where their magnetic field meets the solar wind.
These high-energy particles create cascades of hundreds of secondary, tertiary etc. particles
  The shielding itself can contribute to the variety of secondary particles produced.
  Charged secondary particles deposit a portion of their energy more locally than neutrons
The solar system beyond the atmosphere and the earth’s magnetic field is a tough neighborhood!
Space exploration requires appropriate shielding over a wide range of energy
T.C. Slaba et al.
Life Sciences in Space Research 12 (2017) 1–15
Slide from Lee Bernstein

## Slide 3: Transport codes for shielding applications
Figure 1: Photograph of a BLIP target stack ready for proton bombardment. (courtesy of C. Cutler)
FLUKA simulation of the BLIP target stack showing the primary proton beam and secondary neutron production (N. Simos (2016))
 | FLUKA | INFN (Italy) | http://www.fluka.org/fluka.php | Free reg.
 | PHITS | JAEA (Japan) | https://phits.jaea.go.jp | Open Source
 | MCNP | LANL | https://mcnp.lanl.gov | EC, RSICC
 | GEANT4 | CERN | https://geant4.web.cern.ch | Open Source
 | HZETRN | NASA | https://software.nasa.gov/software/LAR-18803-1 | EC, NASA, Free reg.
All codes have built in models that cover different physical regimes

## Slide 4
https://phits.jaea.go.jp/lec/phits-introduction-en.pdf

## Slide 5
Stopping Powers
(ENDF) data tables
https://phits.jaea.go.jp/lec/phits-introduction-en.pdf

## Slide 6
John Norbury et al.* have shown that large gaps exist in experimental data needed for shielding optimization
“All” projectiles signify He, C, O, Si, Fe
This is where STAR @ RHIC can really help!
*J.W. Norbury et al.
Radiation Measurements 47 (2012) 315e363
Slide from Lee Bernstein

## Slide 7: What data do these codes need to produce meaningful results?
Cross sections: Only total cross section and elastic/reaction cross section needed to first approximation
Particle multiplicities
Outgoing particle distributions: dN/dE’dΩ
Flow, femtoscopy, jets, etc. are unimportant, but coellecense yields are essential!
Two opportunities!
Modeling support for shielding & isotope production applications!
Additional fixed target run at RHIC before EIC

## Slide 8: There are gaps in data compilation: no heavy-ions, not enough high energy
Evaluated (this is what goes in transport codes):
  PDG only elementary particle properties
  CSEWG’s ENDF (US data program) only < 150 MeV + decay data
  Three major regional data projects (JAEA, US, EU) have made forays into HE
Experimental data compilation:
  EXFOR/NSR partial tabulation of data/references most comprehensive but poor HE coverage
  Smaller scale projects with basic science focus: HEPdata, nn-online, GWU DAC
  3 year ROSSINI3 project (ESA-NASA-GSI) (see https://www.gsi.de/work/forschung/biophysik/fragmentation, https://crosssection-db.herokuapp.com)
  Pilot project to compile RHIC/AGS data @NNDC circa 2000, but data appears lost
Opportunity to collaborate to meet data needs for space physics leveraging the high-energy and isotope programs