## Slide 1: EIC Bunch Structure T. Satogata, JLab/ODU EIC Accelerator Development/Pre-Ops L2 Deputy EIC Partner Project Associate Manager For the EIC Accelerator Design/Engineering Team
EPIC DAQ WB September 8, 2022

## Slide 2: Up-front caveats
All parameters here are from CD-1 Conceptual Design Report (CDR)
  Subject to (likely small) changes in baselining for CD-2
EIC design operating assumptions
  Electron energy: ~5-18 GeV continuous
    Design energy reference points are 5, 10, 18 GeV
  Proton energy: 41, 100, 275 GeV, NOT continuous
    Pathlength considerations create “no fly zone” in region between 41-100 GeV proton energies
    Ion energies are similarly constrained, at Z/A ratio

## Slide 3: EIC CDR Luminosity Curve and Limits
e [GeV]
18
10
10
5
5
p [GeV]
275
275
100
100
41
e 10 MW SR limited
Beam-beam limited
p space charge limited
beam size lumi scaling
Nbunches (timing) and bunch intensities modified at highest Ecm to optimize lumi

## Slide 4: EIC CDR Bunch Timings at Store
 | ESR | HSR (Nb=290) | HSR (Nb=1160)
Circumference C [m] | 3833.940 | match Trev | match Trev
Revolution period Trev=C/c [ms] | 12.7886 |  | 
RF harmonic number h [-] | match HSR | 2520 | 7560
RF bucket spacing Tb=Trev/h [ns] NOT bunch spacing!!! | match HSR | 5.075 | 1.692
Number of bunches Nb | match HSR | 290 | 1160
Bunch spacing Tbun [ns] | match HSR | 40.599 | 10.150
Gap length [ns] | match HSR | 1015 | 1015
Trev dominated by electrons: ion energies constrained to match Trev
HSR bunch spacing through cycle: 290 bunches injected into h=315 RF
  1 Tb spacing, 25 Tb gap for h=315 (Nb=290)
  1 Tb spacing (after 1st split), 50 Tb gap for h=630 (Nb=580)
  1 Tb spacing (after 2nd split), 100 Tb gap for h=1260 (Nb=1160)
  2 Tb spacing, 200 Tb gap for h=2520 (Nb=1160)
  6 Tb spacing, 600 Tb gap for h=7560 (Nb=1160)
Notes: 290 bunches in h=315

## Slide 5: EIC CDR Bunch Sizes at Store
The oft-shown animation of crab crossing is a bit misleading on transverse beam sizes
There will be (small) timing correlations to lab frame vertex location as beams pass through each other
  Along direction of electron motion
 | ESR | HSR
RMS bunch length sz [mm/ps] | 7-9/23-30 | 75-60/250-200
RMS momentum spread [10-4] | 5.8-10.9 | 10.3-6.8
RMS horiz beam size sx [um] | 100-250 | 
sz/sx ratio [-] | 28-90 | 240-750
Approximate
actual bunch
x/z sizes

## Slide 6: CDR Parameters: High Divergence e-p

## Slide 7: CDR Parameters: High Acceptance e-p