## Slide 1
1
Secondary Emission Ionization Calorimeters
    Burak Bilki, Yasar Onel - University of Iowa
    David Winn* – Fairfield University
    winn@Fairfield.edu

## Slide 2
Why Secondary Emission Ionization Calorimeters?
Secondary Emission: Rad-Hard + Fast (Damn Fast!)
  Metal-Oxide/Cs SE PMT Dynodes survive > 500 GigaRad
  SEM Beam Monitors survive 1020 mip particles/cm2
SEe signal: SE surfaces inside Hadron Showers:
  SE yield  Scales with particle momentum ~dE/dx
  e-: 3 <  <100, per 0.05 <e-<100 KeV (material depnt)
  ~1.05 -1.1 or 0.05-0.1 SEe- per MIP
  Ex: ~6-24 MIP equiv per GeV(Calice et al)sampling calorimeters - a lower limit on hadron shower SE signals
  > ~60-240 SEe- per 100 GeV pion shower w/ MIPs alone
  BUT SEe- Must be Amplified!

## Slide 3
Why Secondary Emission Ionization Calorimeters? - I
Secondary Emission (SE) signal originates from SE surfaces inside electromagnetic/hadronic showers:
  SEe- yield () scales with particle momentum
  e-: 3 <  <100, per 0.05 <E<100 keV (material dependent)
   ~ 0.05 - 0.1 SEe- per MIP
SE is rad-hard and fast
  a) Metal-Oxide SE PMT Dynodes survive > 100 GigaRad
  b) SE Beam Monitors survive 1020 MIPs/cm2

## Slide 4
 The SEe are treated exactly like PEs in a scintillator calorimeter.
In a scintillator calorimeter, many photons are created, but typically 0.1-1% are collected and converted to PEs by a PMT or SiPM. By contrast, in an SE calorimeter, relatively few SEe are created, but almost all are collected and amplified by the dynode stacks.
A set of SE cathodes and dynodes (SE sensors) may serve as active media in a sampling calorimeter.
Why Secondary Emission Ionization Calorimeters? - II
  Example: ~60-240 SEe- per 100 GeV pion shower w/ MIPs alone
  Normally the secondary electrons are subsequently amplified by a set of dynodes to a suitable level for data acquisition.

## Slide 5
SE Yield/Semi-empirical Sternglass formula: the universal curve of SE emission: SE yield normalized to maximum yield vs particle energy normalized to the energy of max yield.
MgO
CERN beam monitor e, µ, π, p, n
Entrance
Window
cutoff

## Slide 6
High SE Yield Materials
Peak Yields~5-10+; Alumina Easy
MgO
Diamond
SE Yield
Stable in air!
Electrons on MgO
Diamond Gain 300 V vs B Doping Level

## Slide 7
The SE sensor modules need to have sufficiently large areas of dynode to uniformly sense the charged shower particles. Such large and uniform dynodes include electrochemically etched, micromachined or laser-cut metal mesh dynode sheets.
Secondary Emission Sensor Modules
The construction is far easier than a PMT since the entire final assembly can be done in air. There are no critical controlled thin film depositions nor vacuum activation. The module is sealed by welding or brazing or other high temperature joinings with a simple final heated vacuum pump-out and tip-off.
The modules envisioned are compact, high gain, high speed, exceptionally radiation damage resistant and cost effective.
The SE sensor module anodes can be segmented transversely to sizes that are appropriate to reconstruct electromagnetic cores with high precision.

## Slide 8
SE Dynodes: a) Etched Metal Sheets
Hamamatsu Dynodes
15 cm now  ~50 cm
Already diced from large
sheets

## Slide 9
Dn-Dn+1: 0.9 mm
C-C mesh: 13 µm
Wire diameter: 5 µm
MESH DYNODE VARIANTS
SE Dynodes: b) Metal Screen Dynodes: 15D - g~105

## Slide 10
Beam Tests of SE Sensor
We Expect ~500 Shower electrons to Cross Mesh
 ~25-50 SEe assuming all shower e = MIPs
Mesh PMT and Base
Facing Downstream
Photocathode Reverse Bias
or turned off
100 GeV e-
3 cm Pb
19 Stage Mesh
CERN SPS, Oct. 2011

## Slide 11
BEAM TEST: 100 GeV electrons
3 cm Pb ~ 5 X0 Radiator ~ Shower Max
Mesh PMT w/ photocathode turned off and downstream
Peak corresponds to ~40 SE electrons
PRELIMINARY!
Fluctuations High!
PMT Dia ~ Shower Dia
Beam not centered
NOTE µ MIP:
Detection Eff ~10%
Response ~1-2 “SEe”
CERN SPS, Oct. 2011

## Slide 12
SE Module Beam Test
80 GeV e- Beam
Variable absorbers
0 – 9 X0
SE
SE
SE
SE
Shower not contained laterally or longitudinally
 Results require estimates and approximations
2-cm iron absorbers:
X0 = 1.75 cm
Molière Radius: 1.72 cm

## Slide 13
SE Module Tests – Preliminary Results
Normalizing responses of different layers
Example: Normalization of Layer 3 response to Layer 2 response using 7X0 sampling
(Also works in the reverse order  next slide)
Charge > 20 fC

## Slide 14
SE Module Simulation
Geant4 simulation of the SE module test beam setup:
80 GeV e- beam
19 stage mesh dynodes generate SE electrons (dynodes ~ sheets)
Gain is simulated offline (106)
Landau fluctuations are implemented offline

## Slide 15
Second Generation SE Module - I
7 closest-packed PMTs with photocathodes turned off
20 cm x 20 cm x 1.75 cm steel absorbers
4 GeV shower profile

## Slide 16
Second Generation SE Module - II
Tests with single SE sensor and up to 15 3 cm x 3 cm x 0.35 cm W plates
Data taken with wire chamber i.e. the leakage is a bit more under control (but still there)
Data
MC
8 GeV shower profile
Data
MC
16 GeV shower profile

## Slide 17
SE Calorimetry Projections
MC: monotonous quasi-homogeneous 10 µm W mesh,30% open;10µm spacing (Xo~1mm); SE yield max 3 @ 100V. 100 events, 100 GeV electrons; Histogram of collected charge in SEe (105 electrons); Linearity 1-20 GeV.
RMS/E at 100 GeV = 0.0022 -> Stochastic sE/E ≤ 2.2%/√E
High Yield SE materials

## Slide 18
SEe Detector Module -II
3D Stackable x,y,z

## Slide 19
MCPs As Secondary Emitters
Should work effectively
Have simpler design
Should be very fast
No dedicated SE test module yet. But…
We had the Argonne LAPPD (Large Area Picosecond PhotoDetector) MCP to study some (very) preliminaries.
MCP
beam
W absorbers
Fermilab test beam Nov 12-18 2014
Previously studied by A. Rhonzin et.al. and currently by Fermilab and Caltech (next talk).

## Slide 20
Secondary Emission (SE) Calorimetry with MCPs
Argonne MCP comes as a complete photodetector box with a relatively thick glass window. Newer production allows the turning off of the photocathode.
Nevertheless, it is worth trying it as a secondary emission module
 a reasonable shower profile is an indicator of potential performance.
Ideal SE module utilizing MCPs
Insulator
A thin cathode, possibly a secondary emitter layer of high yield material
MCP
anode

## Slide 21
Secondary Emission (SE) Calorimetry with MCPs
MCP
beam
W absorbers
Tested the LAPPD with up to 12 3 cm x 3 cm x 0.35 cm W plates
4 GeV and 8 GeV secondary beams were used triggering with positrons (i.e. with the Čerenkov counter signal in the trigger decision)
Two strips were read out at one end (smaller than the shower size)
Results quite encouraging!
4 GeV
8 GeV

## Slide 22
Select the events with particles traversing the strip:
X: 40 – 85 mm
Y: 56 – 62 mm
~ window boundary
Trigger area ~ 5 cm x 3 cm
One strip read out at both ends
Position Reconstruction with LAPPD
Total signal (R+L) profile

## Slide 23
Position Reconstruction with LAPPD
Fraction of the L signal as a function of x along the strip
Very small correlation, not quite significant.
Time difference between L and R signals
Strong correlation!
Event position can be reconstructed with timing techniques.  More on this in the next talk.
a+bx
a+bx

## Slide 24
Conclusions
Secondary Emission calorimeter is radiation-hard and fast.
Progressive beam test results are encouraging.
SE calorimetry is feasible for large-scale applications.
SE calorimetry is suitable for fine readout segmentation hence imaging calorimetry.
There are many implementation areas for SE calorimetry:
  Forward calorimetry for hadron/lepton/ion colliders
  Beam monitors
  Compton polarimetry for lepton colliders

## Slide 25
Outlook
A dedicated Secondary Emission module is needed for complete validation: Identify a secondary emitter as the cathode. Then use either dynodes of the same type or MCPs as multipliers.