## Slide 1: dRICH Vessel Analysis
Date: 25 Aug 2021
Engineer: C. Taylor
Approver: P. Orfin

## Slide 2: Outline
Technical Requirements
Material Comparison
Recommendations
Analysis

## Slide 3: Technical Requirements
dRICH Vessel Analysis

## Slide 4: Specifications
Source: S. Dalla Torre, 11 August 2021 Presentation
    Entrance and exit walls can deform up to 1-2 cm
    Entrance and exit wall deformation should not induce backbone deformations
    Lateral walls can be thick and rigid (sensor – backbone interface)
    Gas radiator pressure <= 3 bar (absolute)
    Sensor operating temperature = 30-40°C
    Material must be nonmagnetic

## Slide 5: Geometry
Vessel Shape
I.D. | Value (cm) | Description
sd0 | 130 | Overall Length
sd1 | 200 | Outer Radius
sd2 | 10.5 | Beam Tube ID
sd3 | Varied | Beam Tube Wall
sd4 | Varied | Endcap Thk. (2x)
sd5 | Varied | Cylinder Wall
sd6 | Varied | Rib Thk. (6x)
sd0
sd1
sd2
sd3
sd5
sd4
sd6

## Slide 6: Analysis v.2 – 25 Aug 2022 (Ribs Added)
Static Structural using Design of Experiments in ANSYS 2022 R2

## Slide 7: Load Conditions
  Analysis was performed using a 60° wedge
  Analysis does not include gravity
Cyclic Region Symmetry
14.7 psi
3 bar (absolute)
Vacuum
(Beam Tube)
Mirror Symmetry
Update to remove vacuum condition

## Slide 8: Mesh Details

## Slide 9: Mesh Study
Chart: Mesh Element Size (in)
| 0.25 | 0.26041666666666602 | 0.27083333333333298 | 0.28125 | 0.29166666666666602 | 0.30208333333333298 | 0.3125 | 0.32291666666666602 | 0.33333333333333298 | 0.34375 | 0.35416666666666602 | 0.36458333333333298 | 0.375 | 0.38541666666666602 | 0.39583333333333298 | 0.40625 | 0.41666666666666602 | 0.42708333333333298 | 0.4375 | 0.44791666666666602 | 0.45833333333333298 | 0.46875 | 0.47916666666666602 | 0.48958333333333298 | 0.5
 | 145.792 | 144.6081 | 143.1979 | 141.6918 | 140.1731 | 138.7203 | 137.4493 | 136.3567 | 135.3066 | 134.2631 | 133.2468 | 132.3432 | 131.7177 | 131.577 | 131.823 | 132.2223 | 132.6039 | 132.801 | 132.5953 | 131.8817 | 130.8396 | 129.6306 | 128.3529 | 127.0699 | 125.8342
Used for this study

## Slide 10: Sensitivity of Thicknesses
Endcap
Wall
Rib
Beam Tube
Endcap
Wall
Rib
Beam Tube
Local Sensitivity (%)
Max Stress
Max Deformation (Z-dir)
The endcap thickness is the main contributor to results

## Slide 11: Endcap Thickness vs. Stress
304 Stainless Steel Yield Stress
Titanium Ti-6Al-4V (Grade 5) Yield Stress
Titanium (Grade 12) Yield Stress
Aluminum 6061-T6 Yield Stress
Chart: Endcap Thickness (cm)
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25
w/o Ribs | 5960.25 | 1490.0625 | 662.25 | 372.5156 | 238.41 | 165.5625 | 121.6378 | 93.1289 | 73.5833 | 59.6025 | 49.2583 | 41.3906 | 35.2678 | 30.4094 | 26.49 | 23.2822 | 20.6237 | 18.3958 | 16.5104 | 14.9006 | 13.5153 | 12.3146 | 11.267 | 10.3477 | 9.5364
w/ Ribs | 1933.955 | 1789.8416 | 1644.8323 | 1499.921 | 1356.3494 | 1215.3098 | 1077.7299 | 944.5772 | 816.829 | 695.3911 | 581.0664 | 474.6896 | 380.264 | 302.468 | 237.5504 | 182.4289 | 137.169 | 101.8362 | 76.3226 | 60.3772 | 53.6136 | 55.4185 | 65.0367 | 81.7292 | 104.6956
(see 9/10/2021 Analysis)
Note: The intersection of the black solid and red dash lines indicates the thickness required for a Factor of Safety of 1 on the yield strength for a given material.

## Slide 12: Static Structural Results
Note: Results are shown for a 304 stainless steel vessel with 3 cm [1.2 in] endcaps and a 2.5 cm [1.0 in] wall thickness including an Ø21.0 I.D. x 2.5 cm thick beam tube. Weight as shown is 22,800 lbs. (1,900 x 6 sections x 2 halves).
σmax = 142 MPa
ΔZ-dir = +0 / - 0.21 cm
Max stress is the limiting factor for the thickness required

## Slide 13: Radial Deformation
The maximum radial deflection of the vessel wall is 0.02 cm when analyzing a stainless steel vessel with 3.0 cm thick endcaps and 2.5 cm thick vessel walls.
Deformation is measured in the X-Dir on a cylindrical coordinate system.
Deformation
Cylindrical CSYS

## Slide 14: Material Comparison
Material properties were obtained from MatWeb.com

## Slide 15: Strength to weight comparisons
Radius | 200 | cm |  |  |  |  | 
Endplate Thickness | 3 | cm |  |  |  |  | 
Vessel Wall Thickness | 2.5 | cm |  |  |  |  | 
Length | 130 | cm |  |  |  |  | 
Rib Thickness (6x) | 2.5 | cm |  |  |  |  | 
Volume | 1.53 | m^3 |  |  |  |  | 
 | Density | Weight |  | Yield Strength | Deflection @ 3 bar | FoS @ 3 bar | Material Cost*
 | (kg/m^3) | (kg) | (ton) | (MPa) | (cm) |  | ($)
Aluminum 6061-T6 | 2698.8 | 4132.1 | 4.6 | 276 | 0.59 | 1.9 | $ 51,060
Titanium Ti-6Al-4V (Grade 5) | 4428.8 | 6780.9 | 7.5 | 880 | 0.36 | 6.2 | $ 882,280
Titanium (Grade 12) | 4511.8 | 6908.1 | 7.6 | 380 | 0.39 | 2.7 | $ 882,280
304 Stainless Steel | 7999.5 | 12248.1 | 13.5 | 215 | 0.21 | 1.5 | $ 174,090
*Notes:
The material cost estimates are intended to show order of magnitude only. Actual costs will be dependent on fabrication method of the final design.
Costs have been estimated using quotes provided for 1x48x60 inch plates of each material. A cost per unit volume was calculated and used to determine the material cost listed below.

## Slide 16: Recommendations

## Slide 17: Things to consider
The ribs can be optimized to remove the material not participating in the stress distribution further light weighting the design.
Titanium alloys provide an optimal blend of material properties for this application (i.e., strength to weight ratio). A cost vs. benefit analysis would need to be performed to justify this alternative.
How is this vessel supported?
Questions / Comments?