## Slide 1: dRICH Vessel Analysis
Date: 25 Aug 2021
Engineer: C. Taylor
Approver: P. Orfin

## Slide 2: Outline
Summary
Technical Requirements
Analysis
Closed Form Calculation
Material Comparison
Analysis w/ Beam Tube
Division 1 PV Code
Analysis w/ Div. 1 Geometry
Recommendations

## Slide 3: Summary
dRICH Vessel Analysis

## Slide 4: Executive Summary
A conceptual study was performed to determine the structural requirements of a vacuum vessel containing sensitive equipment used in the dRICH and analyzed for feasibility.
The space envelope of the vessel defined by the ATHENA P-0.0 configuration is roughly Ø4.00m x 1.30m in length with flat ends.
ANSYS and closed form calculations show that the wall thickness for an aluminum vessel would be roughly 10.0cm and weigh 11 tons! This result is driven mainly by the deformation limit required to reduce the impact of alignment errors induced by backbone deformations.
PV Elite concluded that a 316 stainless steel vessel with 9cm thick ends with a 1.14cm thick cylinder wall weighing 21 tons would be required to meet the conservative division 1 code.
Alternative geometries were investigated along with various material selections with the goal of reducing the material required for the vessel. It was determined that the preferred geometry using two torispherical ends would NOT fit within the required space envelope. For this reason, a combination of one flat and one torispherical end was investigated.

## Slide 5: Executive Summary – cont’d
The PV Elite results for the flat and torispherical end combination resulted in a 316 stainless steel vessel with a flat end wall thickness of 9.8 cm, torispherical wall of 1.4 cm and a cylinder wall of 1.0 cm weighing 13.4 tons.
Recommendations are provided at this end of this report.

## Slide 6: Technical Requirements
dRICH Vessel Analysis

## Slide 7: Specifications
Source: S. Dalla Torre, 11 August 2021 Presentation
    Entrance and exit walls can deform up to 1-2 cm
    Entrance and exit wall deformation should not induce backbone deformations
    Lateral walls can be thick and rigid (sensor – backbone interface)
    Gas radiator pressure <= 3 bar (absolute)
    Sensor operating temperature = 30-40°C
    Material must be nonmagnetic

## Slide 8: Geometry
Vessel Shape
I.D. | Value (cm) | Description
sd0 | 130 | Length
sd1 | 200 | Radius
sd4 | Varied | Endcap
sd6 | Varied | Wall
sd8 | = sd4 | Endcap
Beam Tube

## Slide 9: Analysis
Static Structural using Design of Experiments in ANSYS 2021 R2

## Slide 10: Load Conditions
  Analysis was performed using a 5° wedge divided into 3 sections such that the endcap and vessel wall could be analyzed individually
  Weak springs were allowed for this analysis
  3 elements through the wall thickness were maintained as dimensions were varied
  Analysis does not include gravity
Cyclic Region Symmetry
14.7 psi
3 bar (absolute)
Beam Tube

## Slide 11: Static Structural Results
Note: Results are shown for a 11.1 ton Aluminum 6061-T6 vessel with 9.5 cm [3.74 in] endcaps and a 10.0 cm [3.94 in] wall thickness
σmax = 64.0 MPa , σcenter = 50.3 MPa
ΔZ-dir = +/- 1.0 cm
Beam Tube
Beam Tube

## Slide 12: Radial Deformation
The maximum radial deflection of the vessel wall is .039 cm when analyzing an aluminum vessel with 9.5 cm thick endcaps and 10.0 cm thick vessel walls. This will need to be considered when designing the backbone support.
Deformation is measured in the X-Dir on a cylindrical coordinate system.
Deformation
Cylindrical CSYS
Beam Tube

## Slide 13: Radial Deformation vs. Wall Thickness
A 10 cm thick aluminum vessel wall was selected as a baseline for comparison

## Slide 14: Closed Form Calculation
ANSYS results are verified using Mathcad

## Slide 15: Calculations
 | ANSYS | Mathcad | %Diff
Deflection (cm) | 1.00 | 0.90 | 10%
Center Stress (MPa) | 50.3 | 43.9 | 13%
Fixed Edge Stress (MPa) | 64.0 | 66.0 | -3%
ANSYS results agree with closed form calculations bounded by 2 different sets of boundary conditions, fixed edge and simply supported. Results align more closely with fixed edge as expected suggesting a factor of safety of ~ 3 for an aluminum endcap 9.5 cm thick.

## Slide 16: Endcap thickness vs. Deformation
Specified allowance

## Slide 17: Endcap Thickness vs. Stress
304 Stainless Steel Yield Stress
Titanium Ti-6Al-4V (Grade 5) Yield Stress
Titanium (Grade 12) Yield Stress
Aluminum 6061-T6 Yield Stress

## Slide 18: Material Comparison
Material properties were obtained from MatWeb.com

## Slide 19: Strength to weight comparisons
Radius | 200 | cm |  | 
Endplate Thickness | 9.5 | cm |  | 
Vessel Wall Thickness | 10 | cm |  | 
Length | 130 | cm |  | 
Volume | 3.75 | m^3 |  | 
 | Density | Weight |  | Yield Strength
 | (kg/m^3) | (kg) | (sh.tn.) | (MPa)
Aluminum 6061-T6 | 2698.8 | 10114.0 | 11.1 | 276
Titanium Ti-6Al-4V (Grade 5) | 4428.8 | 16597.3 | 18.3 | 880
Titanium (Grade 12) | 4511.8 | 16908.5 | 18.6 | 380
304 Stainless Steel | 7999.5 | 29978.9 | 33.0 | 215

## Slide 20: Analysis w/ Beam Tube
Static structural analysis repeated with Ø8.00 x 1.00 thick beam tube included using Ansys 2021 R2

## Slide 21: Load Conditions
  Analysis was performed using a 5° wedge divided into 3 sections such that the endcap and vessel wall could be analyzed individually
  Weak springs were allowed for this analysis
  3 elements through the wall thickness were maintained as dimensions were varied
  Analysis does not include gravity
Cyclic Region Symmetry
14.7 psi
3 bar (absolute)
Ultra-High Vacuum

## Slide 22: Static Structural Results
Note: Results are shown for an aluminum 6061-T6 vessel with 9.5 cm [3.74 in] endcaps and a 10.0 cm [3.94 in] wall thickness including an Ø8.00 x 1.00 thick 304 stainless steel beam tube
σmax = 215 MPa
ΔZ-dir = +/- 0.13 cm
Beam Tube
Beam Tube

## Slide 23: Radial Deformation
The maximum radial deflection of the vessel wall is .012 cm when analyzing an aluminum vessel with 9.5 cm thick endcaps and 10.0 cm thick vessel walls. This will need to be considered when designing the backbone support.
Deformation is measured in the X-Dir on a cylindrical coordinate system.
Deformation
Cylindrical CSYS
Beam Tube

## Slide 24: Division 1 PV Code
Minimum material thickness was determined using PV Elite per Division 1 pressure vessel code requirements

## Slide 25: Welded Flat End Results
Beam Tube

## Slide 26: Welded Flat & Torispherical End Results
r = 0.1*D
R = 0.9*D
Wtitanium = 15,097.0 lbm [ 7.6 tons]
W316 SST =
Note: Aluminum is not advised to to deformations being 3x greater than that of SST
[ 13.4 tons]
Beam Tube

## Slide 27: Analysis w/ Div. 1 Geometry
Static structural analysis repeated with geometry determined by PV Elite using Ansys 2021 R2

## Slide 28: Welded Flat & Torispherical End Results
σmax = 273 MPa
ΔZ-dir = +1.13 / -0.25 cm
Note: Results are shown for a 316 stainless steel vessel. Actual maximum stress will be lower due to welds distributing the stress more evenly at the vessel wall and flat plate transition.
Beam Tube
Beam Tube

## Slide 29: Recommendations

## Slide 30: Things to consider
Incorporating two torispherical ends would greatly reduce the material requirement however, this would require an increase in the existing space envelope. Further investigation would be necessary to determine the exact amount needed.
Internal structural supports such as ribs would decrease the deformation significantly resulting in a lighter, more optimized vessel. One possible alternative could be strategically integrating the mirror support frame as part of an internal vessel support structure.
Titanium alloys provide an optimal blend of material properties for this application (i.e., strength to weight ratio). A cost vs. benefit analysis would need to be performed to justify this alternative.
Questions / Comments?

## Slide 31: Analysis v.2 – 25 Aug 2022 (Ribs Added)
Static Structural using Design of Experiments in ANSYS 2022 R2

## Slide 32: Geometry
Vessel Shape
I.D. | Value (cm) | Description
sd0 | 130 | Length
sd1 | 200 | Radius
sd2 | 10.5 | Beam Tube ID
sd3 | Varied | Beam Tube Wall
sd4 | Varied | Endcap
sd5 | Varied | Wall
sd6 | Varied | Rib
sd0
sd1
sd2
sd3
sd5
sd4
sd6

## Slide 33: Load Conditions
  Analysis was performed using a 60° wedge
  Analysis does not include gravity
Cyclic Region Symmetry
14.7 psi
3 bar (absolute)
Vacuum
(Beam Tube)
Mirror Symmetry

## Slide 34: Mesh Details

## Slide 35: Mesh Study
Chart: Mesh Element Size (in)
| 0.25 | 0.26041666666666602 | 0.27083333333333298 | 0.28125 | 0.29166666666666602 | 0.30208333333333298 | 0.3125 | 0.32291666666666602 | 0.33333333333333298 | 0.34375 | 0.35416666666666602 | 0.36458333333333298 | 0.375 | 0.38541666666666602 | 0.39583333333333298 | 0.40625 | 0.41666666666666602 | 0.42708333333333298 | 0.4375 | 0.44791666666666602 | 0.45833333333333298 | 0.46875 | 0.47916666666666602 | 0.48958333333333298 | 0.5
 | 145.792 | 144.6081 | 143.1979 | 141.6918 | 140.1731 | 138.7203 | 137.4493 | 136.3567 | 135.3066 | 134.2631 | 133.2468 | 132.3432 | 131.7177 | 131.577 | 131.823 | 132.2223 | 132.6039 | 132.801 | 132.5953 | 131.8817 | 130.8396 | 129.6306 | 128.3529 | 127.0699 | 125.8342
Used for this study

## Slide 36: Sensitivity of Thicknesses
Endcap
Wall
Rib
Beam Tube
Endcap
Wall
Rib
Beam Tube
Local Sensitivity (%)
Max Stress
Max Deformation (Z-dir)
The endcap thickness is the main contributor to results

## Slide 37: Endcap Thickness vs. Stress
304 Stainless Steel Yield Stress
Titanium Ti-6Al-4V (Grade 5) Yield Stress
Titanium (Grade 12) Yield Stress
Aluminum 6061-T6 Yield Stress
Chart: Endcap Thickness (cm)
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25
w/o Ribs | 5960.25 | 1490.0625 | 662.25 | 372.5156 | 238.41 | 165.5625 | 121.6378 | 93.1289 | 73.5833 | 59.6025 | 49.2583 | 41.3906 | 35.2678 | 30.4094 | 26.49 | 23.2822 | 20.6237 | 18.3958 | 16.5104 | 14.9006 | 13.5153 | 12.3146 | 11.267 | 10.3477 | 9.5364
w/ Ribs | 1933.955 | 1789.8416 | 1644.8323 | 1499.921 | 1356.3494 | 1215.3098 | 1077.7299 | 944.5772 | 816.829 | 695.3911 | 581.0664 | 474.6896 | 380.264 | 302.468 | 237.5504 | 182.4289 | 137.169 | 101.8362 | 76.3226 | 60.3772 | 53.6136 | 55.4185 | 65.0367 | 81.7292 | 104.6956
(Previous Analysis)

## Slide 38: Static Structural Results
Note: Results are shown for a 304 stainless steel vessel with 3 cm [1.2 in] endcaps and a 2.5 cm [1.0 in] wall thickness including an Ø21.0 I.D. x 2.5 cm thick beam tube. Weight as shown is 22,800 lbs. (1,900 x 6 sections x 2 halves).
σmax = 142 MPa
ΔZ-dir = +0 / - 0.21 cm
Max stress is the limiting factor for the thickness required

## Slide 39: Radial Deformation
The maximum radial deflection of the vessel wall is 0.02 cm when analyzing a stainless steel vessel with 3.0 cm thick endcaps and 2.5 cm thick vessel walls.
Deformation is measured in the X-Dir on a cylindrical coordinate system.
Deformation
Cylindrical CSYS

## Slide 40: Things to consider
The ribs can be optimized to remove the material not participating in the stress distribution further light weighting the design.
Titanium alloys provide an optimal blend of material properties for this application (i.e., strength to weight ratio). A cost vs. benefit analysis would need to be performed to justify this alternative.
Questions / Comments?