## Slide 1: CIELO Data Validation and Benchmarking Activities at the IAEA
A. Trkov, R. Capote
International Atomic Energy Agency
Vienna, Austria

## Slide 2: Acknowledgement
The work presented herein is the result of contributions from several IAEA consultants and voluntary contributions from external collaborators…

## Slide 3: Overview
Scope of data testing at the IAEA with examples
Pitfalls in the use of figures of merit (FoM)
Discrepancies in integral benchmarks
Uncertainties due to data processing and self-shielding treatment

## Slide 4: Scope of data testing
Strategy – taking 235U as an example:
  Start with clean bare configurations
  Proceed with thermal solutions
  Include well-tested reflected systems
  More complex assemblies and broad scope testing

## Slide 5: Bare 235U configurations
Observations:
Large discrepancies in predicted reactivity, which is unreasonable since sensitivities to nuclear data are similar. Examples:
  Caliban: 1% over-prediction (MCNP and TRIPOLI), 0.5% inconsistency in mass of fissile material, neglecting measured abundances of B, etc.)
  ORNL spheres predicted high compared to cylinders
  Discrepancies in the Russian benchmarks (0.5%)…
 There is a need to resolve the discrepancies

## Slide 6: Bare 235U configurations

## Slide 7: HEU Thermal Solutions
Traditionally, the “above-thermal leakage fraction” (ATLF) is an established parameter for characterising solution assemblies
To save time, representative cases were chosen that span the wide range of values
With “beta-2” good performance is preserved
Again, there is large scatter in some groups of benchmarks

## Slide 8: HEU Thermal Solutions

## Slide 9: Reflected assemblies
Preference for simple configurations with few materials that have well-known cross sections
A selection of traditionally used assemblies was collected into the so-called “main” list

## Slide 10: Reflected and other assemblies (main)

## Slide 11: List of “main” benchmarks
1 HEU-MET-FAST-001 hmf001 Godiva
2 HEU-MET-FAST-028 hmf028 Flattop-25
3 IEU-MET-FAST-007 imf007d Big_Ten(detailed)
4 PU-MET-FAST-001 pmf001 Jezebel
5 PU-MET-FAST-002 pmf002 Jezebel-240
6 PU-MET-FAST-006 pmf006 Flattop-Pu
7 U233-MET-FAST-001 umf001 Jezebel-U233
8 U233-MET-FAST-006 umf006 Flattop-23
9 PU-MET-FAST-022 pmf022 Bare(98
10 PU-MET-FAST-029 pmf029 Bare(88
11 IEU-MET-FAST-001 imf001-001 Jemima-1
12 IEU-MET-FAST-001 imf001-002 Jemima-2
13 IEU-MET-FAST-001 imf001-003 Jemima-3
14 IEU-MET-FAST-001 imf001-004 Jemima-4

## Slide 12: Broad scope testing
Benchmarking depends on:
  Availability of input models
  Computer resources
  Capacity to analyse the results
Different sets are used at various places (NRG, LANL, CEA…)
Example:
  Los Alamos suite of 119 ICSBEP benchmarks

## Slide 13: Broad scope testing
Hard to extract useful information!
Notes: One cannot extract useful information.

## Slide 14: Broad scope testing (2σ outliers e80b2)
Presenting 2-sigma outliers only
Notes: Focusing on outliers – some are better, some are worse.
There could be dependence on less-well known materials
The assigned uncertainties of some benchmarks are unreasonably small.

## Slide 15: Pitfalls in the use of FoM
Different possibilities for defining Figures of Merit (FoM) exist:
  r.m.s. Delta-k – equal weight to all, including cases of low accuracy
  Χ2/DoF – sensitive to cases with unrealistically small uncertainties
  … other

## Slide 16: Cumulative contribution to Χ2/DoF
Chart: 
umf003,004
233U, 238U
“main” benchmarks
Jemima
Zeus
Notes: From FoM alone, JEFF-3.3T2 is the winner, but there is more to it.

## Slide 17: Discrepancies in integral benchmarks
As illustrated in the case of bare 235U assemblies, discrepancies of several hundred pcm (parts per 100 000) for cases with similar spectra and sensitivity profiles are more likely caused by bad description or bad benchmark models
A strong effort is needed to resolve such discrepancies

## Slide 18: Data processing and methods
Monte Carlo codes can treat geometry accurately
Starting from the same data source they should give the same result
Differences occur due to:
  Data processing (e.g. resonance reconstruction)
  Methods (e.g. self-shielding in the unresolved resonance range (URR))
  Other …

## Slide 19: Resonance reconstruction
Example:
  Make an ACE file with NJOY
  Convert back to ENDF
  Process the same library with PrePro with 0.1% reconstruction tolerance and same temperature
  Compare the two files
  Study the impact of differences on benchmarks
    E.g. NJOY, PrePro, GRUCON (preliminary, ACE files provided by V. Sinitsa)

## Slide 20: 238U Resonance reconstruction
238U is a good case, that can be fixed by input

## Slide 21: 239Pu Unresolved resonance range
239Pu (NJOY) deviates from ENDF-6 rules in URR
Switching to LSSF=1 representation can help

## Slide 22: 238U Fission Cross Section

## Slide 23: 238U Fission Cross Section
(Provided by D.E. Cullen)

## Slide 24: Impact on selected ICSBEP benchmarks
Only 235U and 238U x.s. changed
Notes: There seems to be some bias in NJOY results, consistent with the observed lower precision in reconstructing the cross sections.
Note the scale, however!

## Slide 25: Self-shielding in the URR - importance
Only 235U and 238U x.s. changed

## Slide 26: Self-shielding in the URR - methods
NJOY probability table method (PTM)
PrePro multi-band parameters
GRUCON average parameters (preliminary , ACE files provided by V. Sinitsa)
Analysis is limited to 235U and 238U, the rest is taken from the generic MCNP library)

## Slide 27: Self-shielding in the URR - methods
Only 235U and 238U x.s. changed

## Slide 28: Conclusions
Discrepancies in integral benchmarks with similar spectra and sensitivities should be resolved
One should be careful in the interpretation of FoM
MC calculations are NOT exact – be aware of uncertainties due to data processing and due to methods

## Slide 29: Conclusions (cont.)
With current data libraries we are converging for well-defined benchmarks; tight convergence criteria are needed
Detailed benchmark models should be used whenever possible to avoid ambiguities

## Slide 30: List of benchmarks in the study of methods
1 HEU-MET-FAST-001 hmf001 Godiva
2 HEU-MET-FAST-002 hmf002-2 Topsy-2
3 HEU-MET-FAST-003 hmf003-01 Topsy-U_2.0in
4 HEU-MET-FAST-003 hmf003-02 Topsy-U_3.0in
5 HEU-MET-FAST-003 hmf003-03 Topsy-U_4.0in
6 HEU-MET-FAST-003 hmf003-10 Topsy-W_4.5in
7 HEU-MET-FAST-003 hmf003-11 Topsy-W_6.5in
8 HEU-MET-FAST-014 hmf014 VNIIEF-CTF-DU
9 HEU-MET-FAST-032 hmf032-1 COMET-TU1_3.93in
10 HEU-MET-FAST-032 hmf032-2 COMET-TU1_3.52in
11 HEU-MET-FAST-032 hmf032-3 COMET-TU1_1.742in
12 HEU-MET-FAST-032 hmf032-4 COMET-TU1-0.683in
13 IEU-COMP-FAST-004 icf004 ZPR-3/12
14 IEU-MET-FAST-007 imf007 Big_Ten
15 IEU-MET-FAST-007 imf007d Big_Ten(detailed)
16 IEU-MET-FAST-010 imf010 ZPR-6/9(U9)
17 IEU-MET-FAST-012 imf012 ZPR-3/41
18 IEU-MET-FAST-013 imf013 ZPR-9/1
19 IEU-MET-FAST-014 imf014-2 ZPR-9/2
20 IEU-MET-FAST-022 imf022-01 FR0_3X-S
21 IEU-MET-FAST-022 imf022-02 FR0_5-S
22 IEU-MET-FAST-022 imf022-03 FR0_6A-S
23 IEU-MET-FAST-022 imf022-04 FR0_7-S
24 IEU-MET-FAST-022 imf022-05 FR0_8-S
25 IEU-MET-FAST-022 imf022-06 FR0_9-S
26 IEU-MET-FAST-022 imf022-07 FR0_10-S
27 MIX-MISC-FAST-001 mif001-01 BFS-35-1
28 MIX-MISC-FAST-001 mif001-02 BFS-35-2
29 MIX-MISC-FAST-001 mif001-03 BFS-35-3
30 MIX-MISC-FAST-001 mif001-09 BFS-31-4
31 MIX-MISC-FAST-001 mif001-10 BFS-31-5
32 MIX-MISC-FAST-001 mif001-11 BFS-42