## Slide 1: Criticality Benchmark Simulations with ENDF/B-VIII.b2 Structural Material Evaluations in GND Format
ND2016
Marie-Anne Descalle, Bret Beck, Caleb Mattoon, Pavlos Vranas, David Brown*
Lawrence Livermore National Laboratory, Livermore, CA
*Brookhaven National Laboratory, Uptown, NY
September 14, 2016

## Slide 2: Generalized Nuclear Data Format Why are we working on it?
Current formats are not very flexible
  half a century old formats
  ENDF (~1968); ENDL(1959)
Data
  Greater precision
  No limit on reaction type
  Accommodate new data types
  Physics-oriented format
  Data sharing: stores evaluated data, as well as MC and deterministic processed data
Codes
  Legacy pre-processing, processing and translation codes are difficult to maintain
  Implementation with GND is simpler

## Slide 3: LLNL GND-friendly Codes and what they can do
FUDGE: For Updating Data and Generating Evaluations
  Translates ENDF formatted data into GND formatted data
  processes GND data for use in Monte Carlo and deterministic transport code, including,
    reconstructing cross sections and angular distributions from resonance parameters,
    and heating cross-sections.
GIDI: General Interaction Data Interface
  read and perform Monte Carlo sampling from GND-formatted data
  implemented for LLNL Monte Carlo code MERCURY and GEANT4
MERCURY: LLNL all particle-transport Monte Carlo code
  MCAPM (old LLNL mcf format)
  GIDI (GND format)
Related presentations at ND2016:B. Beck (FUDGE, GIDI), C. Mattoon (GND)
We now can translate ENDF data , process them and run MC simulations with data in GND format

## Slide 4: ENDF Evaluations in GND format
Three ENDF library releases translated in GND format:
  ENDF/B-VII.1
  ENDF/B-VIII.0b1
  ENDF/B-VIII.0b2- (released 8/19)
Al, Ni, Cu, W and Pb reflectors
  angular distributions can be generated using the FUDGE angular distribution reconstruction capability.
  Results: Data from ENDF file, no reconstruction, no probability table, no thermal n scattering
56Fe evaluations: CIELO, CNDC
84 fast criticality benchmarks from LLNL V&V test suite were run with MERCURY/GIDI
Some comparison to MCNP5 – ENDF/B-VII.1 results
  [Kahler et al. NDS 112 (2011) 2997-3036]

## Slide 5: From ENDF/BVII.0 and ENDF/BVII.1 Fast Criticality Benchmarks
bare
Al
Be
W
Cu
Co
DU
Ni
Pb
Fe
Ti
U
Ordinate: keff

## Slide 6: ENDF/bVII.1 (GND)
ENDF/B-VII.1: MERCURY/GIDI results are in good agreement with MCNP results except for a few cases with U, Fe reflectors
bare
Al
Be
W
Cu
Co
DU
Ni
Pb
Fe
Ti
U
Ordinate: keff

## Slide 7: ENDF/bVIII.0b1 (GND)
ENDF/B-VIII.0b1: Large discrepancies for k effective of critical assemblies with Cu reflectors
bare
Al
Be
W
Cu
Co
DU
Ni
Pb
Fe
Ti
U
Ordinate: keff

## Slide 8: ENDF/BVIII.0b2 (GND)
The new format enables fast turn around when comparing evaluationss.
bare
Al
Be
W
Cu
Co
DU
Ni
Pb
Fe
Ti
U
Ordinate: keffs

## Slide 9: Godiva, Jezebel, Jezebel240, Flattop25 & Pu, Big10

## Slide 10: Cu reflector
ENDF/B-VIII.0b1 to b2: major changes to Cu evaluations
combined to changes in actinides evaluations
b1: fine angular distribution, issues with
double points
b2: Cu angular distribution was modified.

## Slide 11: Al reflector
ENDF/B-VIII.0b1 to b2: changes in actinides evaluations

## Slide 12: Ni reflector
ENDF/B-VIII.0b1 to b2: changes in actinides evaluations

## Slide 13: Ti reflector
ENDF/B-VIII.0b1 to b2: no major changes of Ti evaluations
Difference due to changes in actinides evaluations

## Slide 14: W & Pb reflector
W
Pb
ENDF/B-VIII.0b1 to ENDF/B-VIII.0b2: 180, 182, 183 W changes should affect outgoing gammas
Difference due to changes in actinides evaluations

## Slide 15: CIELO 56Fe evaluations in GND format
ENDF/B-VIII.0b1 includes 56Fe CIELO 243

## Slide 16: ENDF/B.VIII.0 56Fe evaluations in GND format
ENDF/B-VIII.0b2: k effective for PMF assemblies calculated with MERCURY/GIDI are consistent with M. Herman’s MCNP results.

## Slide 17: Conclusion
ENDF/b-VII.1 and ENDF/b-VIII.0b1 and b2 XS libraries are now in GND format, no probability tables and no thermal scattering
Ran 84 criticality benchmarks of the V&V test suite using Mercury/GIDI
Demonstrated the new processing and simulation capabilities of GND, FUDGE and MERCURY/GIDI are working
Overall, MCNP and MERCURY/GIDI are in fairly good agreement for ENDF/B-VII.1 results
ENDF/b-VIII.0b2 versus b1:
  yields lower keff than the b1 version probably due to increased n capture in new actinides evaluations
  Revised Cu evaluations: improvement but underestimation of keff
  56Fe evaluation: overestimation of keff in particular for PMF assemblies
  No changes for Al, Ni, Ti, W, Pb
Allows for rapid integration and comparison of new evaluations

## Slide 18: Ongoing & Future Work
GIDI is being implemented for LLNL Sn code Ardra, and V&V testing will start next month
Angular biasing will be implemented in GIDI
  TOF LLNL Pulsed Spheres
FUDGE will translate data from GND to ACE format for comparison to MCNP results
  We will start testing reconstructed angular distributions within the next two months
Following implementation, we plan to use criticality benchmark simulations to test:
  Probability tables
  Thermal scattering