## Slide 1: LLNL nuclear data processing
CSEWG 2016
Bret Beck
Nov. 15, 2016

## Slide 2: Outline
The “protare”
GND
LLNL nuclear data infrastructure:
  FUDGE
GIDI: GND API
  GND is a new nuclear data format (structure) for storing data
    Caleb’s talk

## Slide 3: The protare
A set of nuclear reaction data for a PROjectile hitting a TARget for an Evaluation
  Examples:
Like an ENDF NSUB + MAT + NLIB
A GND file represents one protare
  Protare: ‘n’, ‘O16’, ‘ENDF/B-VII.1’
  Protare: ‘n’, ‘O16’, ‘ENDF/B-8_beta2’
  Protare: ‘n’, ‘O16’, ‘JENDL-4.0’
‘Map’ file allows all three to be in a data library release
  ‘Map’ is not an official SG38 definition
n + O16 for ENDF/B-VII.0
n + Fe56 for ENDF/B-8_beta2
p + Li6 for JEFF-3.2

## Slide 4: GND: Overview
Stores evaluated and/or processed data
Multiple sets of processed data can be stored in a GND file simultaneously
GND defines a structure that is hierarchical
Talk more about styles later.
Talk more about cross section per each reaction later.

## Slide 5: FUDGE: Capabilities
FUDGE: For Updating Data and Generating Evaluations
Originally developed for LLNL’s ENDL format
  Read and write ENDL data
  Modifying, plot, check, etc.
  Process ENDL data into LLNL legacy files (deterministic and Monte Carlo)
Additionally, can now handle GND data
  Convert ENDF to and from GND, convert ENDL to GND
  Reading/writing
  Printing/plotting
  Modifying
  Converting units (e.g., eV to MeV)
  Processing
    Reconstruct cross sections and angular data from resonance parameters
    Heat cross sections
    Calculate cdfs for Monte Carlo transport
    Multi-group for deterministic and Monte Carlo transport
  Checking

## Slide 6: FUDGE: general comments
Top level written in python
  Has C/C++ interface for computationally intensive calculations
  Some legacy ENDL support in FORTRAN
  Some processing multi-threading (RR, MG but not heating)
Freely available at https://ndclx4.bnl.gov/gf/project/gnd/
For ENDF-VII.1 sub-libraries can translate:
    neutrons, protons, deuterons, tritons, helium3s, gammas, standards, electrons, photoat, thermal_scatt and atomic_relax
Translated and processed the ENDF/B-8_beta3 neutron library
Still have issues with some MAT’s in some libraries that do not follow the ENDF-6 standard

## Slide 7: FUDGE: Manipulating and plotting
Various operations on data types are supported
Including +, -, *, /, etc. on 1d data types
h(x) = f(x) × g(x)

## Slide 8: Current types of processing 1/3
Constructing pointwise cross sections from resonance parameters
Unit conversion: convertUnits( { 'eV' : 'MeV' } )
Average product data (energy and momentum unheated)
  Like kerma data but more general - per particle per reaction
Available energy and momentum by reaction

## Slide 9: Current types of processing 2/3
Heating cross section and average product data
  Equation written in terms of relative velocity and integrated over a Maxwellian target velocity
  E = incident particle energy, E’ = outgoing particle (product) energy
  Subscripts: ‘r’ = relative, ‘i’ = incident particle and ‘t’ is target particle)
Glossing over this!

## Slide 10: Current types of processing 3/3
For distributions calculating cdf from pdf: for Monte Carlo
Calculating multi-group data: for deterministic and Monte Carlo
  Cross section
  Average product data
  Average available energy and momentum
  Distributions (transfer, product, fission matrices)
  Etc.
Calculating upscattering multi-group matrix data for elastic scattering

## Slide 11: Fudge: GND processing script
Fudge/bin/processProtare.py (projectile + target + evaluation)
  Read in a GND file
  Convert energy units: LLNL uses MeV while GND from ENDF is in eV
  Reconstruct cross sections and/or angular data from resonance parameters if needed (threaded)
  Calculate average product energy and momentum data
    This can be used to calculate KERMA but is more general
  Preform Monte Carlo processing if requested (pdf to cdf)
  Loop over each temperature
    Heat cross section data
    Perform multi-group processing if requested (threaded)
  Write out to file: all data put into one GND file

## Slide 12: GND uses ‘styles’ to handle multiple types of data
Styles include evaluated, crossSectionReconstructed, heated, multiGroup, MC, etc.
  All styles except evaluated are derived from another style
  Each type of data (cross section, multiplicity, distribution, etc.) can contain more than one style.
    e.g. a cross section can contain ‘evaluated’, ‘crossSectionReconstructed’, and one or more ‘heated’-style data
recon
eval
heated_1
heated_2

## Slide 13: Processing for Monte Carlo
heated_002
apd
recon
eval
processProtare.py --energyUnit MeV –mc –t 1e-7 –t 1e-6 –t 1e-5 Li6.xml
heated_001
heated_000
MonteCarlo

## Slide 14: Processing for multi-group
heated_002
MultiGroup_002
apd
recon
eval
processProtare.py --energyUnit MeV –mg –t 1e-7 –t 1e-6 –t 1e-5 Li6.xml
heated_001
MultiGroup_001
heated_000
MultiGroup_000
MultiGroup

## Slide 15: FUDGE: Contents of a “styles” element

## Slide 16: FUDGE: Contents of a “crossSection” element

## Slide 17: FUDGE: Contents of a “outputChannel” element

## Slide 18: Testing processing with other codes

## Slide 19: FUDGE: future work
Unresolved resonance probability table generation
  This is being implemented by Dave Brown (BNL)
Multi-band
Thermal scattering generation
  We need to implement something like NJOY’s LEAPR and THERMR
  Have a definition in GND
Thermal upscatter for deterministic transport
  Only treats elastic scattering
  Have code to calculate these data, still need to hook into FUDGE
Kiwi: package that uses FUDGE to generate realizations of nuclear data from mean and covariance data.
Fix GND to ACE and maybe others
Documentation

## Slide 20: GIDI: overview
GIDI: General Interaction Data Interface
  Transport code API for GND
Written in C++
  Update from older version that was written in C
  Starting to test in an LLNL deterministic code
Uses the PoPs (Properties Of Particles) API and database
  Being developed at LLNL
  PoPS is part of SG38 standard
Testing in LLNL deterministic transport code Ardra
Old version used in LLNL Monte Carlo transport code Mercury
  New version to test in Mercury soon
  Old version also used in GEANT

## Slide 21: GIDI: Future work
PoPs: Property Of Particles – a particle database
  Updated to latest GND/PoPs
Deterministic
  Add energy deposition support
  Upscatter
  Far in the future?: on the fly processing like multi-grouping
Monte Carlo
  Convert C routines to C++
  Add energy deposition support
  Add multi-temperature support
  Add angle biasing
  Speed up sampling
    Significant work already completed by a summer student (Nick A.)
  Far in the future?: on the fly processing like heating

## Slide 22: Summary
GND
  I expect few changes and changes to be small
FUDGE
  Nearly updated to latest GND
  Freely available at https://ndclx4.bnl.gov/gf/project/gnd/
  Plan to release another version before 1 Jan. 2017 with multi-group processing
GIDI
  Changing to pure C++
  Multi-group for all temperatures complete by 1 Jan. 2017
  Multi-temperature and Monte Carlo (minus angle biasing) early 2017