## Slide 1
ALICE Data Format
J. Schambach, ORNL

## Slide 2: ALICE DAQ
Detectors
Fee
CRU
(readout
card)
Network
EOS
FLP
FLP
FLP
EPN
EPN
EPN
O2
CRU
(readout
card)
CRU
(readout
card)
8000 links connect the detectors to O2 farm. Total data rate > 3 TB/s
200 FLPs receive data from the detectors FEE. Total data rate ~100 GB/s
  500 readout cards.
250 EPN collect and store data on EOS. Total data rate 90 GB/s
3.4 TB/s data compression 90 GB/s
CRU Common Readout Unit
FLP First Level Processors
EPN Event Processing Nodes
EOS EOS Open Storage
data processing
data
data
data processing
data
data processing
data
readout card (~DAM)
FLP (~EBDC)
EPN

## Slide 3: LHC “Versatile Link” Architecture
CDR: Clock and Data Recovery
DEC: Decoder
DSCR: De-Scrambler
SCR: Scrambler
ENC: Encoder (with Forward Error Correction, FEC)
SER: Serializer
Off-Detector GBT_FPGA: https://gitlab.cern.ch/gbt-fpga
GBTx ASIC
40, 20, or 10 E-Links

## Slide 4: GBT Data Format
The 120-bit “GBT Frame format” is transmitted during a single LHC bunch crossing interval (25 ns), resulting in a line rate of 4.8 Gb/s (120 bit * 40 MHz)
The DATA field is 80 bit => 3.2 Gb/s
The “Wide Bus” DATA field is 112 bit (no FEC) => 4.48 Gb/s
  These 2 are the data rates of the GBT we use in ALICE
EC field provides an additional 2bits (80 Mbps) for “Detector Control”, IC field (2 bits, 80 Mbps) for internal GBTx configuration
Header field (H) provides the alignment for the (DC balanced) frame alignment: either “0110” (“Control”) or “0101” (“Data”)
lpGBT:
Downlink – 64bit Frame (32bit Data, 24bit FEC, 4bit Header, 2bit IC, 2bit EC); data rate 2.56 Gbps
Uplink – either 128bit (5.12 Gbps) or 256bit (10.24 Gbps) frames
  FEC5 (10/20 bits) or FEC12 (24/48bits)
  Data field for 5.12 Gbps: 112bits (FEC5) or 96bits (FEC12)
  Data field for 10.24 Gbps: 224bits (FEC5) or 192bits (FEC12)

## Slide 5: Heartbeat Frame Concept in ALICE Streaming Readout
LHC clock 40 MHz
3564 Bunch Crossing in 1 ORBIT
ORBIT rate ~10 KHz

## Slide 6: Different FEE – Same Data Format
H
B
#0
H
B
#1
H
B
#2
H
B
#3
H
B
#4
H
B
#0
H
B
#1
H
B
#2
H
B
#3
H
B
#4
H
B
#0
H
B
#1
H
B
#2
H
B
#3
H
B
#4
H
B
#0
H
B
#1
H
B
#2
H
B
#3
H
B
#4
streaming
packet
FEE
FEE
FLP
FLP
H
B
#0
H
B
#1
H
B
#2
P
H
Y
P
H
Y
P
H
Y
P
H
Y
P
H
Y
P
H
Y
H
B
#127
H
B
#128
TF
Time Frame = 128 Orbits

## Slide 7: CRU Continuous Mode
RDH HEADER
HB#0 START
HB FRAME
RDH HEADER
HB#1 START
HB#0 END
HB#0
TRG#0
RDH HEADER
PAYLOAD DATA
RDH HEADER
PAYLOAD DATA
“Raw Data Header” (RDH)
Can contain additional hit timing information

## Slide 8: ALICE GBT Protocol
Bits | Description
HEADER | = CONTROL
[79:76] | Control Code
[75:0] | Control Code Parameters (optional, dependent on specific control data word)
Bits | Name | Description
HEADER | CONTROL | 
[79:76] | Control Code | IDLE = 4’b0000
[75:0] |  | Reserved (must be 0)
Bits | Name | Description
HEADER | CONTROL | 
[79:76] | Control Code | SOP = 4’b0001; Start Of Packet
[75:60] | Length | Length of the packet (in bytes); optional (not used; = 0)
[59:44] | TTS Busy | Busy Information bits; optional (not used; = 0)
[43:0] |  | Reserved (must be 0)
Bits | Name | Description
HEADER | CONTROL | = 0
[79:76] | Control Code | EOP = 4’b0010; End Of Packet
[75:60] | Length | Length of the packet (in GBT Words); optional (not used; = 0)
[59:28] | Checksum | Checksum of packet; optional (not used; =0)
[27:27] | End Flag | End of packet flag (1 = Yes, 0 = No); optional (not used; =0)
[26:0] |  | Reserved (must be 0)
Bits | Name | Description
HEADER | CONTROL | = 0
[79:76] | Control Code | SWT = 4’b0011; Single Word Transaction
[75:0] | Parameters | Detector specific parameters
IDLE
START-OF-PACKET
END-OF-PACKET
SINGLE-WORD-TRANSACTION

## Slide 9: ALICE Basic Data Flow (Example ITS)

## Slide 10: ALICE Timing and Trigger Distribution
GBT Bit | Content
<31:0> | Trigger Type
<43:32> | Bunch Crossing ID
<47:44> | Spare
<79:48> | ORBIT
GBT Trigger Word
Trigger Type Bits
CTP: Central Trigger Processor
LTU: Local Trigger Unit
CRU: Common Readout Unit

## Slide 11: Data Throttling (“Heart Beat reject”)

## Slide 12: PON for Trigger/Timing

## Slide 13: PON Basics

## Slide 14: CERN TTC-PON for Trigger and Timing distribution
Local Trigger Unit
Read Out Unit
Central Trigger
Unit
PON (Passive Optical Networks)
  FTTH worldwide access Network
  Point-to-Multipoint
  High bandwidth
  Bidirectional
    Downstream (OLT → ONUs)
    Upstream (ONUs → OLT)
  XG-PON technology (SFP+ PON transceivers)
  Custom protocol
CERN common-project
  Target: phase-1/2 upgrades
  Ready for ALICE phase-1 upgrade
  LHCb is planning to use the harware
OLT: Optical Line Terminal / ONU: Optical Network Unit
OLT
ONU
ONU
…
GBT FPGA
GBTx
GBTx
FE
FE
FE
FE
GBTx
FE
FE
FE
FE
…
ONU
detectors
off-detector

## Slide 15: Downstream Path
OLT → ONUs (broadcast)
9.6Gb/s line-rate (1577nm)
Low and fixed latency
FEC (forward error correction)
  2x BCH(120,106) – double random error correcting code
SC (slow control)
  System control/monitoring (CRC-7 protected)
High User Bandwidth (200b per BC – 8Gb/s)
HDR
8b
SC
4b
USER PAYLOAD
200b
FEC
28b
BC period (25ns)

## Slide 16: Upstream Path
ONUs → OLT (TDMA)
2.4Gb/s line-rate (1270nm)
Synchronized to downstream
8b10b encoded
Total burst length: 125ns (100ns burst + 25ns gap)
Waiting time: 125ns x Number ONUs (8us for 64 ONUs)
User bandwidth: 448Mb/s x (1 / Number ONUs)
HDR
8b
ADDR 8b
USER PAYLOAD
56b
SC
8b
ONU1
ONU2
preamble
58.3ns
140b
Total: 80b (100b with 8b10b)
data
41.7ns
100b
gap
25.0ns
60b

## Slide 17: Test Setup Concept
Software (system manager)
  PC (Python) or soft/hard processor
  Full system control and monitoring from OLT
Firmware
  OLT core: Kintex Ultrascale
  ONU core: Kintex7, Kintex Ultrascale, Arria10
  Example design
Hardware
  Various FPGA evaluation boards + TTC-PON FMC
  SFP+ PON components
Support
OLT
FPGA
…
ONU
FPGA
1:N
ONU
FPGA
ONU
FPGA
KCU105 board
KCU105 board
KC705 board
A10 GX board

## Slide 18: Jitter
Integrated jitter (10Hz – 10MHz, random, rms)
Reference: 0.967ps rms
End Point Recovered Clock: 1.614ps rms

## Slide 19: TTC-PON Project at CERN
https://espace.cern.ch/Project-TTC-PON
https://espace.cern.ch/HighPrecisionTiming
[1] S. Baron and E. Mendes, Recent Developments in the TTC-PON system, talk given at the EP-ESE Electronics Seminars, CERN, Geneva 23, Switzerland, 31 May 2016 https://indico.cern.ch/event/465344/
[2] E. Mendes et al., 2017 The 10G TTC-PON system: challenges, solutions and performance, E. Mendes et al., JINST 12 C02041
Node | VCC | I max | Cost
ONU | 3.3 V | ~ 450 mA | ~ 110 USD
OLT | 3.3 V | ~ 750 mA | ~ 670 USD
Splitter 1:64 | N/A | N/A | ~ 500 USD
Node | Logic resources
ONU Kintex 7 | ~2.5k Slice LUTs
ONU Kintex Ultrascale | ~2.4k CLB LUTs
ONU Arria10 | ~ 1.8k ALMs
OLT Kintex Ultrascale | ~ 3.0k CLB LUTs
Optical Components
FPGA Resources