## Slide 1: Streaming Workshop: ePIC/Protocols/Interface/Timing/Clock Distribution
Fernando Barbosa (JLab), L3 CAM Electronics
December 9, 2022

## Slide 2: Outline
Requirements and Design Philosophy
Streaming Readout Architecture
Readout Chain
Channels
eRD109 ASIC/Electronics
Timeline
Summary

## Slide 3: Requirements and Design Philosophy
Front-End Boards custom designed for each detector, populated with ASICs/COTS, operate in large magnetic fields.
ASICs/COTS process analog signals and digitization tailored to each type of detector technology, data reduction (e.g., zero suppression) desirable.
Maximize synergies in electronics and minimize cabling.
Electronics, including digitizers, close to the detector as much as possible and where applicable.
Prefer to limit FPGA use inside detector volume.
Serviceability as a design criteria.
Triggerless operation of the electronics as default; triggered operation for calibration, test, de-bugging.
Meet current US standards per NEC, UL, FCC, NEMA:
Equipment assessment reviews for conformance to EHS&Q.
Radiation levels at EIC are much lower than at LHC by O(100). EIC detector radiation map has been updated and will guide formulation of electronics requirements for radiation hardness/ tolerance.

## Slide 4: EIC Streaming Readout Architecture
Data
Configuration & Control
Power
Detector
FEB
(Front End Board)
RDO
(Readout Board)
DAM + Computing (Data Aggregation Module)
Storage
ASIC
FPGA
Power Supply System
(HV, LV, Bias)
Cooling Systems
Fiber
LVDS ~ 20-30 m*
Analog ~ 20m
Fiber
L ~ 100 m
fiber
Monitoring
BW: O(100 Tbps)
BW: O(10 Tbps)
Goal: O(100 Gbps)
FEB
FEB
RDO
Switch / Server / Link-Exchange: Readout
Switch / Server: Processing
Switch / Server: Buffer
Total
w/ Jin and Kai
Bunch Crossing ~ 10.2 ns/98.5 MHz
Event Rate ~ 2 us/500 kHz
Low occupancy.
Jitter ~ 5 ps
Front-End Electronics
DAQ
GTU
(Global Timing Unit)
*LVDS – ANSI/TIA/EIA-644A standard. Maximum cable length dependent on data rate.

## Slide 5: EIC Readout Chain
Name
Design
Function
Attributes
Adapter
Detector Specific
-HV/Bias Distribution
-HV divider
-Interconnect Routing
-Sensor Specific
-Passive
Sensor
Detector Specific
-Multi-Channel Sensor
-MAPS
-AC-LGAD
-MPGD
-MCP-PMT
-SiPM
-LAPPD
Front End Board
(FEB)
Detector Specific
-Amplification
-Shaping
-Digitization
-Zero Suppression
-Bias Control & Monitoring
-ASIC/ADC
-Discrete
-Serial Link
Readout Board
(RDO)
Few Variants
-Communication
-Aggregation
-Formatting
-Data Readout
-Config & Control
-Clock & Timing
-FPGA
-Fiber Link
Data Aggregation Module (DAM)
Common
-Computing Interface
-Aggregation
-Software Trigger
-Config & Control
-Clock & Timing
-Large FPGA
-PCIe
-Ethernet
Computing
Common
-Data Buffering and Sinking
-Calibration Support
-QA/Scalers
-Collider Feedback
-Event ID/Building
-Software Trigger
-Monitoring
-COTS
-Ethernet
Global Timing Unit (GTU)
-Interfaces to Collider, Run Control & DAM
-Config & Control
-Clock & Timing
On Detector
SMT BGA

## Slide 6: ePIC Detector Channels
Detector System | Channels | Nominal Readout Technology
Si Tracking: 3 vertex layers, 3 sagitta layers, 4 backward disks, 5 forward disks | 7 m^2 32 B pixels 5,200 MAPS sensors | MAPS
MPGD tracking: 3 layers | 100k | Strips
Calorimeters: Forward: LFHCAL pECAL HCAL inset Barrel: HCAL ECAL Imaging, if used Backward: ECAL | 60k 25k 8k 3k (25k?) 8k 50M pixels 25k | SiPM
Far Forward: B0: 3 MAPS layers 1 or 2 AC-LGAD layer 2 Roman Pots 2 Off Momentum ZDC: Crystal Calorimeter 32 Silicon pad layer 4 silicon pixel layers 2 boxes scintillator | 3x20cmx20cm (300M pixel) 300k or 600k 1M (4 x 135k layers each) 650k (4 x 80k layers each) 400 11520 160k 72 | MAPS AC-LGAG AC-LGAD AC-LGAD APD HGCROC
Far Backward: Low Q Tagger 1 Low Q Tagger 2 2 Calorimeters | 1.3M 480k 700 | AC-LGAD AC-LGAD
PID-TOF | 3M-50M | AC-LGAD
PID-Cherenkov: dRICH pfRICH (if selected) mRICH (if selected) DIRC | 300k 225k 74k | SiPM SiPM SiPM
The five (5) eRD109 proposals to be considered, cover most of the EIC readout requirements.
And may extend to others.
Note: Some of these entries have not been updated to the current number of sensors.

## Slide 7: Readout Channels & eRD109 proposals
Detector Group | Channels | AC-LGAD | SiPM/PMT | MPGD
 | MAPS | AC/DC-LGAD | SiPM/PMT | MPGD
Tracking | 32 B |  |  | 100k
Calorimeters | 50M |  | 150k | 
Far Forward | 300M | 2.3M | 500 | 
Far Backward |  | 1.8M | 700 | 
PID |  | 3M-50M | 600k | 
TOTAL | 32 B | 7.1M-54M | 750k | 100k
ASIC | ITS-3 | EICROC | Discrete/COTS HGCROC3 ALCOR-EIC | SALSA
These ASICs are leading candidates for the EIC. The large number of channels, density, granularity and geometry favor high circuit density solutions.
We continue to assess ASIC developments from other sources such as NALU, Pacific Microchip, Alphacore, SenseICs, Weeroc.
Some sub-detectors, with less restrictive requirements, may benefit from discrete implementations and developments such as from STAR and sPHENIX.
Note: Some of these entries have not been updated to the current number of sensors.

## Slide 8: Readout Channels Updates
Allows for a proper estimate of input characteristics (capacitance, dark noise, etc.) and PCB layout and size.
Allows for proper cost estimates in P6 (i.e., Project) and scaling.
ePIC |  |  |  | 
Detector System | Nominal Readout Technology | # Sensors | Grouping | # Readout Channels
Calorimeters: | SiPM |  |  | 
Forward: LFHCAL | 3x3 mm | 63280 | 2::1 | 31640
pECAL | 6x6 mm | 76000 | 4::1 | 19000
Barrel: HCAL | 3x3 mm | 7680 | 5::1 | 1536
ECAL | 3x3 mm | 130560 | 16::1 | 8160
Backward: ECAL | 3x3 mm | 52000 | 16::1 | 3256
nHCAL | 3x3 mm | 16200 | 5::1 | 3240
 |  |  | TOTAL | 66832
An example of recently updated information – Calorimeters (in P6):
# Calorimeter Digitizer Channels

## Slide 9
Five (5) proposals were received and originated from various EIC sub-detector groups. These cover the R&D efforts for ASICs and Electronics in support of the EIC detector readout:
Proposal | File | Authors | Sub-Detector | Sensor Type | Readout Solution
A | eRD109_pECAL_readout_prototype_FINAL | G. Visser (IU), et al. | Calorimeter | SiPM | Discrete, COTS, ASIC
B | eRD109CalorimeterReadout | N. Novitzky (ORNL), et al. | Calorimeter | SiPM | ASIC (HGCROCv3)
C | eRD109-alcor | M. Ruspa (INFN), et al. | dRICH | SiPM | ASIC (ALCOR)
D | ACLGAD_ASIC_Electronics_FY23 | Z. Ye (UIC), et al. | Central, Far-Forward | AC-LGAD | ASIC (EICROC1, FCFD1) (2)
E | eRD109_SALSA_proposal_vfinal1 | D. Neyret (CEA), et al. | Micromegas, GEM, MicroRWell | MPGD | ASIC (SALSA)
eRD109 ASIC/Electronics
R&D initiatives to develop front end readout solutions for EIC.

## Slide 10: Proposal A – Calorimeters, SiPMs – Discrete/COTS/ASIC
Develop a simple, high resolution waveform readout solution for the calorimeters with SiPMs by:
  Employing discrete, COTS devices.
  Developing PCBs for full readout chain.
  Developing cabling, power, cooling infrastructure.
  Making it adaptable to implementations that may benefit from the availability of ASICs.
Adapter PCBs
FEB PCBs
Based on STAR FCS.
eRD109 ASIC/Electronics
R&D initiatives to develop front end readout solutions for EIC.

## Slide 11: Proposal B – Calorimeters, SiPMs – HGCROCv3
Develop a readout solution for the calorimeters with SiPMs by:
  Employing existing HGCROCv3 ASIC
  Developing PCBs for full readout chain
  Developing cabling infrastructure
Adapter PCBs
FEB PCBs
RDO PCBs

## Slide 12
SiPM version.
Large dynamic range.
Low noise.
Charge: ADC+TOT.
Time: TOA (25 ps).
512 DRAM buffer.
2x 1.28 Gbps links.
I2C controls.
40 MHz operation.
20 mW/Ch.
Radiation tolerant.
Developed for CMS.

## Slide 13: Proposal C – dRICH, SiPMs – ALCOR
64-Ch, 110/65 nm CMOS, SiPM readout.
Dual polarity, RCG Amplification, conditioning, digitization.
Modes of operation: single-photon tagging or time and charge.
Triggerless and triggered operation.
25 ps TDCs, 5 MHz input.
4 or 8x 640 Mbps LVDS links.
SPI configuration.
Develop a readout solution specific to the dRICH with SiPMs by:
  Qualifying existing ALCOR v2 ASIC.
  Further development and refinements towards final ALCOR v3.
Originally developed by INFN for DARKSIDE.

## Slide 14: Proposal D – AC-LGAD (Low Gain Avalanche Diode) – EICROC
Collaboration by OMEGA/IJCLab/CEA-Irfu/AGH
Develop a readout solution for AC-LGADs by considering three (3) options:
  Develop the EICROC2 based on existing EICROC0 (4x4 pads):
  EICROC1 (8x4 or 16x4 pads): 2023
  EICROC2 (32x16 or 32x32 pads): 2024 - 2025
Preamp, discriminator – ATLAS ALTIROC.
I2C slow controls – CMS HGCROC.
TOA TDC – CEA-Irfu.
ADC (8b) – AGH Krakow and IJCLab (EICROC1, EICROC2).
Readout FIFO depth 8 (200 ns).
Jitter: 15-20 ps.
Power: 1-2 mW/Ch.
4x4 500 um pixels
One pixel – EICROC0
One pixel

## Slide 15: Proposal D – AC-LGAD (Low Gain Avalanche Diode) – FCFD (Fermilab CFD), …
  2. Develop the FCFDv2 based on existing FCFDv0:
  FCFDv1: 2023
  FCFCv2: 2024 - 2025
TSMC 65 nm.
Timing precision: ~30 ps @ 5 fC; <10 ps @ 30 fC.
  3. Investigate third-party ASIC solutions, e.g.:
  HPSoC – NALU.
  ASROC – Anadyne.
  FAST – INFN.
  …

## Slide 16: Proposal E – MPGD (Micro-Patterned Gaseous Detectors) – SALSA
64-Ch, updated design from SAMPA V5, migrating to 65 nm CMOS.
Peaking time: 50 – 500 ns
Inputs: Cin optimized for 200 pF; Rates: >25 kHz/Ch (~100’s kHz); Dual polarity.
ADC: 12 bits, 5 – 50 MSPS.
Extensive data processing capabilities.
Triggerless and triggered operation.
Power: 15 mW/Ch
Several 1 Gbps links.
I2C configuration.
SALSA prototype submission – late 2022 ( a few channels).
Collaboration of Irfu CEA Saclay and U. of São Paulo.
Develop a readout solution for MPGDs, based on previous ASICs:
  SALSA1: 2023
  SALSA2: 2024
  SALSA (pre-production): 2025

## Slide 17: Timeline
Bulk of Construction & Installation phase for Electronics: April 2025 – January 2030.
Installation of some items may be extended to April 2031.
Construction and Installation includes procurements and deliveries and are initiated at different times of this phase.
R&D until 4/2025.
(Most~1.5 Years)
Design until 9/2027.
(Most~2 Years)
4/2025 to 4/2031.
(~6 Years)

## Slide 18: Timeline (cont.)
DOE OPA Status Review: January 31-February 2, 2023 (Primavera P6 towards final version).
CD-2 – Baseline: Review October 2024/ Approval January 2025
CD-3 – Construction Phase: Review TBD/ April 2025 – April 2031
Resource loaded schedules were earlier developed for the Reference Detector (CD-1) and then for the ECCE selected proposal.
ePIC presently follows the ECCE proposed schedule.
Resource loaded schedules have just been submitted for updates to the Primavera P6.
These will be transitioned over the next 6 months to the final ePIC schedule towards CD-2.
Summary Gantt chart for Electronics WBS 10.06.08 (internal tasks not shown for simplicity)

## Slide 19: Summary
A very active technical review schedule:
  Electronics&DAQ – August 2022
  eRD109 DAC – October 2022
  Calorimeters – December 2022
  More to come.
Start funding eRD109 activities ASAP.
Need to finalize detector sensor and readout channel count, normalize nomenclature, finalize specifications.
Transition resource-loaded schedules to final ePIC P6 by June 2023.