## Slide 1: Short summary of RHIC Run-16 and outlook for for Run-17/18 and BES-II Wolfram Fischer
16 June 2016
BNL NPP PAC
Notes: 09:00, 30 min total => 25 slides

## Slide 2: Run-16 – most demanding in terms of flexibility to date
6 setups for physics, d+Au with Au cooling except at lowest energy (new aperture limit at Coherent electron Cooling test, sensitive to losses)

## Slide 3: Au+Au at √sNN = 200 GeV – record luminosities
Lavg = 44x design (plans for 2x more)
replacement of shorted quench protection diode (19.5 days)
losses of secondary
BFPP/EMD beams (~ L) contributed

## Slide 4: Coherent electron Cooling test V. Litvinenko, I. Pinayev et al.
Novel cooling scheme for eRHIC
2016 first year with beam transported from SRF gun to dump, acceleration in newly installed 704 MHz SRF cavity
had demonstrated 3 nC/bunch in 2015, record for CW guns
Still to be demonstrated (next 2 years):
full electron beam parameters (energy, bunch charge, rep rate, emittances)
interaction with Au beam, amplification of density modulations
cooling
Undulator is aperture limit for BES-II (needs to be removed)

## Slide 5: Run-17: ph+ph √s = 510 GeV – luminosity leveled at 1.6x1033 cm-2s-1
Calculation with multiple b* squeezes (expect only one in Run-17) – Y. Luo
Goal: L within ±10% of target
Luminosity [1032 cm-2s-1]

## Slide 6: Run-18 Possible isobar combinations
 | 96Zr40+ | 96Ru44+
Natural abundance | 2.81% | 5.54%
... from EBIS | enriched 96Zr metal available | no source of enriched 96Ru
... from Tandem | good intensity with ZrH2 | good intensity with Ru metal
 | 124Sn50+ | 124Xe54+
Natural abundance | 5.79% | 0.095%
... from EBIS | possible | possible
... from Tandem | possible | not possible
 | 130Te52+ | 130Ba56+
Natural abundance | 34.08% | 0.11%
... from EBIS |  | difficult
... from Tandem | good intensity with CdTe | perhaps with enriched Ba in BaH2
 | 136Xe54+ | 136Ce58+
Natural abundance | 8.86% | 0.185%
... from EBIS |  | 
... from Tandem | no possible | not possible, poisons ionizer
Notes: Checked abundance (mole fraction) for all isotopes (Wikipedia).

## Slide 7: Run-18: 96Zr + 96Zr, 96Ru + 96Ru – luminosity estimates
estimate from last year (likely too conservative)
based on 2016 test, natural Ru, from Tandem

## Slide 8: Other requests
RHICf (Run-17)
  discussed with RHICf, request reasonable (both colliding and fixed target part)
  largest uncertainty is measurement and adjustment of radial polarization in time (can tolerate large error)
Au+Au sNN = 62.4 GeV (Run-17)
Au+Au sNN = 27 GeV (Run-18)
  no issues
RHICf

## Slide 9: LEReC Physics integration BES-II required events
General strategy to maximize integrated luminosity:
Cooling at the 3 lowest energies (4x gain in Lavg), no cooling at the 2 highest energies (3x gain in Lavg) => demonstrated at √sNN = 19.6 GeV in Run-16
Increase cryo-time from 22 to 24 weeks/year
Start BES-II at highest energies (machine ready w/o cooling)
Interleave cooling commissioning with physics operation
Finish BES-II at lowest energies (largest gain in Lavg and time)
RHIC Beam Energy Scan II (BES-II) for search of critical point in QCD phase diagram
center-of-mass energy √sNN | GeV | 7.7 | 9.1 | 11.5 | 14.6 | 19.6
events BES-I, actual | M | 4.3 |  | 11.7 | 24 | 36
events BES-II, min goal | M | 80 | 100 | 150 | 200 | 300
events BES-II, full goal | M | 100 | 160 | 230 | 300 | 400
Notes: STAR vertex acceptance: +- 1m
STAR contacts: Zhangbu Xu (spokesperson), Bill Christie, Paul Soerensen, Daniel Cebra

## Slide 10: Physics integration BES-I and BES-II luminosities
4x increase in Lavg with e-cooling
3x increase in Lavg without e-cooling
nominal injection energy

## Slide 11
COOLING
in Blue RHIC ring
COOLING
in Yellow RHIC ring
64 m to IP2
Beam Dump
20° Bending Magnets
DC e- Gun
704 SRF
Booster Cavity
2.1 GHz Cu Cavity
9 MHz Cu Cavity
704 MHz Cu Cavity
Commissioning
Diagnostic Line 1
Commissioning
Diagnostic Line 2
RHIC TRIPLET
RHIC DX
180° Bending Magnet
e-
e-
LEReC Solenoids
Compensating (LF)
Matching (HF)
Merger/Transport
e-
Low Energy RHIC electron Cooling (LEReC)
(not to scale)
Energies E : 1.6, 2.0 (2.65) MeV Avg. current Iavg : 27 mA Momentum dp/p : 5×10-4
Luminosity gain : 4×
A. Fedotov
1st bunched beam electron cooler planned operation in 2019/2020

## Slide 13: 56 MHz SRF +11% total luminosity gain
Notes: Fillno 19941

## Slide 14: 56 MHz SRF +15% luminosity gain in +- 10 cm
Notes: Fillno 19941

## Slide 15: Run-17 ph+ph at √s = 510 GeV (STAR)
STAR requested level luminosity at 1.3×1032 cm-2s-1
(0.9 events per bunch-bunch crossing, ≈ 50% of Run-13 max, ≈ 30% of Run-17 expected max)
Possible methods for leveling: Dynamic b* change during store (tested in Run-14) Changing transverse offset with electron lens (needs study)
New operating mode, plan for Lavg ≈ 90% Lpeak
Need Run-17 also for high-luminosity test for sPHENIX era
Run-17 leveled luminosity request
Run-13 luminosity (17491)

## Slide 16: Ru+Ru and Zr+Zr Run-17 at √sNN = 200 GeV (STAR)
Full intensity = Ru, Zr charge per bunch ≥ Au charge per bunch
Need enriched source material for laser ion source or hollow cathode source Ru-96 abundance 5.6%, Zr-96 abundance 2.8%
Enriched Zr-96 available in metallic form => can run at full intensity
Enriched Ru-96 not available from any source (still searching ...) Need ≈ 1 g for operation Have 40 mg in hand (97.92% enriched) 400 mg target material at GSI => can likely run at 5% of full intensity tested in Run-16
ruthenium grown out of gas phase (Wikipedia)
zirconium (Wikipedia)
Notes: Calutron picture, Ru picture, Zr picture