## Slide 1: ePIC Calorimetry WG
erhtjhtyhy
Paul E Reimer
Newport News, VA
10 January 2023
Thanks to Calo WG, Conveners and esp. Alexander Kiselev, Alexander Baxilevsky and Elke C Aschenauer whose slides I’ve borrowed
This work was partially supported under grant DE-AC02-06CH11357 from the US Department of Energy, Office of Nuclear Physics

## Slide 2: Calorimetry
Why do we need what we need where it is?
Electromagnetic calorimeter → Measure photons (E, angle), identify electrons
  PbWO4 Crystals (backward), W/SciFi Spacal (forward)
  Barrel: Pb/SciFi+imaging part or new Scintillating glass
Hadron calorimeter → Measure charged hadrons, neutrons and KL0
  challenge achieve ~50%/√E + 10% for low E hadrons (<E> ~ 20 GeV)
  Fe/Sc sandwich with longitudinal segmentation
Θ = 2o
Θ = 45o
Θ = 90o
Θ = 135o
Θ = 178o
z
high x
medium x
low x
hadrons
hadrons
low Q2
high Q2
electron beam
p/A beam
Central
Detector
Hadron
Endcap
Lepton
Endcap
scattered
lepton
and all the detectors integrated in the IR along the beam line

## Slide 3: E&M Calorimetry
Electron/photon PID, energy, angle/position:
Coverage (in rapidity and energy), resolution, e/𝜋, granularity, projectivity
PYTHIA
18 x 275 GeV
DIS e
MILOU DVCS
e+p 18×275 GeV
DVCS photons
SIDIS π0
PYTHIA
18 x 275 GeV
h-endcap
e-endcap
Barrel

## Slide 4: E&M Calorimetry
Electron/photon PID, energy, angle/position:
Coverage (in rapidity and energy), resolution, e/𝜋, granularity, projectivity
PYTHIA
18 x 275 GeV
DIS e
MILOU DVCS
e+p 18×275 GeV
DVCS photons
SIDIS π0
PYTHIA
18 x 275 GeV
h-endcap
e-endcap
Barrel

## Slide 5
 | 𝜎E/E | E range, GeV | 𝜋± suppression (w/other subsystems) | 𝜋0/𝜸 discr.
e-endcap |  | 0.05−18 GeV | Up to 104 | Up to 7 GeV/c
Barrel |  | 0.05−50 GeV | Up to 104 | Up to 10 GeV/c
h-endcap |  | 0.1−100 GeV | Up to 104 | Up to 50 GeV/c
 | 𝜎E/E | E range, GeV | 𝜋± suppression (w/other subsystems) | 𝜋0/𝜸 discr.
e-endcap |  | 0.05−18 GeV | Up to 104 | Up to 7 GeV/c
Barrel |  | 0.05−50 GeV | Up to 104 | Up to 10 GeV/c
h-endcap |  | 0.1−100 GeV | Up to 104 | Up to 50 GeV/c
As documented in YR and
“General, Functional, and Performance Requirements for the EIC Detector Systems”
Continuous acceptance (particularly from e-endcap to barrel)
Minimal material budget on the way from the vertex (particularly for e-endcap to barrel)
Photosensors and FEE tolerate magnetic field
Operate at full luminosity and expected background conditions (rad. dose, neutron flux)
E&M Calorimetry

## Slide 6: e-endcap: PbWO4
Well established technology
Compact & High granularity: 2 2 20 cm3
High resolution:
Excellent e/𝜋 capabilities: 𝜋 suppres. a few 103
Radiation hard: >1000 krad
Temperature sensitive: d(LightYield)/dT = -(2-3)%/℃
Jlab-PrimEx eta/NPS PWO EMCal prototype
Consortium with >10 institutions
Extensive experience from recent PANDA (GSI) and CMS (CERN)
NIM A 1013 (2021), 165683

## Slide 7: h-endcap: W/SciFi
Established technology: sPHENIX barrel EMCal
Compact: X0 = 0.7cm
High granularity: Rm = 2cm
Sampling Fraction: 2-3%
Modest Resolution:
BNL-sPHENIX: W/SciFi
R&D:
  Improve light collection eff. and uniformity

## Slide 8: Barrel: Two Options
Complementary options for BECAL:
SciGlass or Imaging Calorimeter
Discussion in the following two talks by Joshua Crafts (CUA) and by Maria Zurek (ANL)

## Slide 9: Hadronic Calorimetry
soft, low multiplicity jets
low energy hadrons
(except for the very forward region)
Energy resolution driven by particle flow reconstruction
Granularity driven by neutral cluster isolation and jet substructure measurements

## Slide 10: Hadronic Calorimetry
Yields vs momentum for a 20 x 250 GeV configuration, -4 < h < 4
 | Ideal | Acceptable
 | Ideal | Acceptable

## Slide 11: Backward Hadronic Calorimeter
Talk by Leszek
STAR EEMC
Recycle scintillating plates from STAR
Embedded WLS fibers
SiPM readout
Replace lead absorber by steel
Full depth ~440mm only
It is indeed a tail catcher
High energy resolution is not needed
Acceptance -4 < h < -1
Fe/Sc sandwich , ~2.0 lI

## Slide 12: Barrel Hadronic Calorimeter
Partly reuse sPHENIX barrel calorimeter
Replace SiPMs
Upgrade electronics
Moderate energy resolution suffices
Acceptance -1 < h < 1
Fe/Sc sandwich, ~3.5 lI

## Slide 13: Forward Hadronic Calorimeter
New innovative design
High 3D granularity
High energy resolution
Acceptance 1 < h < 4
Fe/Sc + W/Sc sandwich , ~6.9 lI

## Slide 14: Forward Hcal Insert
Measure low angle high particles
See final talk by Miguel Arratia in this session

## Slide 15: EPIC Calorimetry
Backwards EMCal
PbW04 crystals
Complementary options for BECAL:
SciGlass or Imaging Calorimeter
PbSc Layer
Barrel HCAL (sPHENIX re-use)
Backwards HCal
Steel/Sc Sandwich
tail catcher
High granularity W/SciFi EMCal
Longitudinally separated HCAL with high-h insert
Imaging Layer
slide from E.C. Aschenauer

## Slide 16
Θ = 2o
Θ = 45o
Θ = 90o
Θ = 135o
Θ = 178o
z
high x
medium x
low x
hadrons
hadrons
low Q2
high Q2
electron beam
p/A beam
Central
Detector
Hadron
Endcap
Lepton
Endcap
scattered
lepton
and all the detectors integrated in the IR along the beam line