## Slide 1
Considerations on EIC LAS Design for ePIC SVT Configuration v0.0
21/11/2022
Notes: The abstract pattern can be removed or repositioned if required. Be careful to ‘Send to Back’ so that it does not obscure any important information.

## Slide 2
Background
EPIC - SVT
  Building on two talks from last time
    https://indico.bnl.gov/event/17713/contributions/70439/attachments/44360/74847/20221107-ePIC-SVT-cfg-v0.0.pdf (Laura)
    https://indico.bnl.gov/event/17713/contributions/70440/attachments/44407/74938/Apadula_EICSC_11_7_22.pdf (Nicky)
  Current design misses engineering detail
  Need to think about this, and about unanswered questions…

## Slide 3
Engineering Issues - Electronics
Stitching
  ITS3 plans long, thin sensors of a single length
  Suitable for vertex layers…
  …however, current disc plans envision many lengths
  Will this be possible?
https://indico.cern.ch/event/1127562/contributions/4904520/attachments/2511611/4318769/20220921.PL.MOSS.TWEPP2022.pdf
ITS3 Plan

## Slide 4
Engineering Issues - Electronics

?
?
Stitching
  What adjustments to the stitching plan are possible?
  Are multiple layouts per wafer possible, or one type per wafer?
  Implications for yield, cost, number of wafers…

## Slide 5
Engineering Issues - Electronics
Powering
  How will power reach the various layers?
  Vertex
    Powered from one side
    Issues around 90 degree bend explored in Nicky’s talk from last week
  Staves
    Current plan for longest barrel layer is 4 sensors of 1x7 reticules
    How to power? PCB? Copper Lines? Effect on material budget?

## Slide 6
Engineering Issues - Electronics
Powering
  Staves
    Longest barrel layer is 3x longest possible sensor
    How to power? PCB? Copper lines? Effect on material budget?
    Yield issues with using long (1x7) sensors? But additional material issues with using smaller ones? Acceptable trade-off?

## Slide 7
Engineering Issues - Electronics
Powering
  Discs
    Similar issues
    Perhaps less severe, due to distance from interaction point, but needs physics simulation

## Slide 8
Engineering Issues - Electronics
Cable Mass Reduction vs. Design Effort
  Using ITS3 as is for the staves and discs (even with stitching plan changes) leads to the cabling level outlined in the prior slides
  Is this acceptable from a physics point of view?
  Reduction would require
    Stand-alone or integrated DC-DC or serial powering blocks
    Suitable design database access
Option | Mass | Timeline | Notes
Do nothing – cabling only | Highest | N/A – do nothing | 
Stand-alone DC-DC/serial powering | Medium | Use existing - ?? 180nm development – Q1 2024 | 
Integrated DC-DC/serial powering | Lowest | Standalone – Q1 2024 Integrated – Q1 2025 | Database access critical

## Slide 9
Engineering Issues - Electronics
Miscellaneous
  What level of access will be possible?
  Current modelling assumes only silicon in the active area, but this is not the case…
  Effect of sensor peripheries?
Data Handling
  Note that power cabling issues apply equally to data cabling.
  Possibly harder, since cannot be combined.
  Data aggregation needed for staves?

## Slide 10
Summary
Technical Questions
  What level of access will be possible?
  What stitching plans are permissible? Different sensor sizes?
Modelling Questions
  Effect of true sensor profile?
  Effect of sensor peripheries?
  Power/Data
    What degree of power/data cabling would be needed in the current design?
    How would this affect the physics simulations?
    Does this imply the need for on-chip power management or on-chip data aggregation?
How to track these questions? Also, other points to capture, like those raised last week.

## Slide 11
Notes: The abstract pattern can be removed or repositioned if required. Be careful to ‘Send to Back’ so that it does not obscure any important information.