## Slide 1: Q1: Based on the recent realistic simulations of CeC cooling, can you present a summary of updated requirements for the experiment, and also highlight any new effects and requirements that need to be taken into account
…
Vladimir Litvinenko

## Slide 2: Q2: List the observed beam stability issues that hampered progress with the CeC experiments, and list possible mitigations
…
Vladimir Litvinenko

## Slide 3: Q3: Clarify what would happen to sPHENIX if the dump kicker would pre-fire when the relays are closed before transition
The thyratrons have never pre-fired below 10.85 kV & transition with Au79+ is at 6.21 kV.
Until demonstrated safe, the sPHENIX HV acquisition & solenoid magnet will be turned-off during injection & ramp, therefore limiting the risk of damage to the MVTX and other sensitive devices.
Matthieu Valette

## Slide 4: Q4: What is the reliability of injector chain through the AGS. What are the drivers for downtime. Clarify the long-term future for the motor-generators.
Based on the Run22 statistics, the injectors (AGS/Booster) availability is around 97%. LINAC availability is also around 97%.
For injectors, the major contributors of the 3% downtime are power supplies (0.8%), cooling water (0.7%) and RF(0.6%).
For LINAC, a big contributor of failure is the acceleration module RF system, which accounted for about 50% downtime
The long-term plan for the motor-generators is to use Siemens while using Westinghouse as its backup. Working with several vendors to ensure regular service of MG sets.
Haixin Huang