## Slide 1: RHIC Performance Update
December 13, 2022
Michiko Minty
Associate Chair for Accelerators and Applications
Accelerator Division Head

## Slide 2
Recent RHIC Run Performance
Beam Energy Scan program (BES-II during RHIC Run-19 through Run-21)
RHIC Run-22: last full energy p+p run prior to EIC construction
RHIC Run-23 to Run-25
RHIC 25 year upgrade plan and cryo upgrade for the EIC
Response to recommendation from C-AD MAC 2021
Summary
Contents
2
M. Minty, CAD MAC – Dec 2022

## Slide 3: Recent RHIC Run Performance
M. Minty, CAD MAC – Dec 2022

## Slide 4: Beam Energy Scan (BES) Program
From 2015 NSAC Long Range Plan for Nuclear Science
BES-I: 2010 - 2011, 2014
BES-II: 2018 - 2020
4
M. Minty, CAD MAC – Dec 2022
Notes: Picture from 2015 NSAC long-range plan

## Slide 5
COOLING
in Blue RHIC ring
COOLING
in Yellow RHIC ring
High-Power Beam Dump
Extraction beam line
DC e- Gun
704 MHz SRF
Booster Cavity
2.1 GHz Cu Cavity
9 MHz Cu Cavity
704 MHz Cu Cavity
Injection beam dump
RF Diagnostic Beamline
RHIC TRIPLET
RHIC DX
180°
Bending
Magnet
e-
e-
e-
* NOT to scale
Cathode
loading system
LF solenoid
HF solenoid
Transport solenoid
Quad corrector
Trim corrector
Corrector 3.8 ID
Corrector 6.0 ID
BPM 2.4 ID
BPM 4.8 ID
Bellows
Ion pump
Merger
Beamline
Transport
Beamline
704 MHz Cu Deflector Cavity
A. Fedotov et al, Experimental Demonstration of Hadron Beam Cooling Using Radio-Frequency Accelerated Electron Bunches, Physical Review Letters 124, 084801 (Feb 2020).
First operational electron cooling in a collider (Run-20)
Critical for lowest-energy RHIC program in Run-21
DC gun
high QE cathodes
high-power fiber laser
5 RF systems, including one SRF
machine protection
many magnets
instrumentation
100 meters of beamlines
Technologies
Low Energy RHIC electron Cooling (LEReC)
Principle Investigator
Alexei Fedotov
5
M. Minty, CAD MAC – Dec 2022

## Slide 6
All Run-20 goals achieved or exceeded
RHIC Run-20 – first operational use of LEReC
First demonstration of high-energy bunched-beam electron cooling
First application of electron cooling in a collider
Run Coordinator: Chuyu Liu (Run-19 to 21)
LEReC Principal Investigator: Alexei Fedotov
M. Minty, CAD MAC – Dec 2022

## Slide 7: RHIC Run-21 – highest priority for BES-II
Second year with low-energy electron cooler (LEReC)
Most difficult energy (~40% lower than nominal injection energy)
min projected
max projected
Highest priority Run-21 goal significantly exceeded
Run Coordinator: Chuyu Liu (Run-19 to 21)
LEReC Principal Investigator: Alexei Fedotov
M. Minty, CAD MAC – Dec 2022

## Slide 8: BES-I vs BES-II luminosity
1st year
2nd year
3rd year
Goal was Lavg (BES-II) = 4x Lavg (BES-I)
In BES-II
3.8 x Lavg (BES-I)
4.0 x Lavg (BES-I)
4.7 x Lavg (BES-I)
6.4 x Lavg (BES-I)
~10 x Lavg (BES-I)
1st year
2nd year
Successful completion of the multi-year BES program
3rd year
~10x BES-I
with LEReC
with LEReC
at lowest beam energies
M. Minty, CAD MAC – Dec 2022

## Slide 9
RHIC Run-22 – last full energy p+p run at RHIC
Schedule
p+p polarized proton collisions at 508 GeV c.o.m. with
new STAR forward detector upgrade
  final cooldown to 4K delayed by 13 days
  14 day run extension granted by DOE Office of NP
Run-22 delivered luminosity
Run-22 delivered figure of merit
Performance summary
Run coordinator: Vincent Schoefer
  forward program: 107%, exceeding the goal
  mid-rapidity: ~98%, achieving the goal
  two snake magnets damaged (power outage)
  extended running with AGS Westinghouse motor generator
(Unusual) run challenges
Successful completion of last full energy polarized proton run
M. Minty, CAD MAC – Dec 2022

## Slide 10: RHIC Availability
Availability = beam time / scheduled beam time (denominator excludes scheduled maintenance)
Availability goal: 85% (raised in FY20, from 82.5%)
Au+Au
(BES-II)
low energy
p+p
255 GeV
courtesy C. Naylor
>85% availability achieved averaged over last 10 years
86.7% 10-year average
M. Minty, CAD MAC – Dec 2022

## Slide 11: RHIC runs 2023 - 2025
M. Minty, CAD MAC – Dec 2022

## Slide 12
M. Minty, CAD MAC – Dec 2022
RHIC Run Scenarios 2023 – 2025

## Slide 13: Reliability - operation during summer months
Heat
  Many support buildings not equipped to operate with sustained high temperatures
  Many unique AC systems
Humidity
  Reduced cooling tower efficiency, increased load on AC equipment
  Condensation issues
    Maintenance
      ensure existing systems are operable at full capacity
      verify existing AC spares inventory (9 portable units, 6 portable high-volume fans)
Mitigation
  Aging equipment, some obsolete controls and parts
Air Conditioning
  New procurements
    spare AC systems for RHIC alcoves (5)
    portable AC units for RHIC service buildings (6) for power supply quench detection racks
  AC ductwork modifications
  More frequent power dips and/or outages (storm related), possible brown-outs
Power
Concerns
M. Minty, CAD MAC – Dec 2022

## Slide 14: Reliability - injector complex
LINAC RF power amplifiers - continuing to maintain a 5-year inventory
  Transitioned (completed in 2019) from person-based to group-based operational support by transfer of
  responsibilities to C-AD support groups
  Note: accelerator readiness reviews are needed for these (existing) facilities
LINAC / AGS Increased detail in shutdown schedule management lately as time available for maintenance becoming shorter with expanding user programs at MIRP (isotope production) and NSRL (NASA)
AGS Motor generators (MG) – Siemens MG and back-up Westinghouse MG with 40+ and 60+ years in operation, respectively: coordinating closely with new companies (TECO Westinghouse, Industrial Power Systems, and ABB)
M. Minty, CAD MAC – Dec 2022

## Slide 15: Reliability – infrastructure upgrades
Select BNL Science Lab Initiatives (SLIs)
  1) Critical Utilities Rehabilitation Project, CURP (FY20 – FY26, $92M) – CD2/3 completed
    Electrical distribution system upgrade including a new feeder to replace 60-year-old underground feeder and 13.8 kV switch gear
    Steam distribution system upgrade (replace up to 3 central plant chillers, install an additional chilled water storage tank)
  2) Critical Utilities Revitalization & Enhancement, CURE ($200-350M) – proposed
    Replace or refurbish components of the original building electrical distribution equipment (all more than 50-years old switchgears, motor control centers, power panels and automatic transfer switches) to enhance operational safety and reliability in several facilities
    Notes: compatibility and availability of spares a concern, however components are generally reliable upgrades improve safety during servicing
M. Minty, CAD MAC – Dec 2022

## Slide 16: Other factors affecting operational reliability
  active hiring in close coordination with HR and recruiters
  training and (some) mentoring of new and existing workers
  improving documentation of procedures, workplans, project archiving
  no fixed price contract, price volatility
    FY21: $41/MWh
    FY22: $61/MWh
    FY23: planning with $69/MWh
Personnel
retirements, relocations, and burnout – addressing with
Electrical costs
Cost of LHe
  BNL contract bid for $50/gallon
  sole source quote received (Oct 27) for $77.4/gallon
$57/MWh
M. Minty, CAD MAC – Dec 2022

## Slide 17
RHIC Snake Magnet – plan for Run-24
Installation schedule estimate with early start
installation mechanical ~ 3 weeks
electrical testing ~ 3 weeks
Dummy magnet installed and fully tested (leak-checked) for Run-23
Repaired RHIC Snake Magnet will be ready for Run-24
Installation prior to Run-23 contingent on sPHENIX schedule and available workforce
M. Minty, CAD MAC – Dec 2022
Repair completion: March 23, 2023 (schedule detail in backup slides)

## Slide 18: RHIC 25-year plan and cryo upgrade for the EIC
M. Minty, CAD MAC – Dec 2022

## Slide 19
25+ Year Upgrade Plan
Goals
  maintain technical infrastructure
  ensure hadron injector complex ready for EIC commissioning while also running for external users (NSRL and BLIP), and possibly HEET
  ensure that system upgrades satisfy both short-term injector and RHIC needs as well as longer-term EIC requirements
Initiated in 2018 for RHIC and the injector complex with considerations for the EIC
Assessed periodically based on need for
  performance upgrades
  upgrades of obsolete systems
Assumes no further large accelerator upgrades until the end of RHIC operations in 2025
Manager: Rob Michnoff
M. Minty, CAD MAC – Dec 2022

## Slide 20: Technical infrastructure upgrades
Bldg. 912 Existing SRF Infrastructure
(clean rooms, HPR, VTFs, RF test area)
Existing Laser development area
Cryo Upgrade in progress
Bldg. 924 Instrumentation
Upgrade complete
Bldg. 905 Vacuum
Almost complete
Bldg. 911 Power Supplies
Complete
Building upgrades supported mostly by BNL, technical upgrades by C-AD
20
M. Minty, CAD MAC – Dec 2022

## Slide 21: 2018 – Evaluation of upgrade and infrastructure needs for RHIC+EIC Over Next 25+ Years
Costs initially sorted into funding streams (eventually assumed by EIC)
C-AD labor not included (historically used ~25 FTE for upgrades)
Some large items (e.g. Booster MMPS $11.5M, Booster transformers $4.8M) not captured in present funding plan
21
Update in progress
21
 | (all numbers in $M) | Total cost | RHIC |  |  | EIC |  | 
 |  | with OH | Total | Ops | CE/AIP | Total | Ops | CE/AIP
1 | Buildings | 0.8 | 0.8 | 0.8 | 0.0 | 0.0 | 0.0 | 0.0
2 | Water Systems | 4.9 | 2.2 | 1.1 | 1.1 | 2.7 | 1.0 | 1.7
3 | Electric Power Distribution | 16.6 | 9.2 | 2.0 | 7.2 | 7.4 | 0.2 | 7.2
4 | Electrical Systems | 42.0 | 37.1 | 15.3 | 21.8 | 4.9 | 0.8 | 4.2
5 | Cryogenic Systems | 23.9 | 23.9 | 2.4 | 21.5 | 0.0 | 0.0 | 0.0
6 | Vacuum Systems | 10.0 | 4.8 | 2.8 | 2.0 | 5.3 | 0.5 | 4.8
7 | RF Systems | 11.0 | 1.7 | 0.1 | 1.5 | 9.4 | 1.4 | 8.0
8 | Instrumentation Systems | 11.2 | 9.8 | 3.2 | 6.6 | 1.4 | 1.0 | 0.4
9 | Controls Systems | 32.3 | 12.1 | 8.4 | 5.9 | 20.2 | 6.3 | 13.9
10 | Preinjector Systems | 1.2 | 1.2 | 0.6 | 0.6 | 0.0 | 0.0 | 0.0
11 | Other | 0.1 | 0.0 | 0.0 | 0.0 | 0.1 | 0.0 | 0.1
 | Total cost | 154.2 | 102.8 | 36.9 | 68.2 | 51.4 | 11.1 | 40.2
 | Annual cost | 6.1 |  |  |  |  |  | 
 | Expected annual funding | 5.5 | 5.5 | 2.0 | 3.5 | 5.5 | 2.0 | 3.5
Paid in part by lab infrastructure funding
Largest medium-term need
Present plans call for use of all AIP funds to support cryogenic system upgrades
M. Minty, CAD MAC – Dec 2022

## Slide 22
AIP and CE Funding plan (FY2021-2028) - updated 2022 LMBB scenario 1
Availability goal raised from 82.5% to 85% two years ago
Booster Main Magnet Power Supply upgrade not presently funded by AIP
CE completed before end of FY2025 and AGS cycloconverter upgrade would still benefit RHIC
Majority of AIP funding needed for cryo upgrades, not sufficient for completion before EIC commissioning starts (cryo upgrades would continue beyond FY2028)
[Note: AIPs can only start with all funding in hand]
M. Minty, CAD MAC – Dec 2022

## Slide 23
AIP and CE Funding plan (FY2021-2028) - 2022 LMBB scenario 2
Alternative funding resources requested to complete cryo upgrades before the EIC
Availability goal raised from 82.5% to 85% 2 years ago
Almost same plan for Capital Equipment as for Scenario 1
CE completed before end of FY2025 and AGS cycloconverter upgrade would still benefit RHIC
M. Minty, CAD MAC – Dec 2022

## Slide 24: Cryo upgrade detail
Bldg 912 SRF test facility
new Cryo Plant: $7M available in the AIP bank for major procurements
  received quotes for planned work significantly higher than expected – coordinating to reduce scope
Phase 1 upgrade: main 4K Plant
oil skids, intercoolers/aftercoolers, ambient vaporizers
Phase 2 upgrade: main 4K Plant
cold end (10K-4.5K) heat exchanger and expander 7
Phase 3 upgrades for reduction in Helium consumption
main 4K plant: replace mechanical joints and flanged warm valves with welded joints
collider ring: replace current lead return circuits and valve box fittings with welded joints
more urgent now: 7% per year price increase over 15 years; significant increase last year
M. Minty, CAD MAC – Dec 2022

## Slide 25: Response to Recommendation from C-AD MAC 2021
M. Minty, CAD MAC – Dec 2022

## Slide 26
Recommendation: Perform an assessment of components and spares needed to continue running in the EIC era
Ongoing effort as part of the 25-year plan
LINAC/Booster/AGS
oversight of component spares continue to be maintained by support groups
LINAC/Booster will continue to operate in support of user programs
AGS may operate if HEET facility is funded
The EIC does not place additional requirements on the (hadron) injectors
Spares for the new electron accelerators (Rapid Cycling Synchrotron and Electron Storage Ring) are the purview of the EIC Project
For the EIC Hadron Storage Ring, multiple superconducting magnets will be available
M. Minty, CAD MAC – Dec 2022

## Slide 27: Summary
M. Minty, CAD MAC – Dec 2022

## Slide 28
Summary
RHIC runs – 4 years solid and successful performance
RHIC run performance (Runs 19-21) – completion of the BES-II program with LEReC
    successful (beyond expectation) demonstration of high-energy electron beam cooling
    first-ever utilization of high-energy bunched-beam electron beam cooling in a collider
    completion of multi-year beam energy scan program
  RHIC Run-22 - last run with full energy polarized proton collisions
    with 2-week extension, goals met despite challenges (RHIC Blue Ring Siberian Snake, extended operation
    using AGS backup motor generator)
Reliability challenges in upcoming runs
  proactively addressing concerns about operation through summer months
  emergent increase in electricity and helium costs
  challenged by dynamically changing workforce
RHIC Blue Snake magnet repair and mitigation plan for Run 2024
  repairs to be completed March, 2023
  dummy magnet in place for Run-23, installation prior to Run-23 TBD
  expected to be ready for run-24
Ongoing and planned AIP and CE projects including RHIC 25-year plan and cryo upgrade
  all AIP funds are planned to be spent on cryo upgrades
  cryo upgrades will likely continue beyond FY28 with present level of AIP funding
  alternative funding resources needed to complete main cryo upgrades
w/ LEReC
w/ LEReC
M. Minty, CAD MAC – Dec 2022

## Slide 29: Backup Slides
M. Minty, CAD MAC – Dec 2022

## Slide 30
3-D cooling was commissioned and optimized using 2 MeV electron beam for Physics operation at sNN = 9.2 GeV.
First operational electron cooling in a collider (cooling of ion beams in collisions and luminosity optimization with cooling) was established.
Stable 24/7 running of high-current electron accelerator over many weeks.
Cooling was made operational, including implementation of laser position feedback, intensity feedback, energy feedback, automatic cooling section orbit corrections and feedback.
Controls of LEReC accelerator was transferred to the MCR operations, with support by LEReC experts when needed.
Five LEReC peer-review articles were published (see listing in reference slides): one Phys Rev Letters and four Phys Rev Accel Beams papers, including two which were selected as “Editors’ suggestion”.
Alexei Fedotov received 2019 Brookhaven Science and Technology Award with citation of world’s first “demonstration of bunched beam electron cooling”
LEReC summary for 2020
M. Minty DOE 2020 Site Visit

## Slide 31
Beam Energy Scan II scoreboard
all Run-20 goals achieved or exceeded
M. Minty DOE 2020 Site Visit

## Slide 32
RHIC Run-21 – completion of entire beam use request
Highest priority FY21 goal for BES-II achieved with LEReC in 13 weeks.
Met all next-priority STAR goals including an additional d+Au run (8 modes + beam delivery for CeC).
Missions achieved with limited on-site staff and full off-site coverage during the COVID pandemic.
All Run-21 goals achieved or exceeded + additional d+Au run
1.7 B
8.65
17.3
100 200 d+Au 100 M 4
100 M (central)
M. Minty DOE 2021 Site Visit

## Slide 33
Operated 24/7 high-current electron beams with stable cooling at lowest-ever, and most challenging, RHIC beam operating energy (3.85 GeV/n) in FY21 Run.
All performance goals attained. Additional operational improvements implemented:
  New LEReC 1.4 GHz cavity and new RHIC bunch-by-bunch dampers
  Feedback-based beam control for electron orbits in cooling sections, electron beam energy, electron beam intensity and laser position feedback.
  Utilization of existing 3rd harmonic (28 MHz) cavity in RHIC to reduce ion beam peak current
  Optimization of electron beam currents based on operational experience
    15-20 mA (for Au ions at 4.6 GeV/n in 2020)
    8-20 mA (for Au ions at 3.85 GeV/n in 2021)
Select demonstrated additional technological advances:
  Robust photocathodes with high initial Quantum Efficiency
  Photocathode lifetimes of 6-10 days
  Stable and reliable operation of high-power fiber laser for photoelectron gun
With LEReC, the highest-priority goal of the BES-II program was successfully completed in FY21 in ~ 13 weeks.
Highlights from FY21 BES-II program with LEReC
1.4 GHz cavity
Run Coordinator: Chuyu Liu
M. Minty DOE 2021 Site Visit
Notes: 1.4 GHz cavity, amplifier and circulator installed November, 2020. Designed to increase the electron bunch length from 0.4 to 0.6 ns while preserving the slice energy spread. Intent to reduce the “heating” effect from the electrons on the ions.
Bunch-by-bunch damper: used repurposed stripline kickers and existing BPMs. Long-desired general purpose device to combat instabilities. Reduces tune spread to allow for smaller chromaticity.

## Slide 34
RHIC Blue Snake Magnet
Note: plan for Run-23 is Au+Au (unpolarized), snake magnet needed for Run-24 (p+p )
Two Snake magnets damaged during Run-22 (12/3/21, 12/12/22)
During Run-22
all 4 spare magnets tested at SC Magnet Division (SMD)
prepared plans for repair (SMD and C-AD)
Gary McIntyre (C-AD, retired) hired as consultant
During and after RHIC run
one spare magnet appropriately reconfigured (SMD)
After RHIC run
extensive electrical testing and training (C-AD electrical systems group)
transported to SMD for repair (6/6/22), next slides
damaged
M. Minty, CAD MAC – Dec 2022

## Slide 35
  1 Spare Storage Unit
    reworked to correct configuration
    Hung on top hat and is being wired for cold test
  1 Spare Storage Unit
    Electrically tested & ready for magnet assembly
  Magnet Disassembly
    Cold mass, heat shields removed from cryostat
    Cold mass disassembly nearly complete
      End volumes, bus work removed
      Helium vessel shells cut off
      Cold mass reinstalled onto assembly fixture
  Cold test 1 Storage Unit
  Remove beam pipe / BPM assembly
  Remove storage units from assembly fixture & replace with spares
  Complete cold mass assembly & pressure/leak check test
  Complete cryostatted magnet assembly
RHIC Snake Magnet - repair details
Work completed
Work remaining
M. Anerella (SMD)
Repair completion: March 3 , 2023 (schedule detail in backup slides)
M. Minty, CAD MAC – Dec 2022

## Slide 36
RHIC Snake Magnet - repair schedule
M. Anerella (SMD)
M. Minty, CAD MAC – Dec 2022