## Slide 1
FFA’23
Compact Accelerators based on Canted-Cosine-Theta Magnets
Hannah Norman
  Universities of Manchester and Melbourne, Cockcroft Institute
  14/09/23
hannah.norman@manchester.ac.uk

## Slide 2: Outline
(Brief) Review of Canted-Cosine-Theta (CCT) Technology
Application to Compact Accelerators:
  NIMMS (Next Ion Medical Machine Study) Superconducting Synchrotron
    Beam Dynamics and Stability Studies
  CCT Magnets in FFAs: How would that work?
      TURBO
Review and Questions

## Slide 3
What are CCTs?
Image credits: G Kirby and J van Nugteren, CERN

## Slide 4
From Maxwell’s magnetic field equations, we arrive at the Laplace equation
Quick Magnet Theory
From 2D magnetic field solution:
Bn , An = Normal and Skew multipoles
FT on Bmain returns multipole coefficients
Scale for different Rref to know field everywhere

## Slide 5: Coil-Based Superconducting Magnets
One quadrant of cosine-theta coil
Hadron colliders require strong (> 4 T) magnetic fields
  Superconducting magnets needed
  Common type is ‘Cosine-Theta’
  Wire carrying current on annulus of width bw
  Pure dipole (n=1) field produced for current density

## Slide 6: Canted-Cosine-Theta Magnets
Dipole component adds
Solenoid component cancels
How do they work?
(AKA double helix, tilted solenoid, etc…)
Coil-dominated
‘Perfect’ dipole field due to
Basic idea of CCT

## Slide 7: Examples of CCT
A very attractive solution for…
CCT Winding Geometry
ϑ = azimuth, h = winding pitch, α = tilt, n = order, ϕ = phase (0 = normal, ½ = skew)
Requires little to no pre-stress
Requires no additional supports
Can achieve very strong fields (16 T)
Concept to combat limitations in cos-theta magnets:
Winding Path Equations

## Slide 8: High Energy Colliders
*(now will be racetrack)
Name | Conductor | Bore [mm] | I [kA] | B-bore [T] | B-bore tested [T]
CCT1 | NbTi | 50 | 4.0 | 2.5 | 2.4
CCT2 | NbTi | 90 | 10.3 | 5.1 | 4.6
CCT3 | Nb3Sn | 90 | 17.7 | 10.0 | 7.4
FCC-hh Main Dipole*
Fast turnaround of CCT development
Poor control of cable positioning
Costly materials (Nb3Sn conductor → $1.7M USD per magnet)
Study Outcomes:
Design goals: 16T, 15m long, 50mm aperture
  R&D short samples parameters (2-layer, operating at 4.2 k)

## Slide 9
Corrector (HIE-ISOLDE)
Extraction septum magnet (SuShi)
High Energy Applications
Superconducting Shield (SuShi) Septum Magnet
High Intensity and Energy (HIE) Isotope Mass Separator (ISOLDE) Main Ring layout
Project | Magnet | Field [T] | Gradient [T/m] | Current [A]
HIE-ISOLDE | F | 2.27 | 13.8 | 437
 | D | 2.27 | -13.8 | 437
 | Trim Quads | - | 2.2 | ± 300
SuShi | Dipole | 3.0 | - | 428

## Slide 10: Medical Accelerators
PAMELA FFA
Magnet | Field [T] | Current [A] | Length [m] | Rinner [mm] | Router [mm]
F | 3.9 | 755 | 0.6644 | 170 | 216.2
D | 5.06 | 650 | 0.66 | 170 | 244
Variation of multipole strength along magnet
length
Solenoidal components did not cancel locally
  Lead to beam losses after a few turns
  2 additional layers to cancel unwanted components
Multipole errors adjusted via winding
  Tune shift (0.3, 0.23) (h,v) v.s. (0.5, 0.5) previously
Study Outcomes:
PAMELA FFA and particle tracing through cell

## Slide 11: Medical Technology
Gantries (LBNL, HUST)
LBNL (top), HUST (bottom) SC gantry layouts
Parameter | LBNL | HUST
B[T] | 2.4 | 2.46
Gradient [T/m] | 17.43 | 12.0
Current [A] | 922 | 584.38 (dip), 370.84 (quad)
Physical Bend [°] | 67.5 | 90

## Slide 12
Why CCTs?
Image credits: G Kirby and J van Nugteren, CERN

## Slide 13: Advantages
Due to the unique geometry of the CCT,
Dipole
Quadrupole
Sextupole
Octupole
Decapole
Dodecapole…
Can be combined function (depending on coil winding)
Good field quality
Small stresses on conductor
Can independently tune harmonics
Compact design
Simple to wind
Can be strongly curved (for e.g space saving purposes)

## Slide 14: Why not CCTs?
Though proposed in 1969, CCTs are still a relatively new concept and widely untested
Need more conductor for higher fields (£££)
No one has used them in medical accelerators in practice yet
Can be complicated to design and resolve fields (especially for curved case)
Can’t ramp quickly (leads to quench)

## Slide 15: Possible Applications
Though CCTs look good on paper, we should be careful about how we are using them and what we are using them for
Application | Field | Length | # of magnets | Benefit v.s. cost, effort
Large Colliders | Large (> 16 T) | Long (15 m) | Lots | Arguable
Compact Machines | Small (3-4 T) | Short (~2 m) | Few | Huge
Let’s look at applying a CCT to a compact machine…

## Slide 16
Application to Compact Accelerators:
NIMMS
(Next Ion Medical Machine Study)
A collaborative study from CERN to develop portfolio of technology for future facilities
Image credits: Thomas Kaestenbauer, CERN

## Slide 17: NIMMS Initiative (2019-present)
17
Develop a “toolbox” of technologies for a new generation of medical ion accelerators
Follow-up study to PIMMS (2000) (CNAO/MedAustron)
Support from EU programs HITRIplus and iFAST + many collaborators
Partnered with SEEIIST to construct treatment + research facility in South East Europe
Goal of NIMMS: Design an ion therapy machine (+ gantry) for future facilities
Specifications:
Smaller (footprint 1000m2 )
Cheaper (<€120M building costs)
Accelerate heavy ions (C, He, etc.)
Higher intensities (>1x1010 pps)
Example layout of SEEIIST facility

## Slide 18: Future Ion Therapy Machines
NIMMS Superconducting Compact Synchrotron, square and triangular versions courtesy of E. Benedetto
18
Possible Candidates:
+ others…
Example layout with normal conducting synchrotron , courtesy of M. Vretenar
Main Specs:
75m circum.
Max B = 2T
Main Specs:
27m circum.
Max B = 3.5T
Normal Conducting Synchrotron
Superconducting Synchrotron

## Slide 19: NIMMS Medical Superconducting Synchrotron
Goal: Design a smaller heavy ion therapy synchrotron for next gen. facilities
NIMMS Superconducting Compact Synchrotron, courtesy of E. Benedetto
What makes this design special?
19
Based on 90° CCT magnets at 3.5 T
27 m circumference, 1.89 m bending radius
Combined-function quadrupole layers inside dipole
Adapt magnets from synchrotron to gantry
→ Study effects of special magnet geometry
Aim: Perform beam dynamics simulations

## Slide 20: Magnet Options
20
Original NIMMS design based on AG-CCT
Two alternative main magnet options:
  CF-CCT (WIP)
  CF Cosine-Theta dipole
Modelling in OPERA 3D:
Curved cosine-theta demonstrator EM model (30 °)
AG-CCT (coils only) EM model (90 °)
Credit: W. Wan, LBNL
90° bend
B = 3.5T, g= 10 T/m
Courtesy of M. Karpinnen
30° bend
B = 3T, g= 3.5 T/m

## Slide 21: Curved, Combined-Function Magnets
21
How does curvature affect the field distribution?
How does this affect particles in the accelerator?
What issues arise from additional CF layers?
Alternating gradient CCT layers
Problem: We can’t use multipole expansion
Curvature (seemingly) introduces additional harmonics
→ Can be corrected
Table from C Goodzeit

## Slide 22: Validity of Multipole Expansion
We’ve already seen we can express the magnetic field in a 2D straight system as:
Vector potential in curved coordinates:
Not a solution to Maxwell’s equations
Multipoles have no physical meaning
Can’t use scaling law
22

## Slide 23: Validity of Multipole Expansion
Three cases where we can’t use multipole expansion to describe the field:
When might we have all three to worry about? In FFAs!
In curved coordinate systems
Longitudinally dependent fields (at the ends)
Where the field has longitudinal components (off-axis)
Workaround Solution:
Taylor expansion of potential satisfies* Maxwell’s equations
23
Notes: *recursion relations

## Slide 24: Validity of Multipole Expansion
Analytical solution
(x,y) cross-terms for each z
Can fit to field from straight magnet fieldmaps → Adapting for curved CCT (WIP)
24
In 3D*:
2D fit to field map data for ideal straight magnet
Notes: *recursion relations

## Slide 25: Straight and Curved Magnet Comparison
Component | Straight |  | Curved | 
 | FFT | Fit | FFT | Fit
B1 (Dip.) [Tm] | -3.46 | -3.46 | -3.46 | -3.43
b2*(Quad.)[10-4 ] | -318.2 | -287.4 | 236.1 | 275.6
b3 (Sext.)[10-4 ] | 3.1 | 3.0 | 1.9 | 1.5
b4 (Oct.)[10-4 ] | -1.7 | 2.0 | 2.5 | 5.2
x
y
z
(*On-axis analysis for now)
Developed two analytical techniques*
25
Measuring field as a function of angle
  Calculate multipoles using Fourier analysis
Measuring field map over line
  Fit straight line to main field along midplane (y=0)
Field sampling in OPERA 3D

## Slide 26: Curved CCT Field Gradients
Using the 2nd technique:
26
Measuring field map over line
  Fit straight line to main field along midplane (y=0)
Component | Outer Fringes | F-Layers | D-layers (Main Body)
B1 (Dip.) [Tm] | 2.50 | 3.30 | 3.93
B2(Quad.)[T/m] | -7.26 | -9.23 | 9.67
B3 (Sext.)[T/m2 ] | 2.80 | 3.10 | 5.42
B4 (Oct.)[T/m3 ] | 309.80 | 244.44 | 298.80
Expected result
Perpendicular vectors to central CCT curvature for field sampling

## Slide 27
How do the Gradients affect Beam Dynamics?
Image credits: CNAO, CERN

## Slide 28: Particle Tracking Study
Parameter | Value
Ekmax [MeV/u] | 430
Nparticles [-] | 2 x 1010
σx, σy [mm] | 0.85, 1.78
Qx , Qy [-] | 1.68, 1.13 (extraction) 1.72, 1.09
NIMMS Synchrotron in MAD-X with magnets shown
Initial tracking parameters for the NIMMS Synchrotron
28
Track particles in synchrotron lattice
With and without curved magnet errors
Feed errors into lattice dipoles for tracking
→ How ‘bad’ are they?

## Slide 29: Frequency Map Analysis
29
Tracked particles at initial offset (x,y) in accelerator for 2048 turns
Gathered position data from each particle per turn
Performed an FFT on data to return qx (NAFF)
Turn-by-turn data split to identify stable tune regions
→ This lets us see how long those particles last
Left: No resonances driving particle loss
Right: Amplitude growth outside physical aperture
Key Takeaway: Gradients aren’t causing huge tune shifts
Normal working point
Extraction working point

## Slide 30: Particle Tracking Study
Map of starting tracking locations (x,y) corresponding to
each particle’s time in the ring. DA estimated from bottom dark blue region
30
Map (x,y) to identify stable regions (DA)
DA mostly preserved (horizontally) up to half-aperture:
  |x| = 0.013 m, |y| = 0.003 m, compared with base lattice |x|= 0.014 m, |y| = 0.010 m
→ Further checks needed:
Redefining our magnet
Benchmarking with another tracking code

## Slide 31: Integrated Gradients v.s. Gradient Lenses
Dynamic aperture with integrated sextupole field (k3L) distributed inside SBENDS
Dynamic aperture with sextupole strength k3 distributed in two thin lenses in the extremities of each SBEND
How do we represent our magnets + gradients?
Commonly use ‘integrated’ gradients distributed over magnet
Looking at DA, integrated gradients v.s. lenses aren’t equivalent
How do we know which one is right?
31

## Slide 32
32
Split up magnet into more slices in fringes to capture finer field detail at ends
Higher order derivatives over magnet length, courtesy of L Garolfi
Rinse and Repeat (with more slices)
MAD-X Survey for original magnet (left) and split up magnet with additional lenses (right)

## Slide 33: How many slices are actually enough?
Can verify by tracking in 3D fieldmap
Compare error in phsp with MAD-X/PTC
Currently a WIP → will also extend to full ring
Want to validate minimum no. of slices with Zgoubi(doo)
Zgoubi: Ray tracing code to describe off-axis fields, lattice non-linearity (used in FFAs)
2D Polar fieldmap of CCT in OPERA 3D
2D Polar fieldmap of CCT in Zgoubi
Bz[T]
33

## Slide 34: Tolerance Study
Example particle survival plot for k2L, k3L being varied
34
Will want to know how much tuning needed for gradients
Vary k2L, k3L and check particle survival
→ Use combination with highest survival and re-run study

## Slide 35: Summary of Tracking Study Results
Curved CCT harmonics (fairly) well-tolerated by compact synchrotron dynamics using integrated gradients
  Re-run study with many slices
  Validate results by tracking in 3D fieldmap (Zgoubi)
Need to establish tolerances on DA
Introduce 2D field components for non-linear effects
Repeat study → retune magnets
What have we learned?

## Slide 36
Application to FFAs
EMMA, Image credit: S.L. Sheehy

## Slide 37: Possible Application: TURBO (Technology for Rapid Beam Operation)
TURBO FFA Beamline (lab demonstrator version)
Courtesy of J. Yap
37
Scaled-down (0.5-3 MeV) test beamline for treatment
Closed-dispersion FFA arc for Large P Acceptance
Accommodates clinical system requirements
Controllable beam dynamics for transported energies
Non-linear magnets with required multipoles for stability
Unique magnets at each point in arc → CCT demonstrator
Concept:
To show:
Requires:
See Adam Steinberg’s Talk

## Slide 38: Scaling Up
  Higher strength magnets (maximum field ~3.5 T) to treat in modes
  Adjustable multipoles
  Good field quality (1E-4)
  Compactness
1st mode
2nd mode
3rd mode
Species | E [MeV/u] | Tm] |  | T]
p+ | 70 - 250 | 1.23 – 2.43 | 33% | 0.6 – 1.22
4He2+ | 70 - 250 | 2.43 – 3.32 | 33% | 1.22 – 1.66
12C6+ | 70 - 430 | 2.50 – 6.63 | 45% | 1.25 – 3.32
16O8+ | 70 - 500 | 2.50 – 7.26 | 49% | 1.25 – 3.63
Species | E [MeV/u] |  |  | 
p+ | 70 - 250 | 1.23 – 2.43 | 33% | 0.6 – 1.22
4He2+ | 70 - 250 | 2.43 – 3.32 | 33% | 1.22 – 1.66
12C6+ | 70 - 430 | 2.50 – 6.63 | 45% | 1.25 – 3.32
16O8+ | 70 - 500 | 2.50 – 7.26 | 49% | 1.25 – 3.63
Full-scale Clinical Beamline Requires:

## Slide 39: Scaling Up
Alternating-Gradient CCT dipole magnet
  Strong focusing
  Large field to accommodate heavier ions to full kinetic energies
  Compactness, light weight
  Tuneable multipoles
Apply and adapt EM model of AG-CCT in collaboration with NIMMS
But first, a model…
Curved Alternating-Gradient CCT demonstrator could provide:
Notes: Mention momentum ranges achievable (also what was achieved with the previous gantries)

## Slide 40: Summary
Heavy ion therapy necessary but limited by size, cost
Need innovative accelerators based on superconducting magnets
Tools developed for studying effect of magnet gradients on particles in accelerators
Continue study for curved CCT with 3D fields
Establish design criteria for a CCT for other applications (TURBO) (watch this space!)
Canted-Cosine Theta Magnets are an enabling technology
Huge potential, if used correctly
Applications:

## Slide 41: Thanks to:
UniMelb team:
A. Steinberg
J. Yap
F. Zhang
S. Williams
Supervisors: Prof. R Appleby (UoM), Dr S. Sheehy (UniMelb)
Collaborators: Dr E. Benedetto, Dr M. Karppinen (external, NIMMS)
41

## Slide 42: References
[1] D.I. Meyer and R. Flasck “A new configuration for a dipole magnet for use in high energy physics application”, Nucl. Instr. and Methods 80, pp. 339-341, 1970.
[2] S. Caspi S, “A 16T Canted-Cosine-Theta (CCT): An option for the FCC”, presentation, 2015, accessed 01/09/2022
CCT winding diagram, from [2]
[3] FCC-hh main dipole CCT from S. Caspi, “Status and Development of a Nb3Sn CCT magnet”, presentation, 2016, accessed 01/09/2022
[4] HL-LHC main corrector magnets and design parameters (straight and curved), G. Kirby, https://www.researchgate.net/project/LHC-hi-Lumi-orbit-corrector-5Tm-CCT, accessed 26/09/22 (gets updated daily)
[5] Super-beta layout and CCT quadrupole diagram, F Bosi et al (2013). Compact Superconducting High Gradient Quadrupole Magnets for the Interaction Regions of High Luminosity Colliders. 10.1109/TASC.2012.2231716.
[6] Recoil separator ring, Resta Lopez, Javier et al (2021). DESIGN AND BEAM DYNAMICS STUDIES OF A NOVEL COMPACT RECOIL SEPARATOR RING FOR NUCLEAR RESEARCH WITH RADIOACTIVE BEAMS. 10.18429/JACoW-IPAC2021-WEPAB180.
[7] SuShi septum magnet, from http://sushi-septum-project.web.cern.ch/, accessed 27/09/22
[8] PAMELA layout, cell and CCT design details, Witte, Holger et al (2012). The Advantages and Challenges of Helical Coils for Small Accelerators—A Case Study- IEEE TRANS APPL SUPERCONDUCT. 22. 4100110-4100110. 10.1109/TASC.2012.2186135.
[9] Superconducting gantry, CCT and design parameters, L. Brouwer et al, Design and test of a curved superconducting dipole magnet for proton therapy (2020) https://doi.org/10.1016/j.nima.2020.163414.
[10] Superconducting gantry and CCT design parameters, C. Li, "Coil Error Analysis of a Curved Canted-Cosine-Theta Magnet Applied to a Superconducting Gantry (2022) Art no. 4006105, doi: 10.1109/TASC.2022.3170857.
[11] CCT Windings, from G. Kirby “State of the art in CCTs”, 2022, [accessed 27/09/22]
[12] J.S.L. Yap, et al “TURBO: A Novel Beam Delivery System Enabling Rapid Depth Scanning for Charged Particle Therapy (2022) doi:10.18429/JACoW-IPAC2022-THPOMS001
13[] Radiotherapy clinic, https://www.whittington.nhs.uk/default.asp?c=27306 , accessed 28/09/22
[14] HIT Carbon gantry, adapted from https://www.worldscientific.com/doi/abs/10.1142/S0217751X14410024?journalCode=ijmpa , accessed 08/09/22
[15] NIMMS Superconducting Compact Synchrotron, adapted from E. Benedetto
CCT Diagram, E. Benedetto, et al., “A Carbon-Ion Superconducting Gantry and a Synchrotron Based on Canted Cosine Theta Magnets (2021) ,”doi:10.48550/arXiv.2105.04205
[16] Goodzeit, C, et al (2007). Combined function magnets using double-helix coils. 560 - 562. 10.1109/PAC.2007.4440278.
[17] D. Veres, et al, “A New Algorithm for Optimizing the Field Quality of Curved CCT Magnets (2022) doi:10.1109/TASC.2022. 3162389
[18] Curved and straight cosine-theta models, courtesy of M. Karpinnen
[19] H.X.Q. Norman, et al “Performance Study of the NIMMS Superconducting Compact Synchrotron for Ion Therapy with Strongly Curved Magnets (2022) ”,doi:10.18429/JACoW-IPAC2022-THPOMS028

## Slide 43: Extra Slides

## Slide 44: Approximate 3D Map with a Lattice
Compare tracking in fieldmap v.s. SBENDS + lenses for 1 magnet in RF-TRACK
Calculate difference in phase space params.
For certain number of slices in body + fringe regions, 1:1 mapping with tracking in 3D fieldmap
Aim: Find min. set of elements to describe any magnet
From NIMMS/HITRI+: Can replace a 3D fieldmap with a number of SBENDS + gradient lenses
Error estimate 𝜒 2 from converting a 3D field map to a matrix-based symplectic lattice, courtesy of L Garolfi
44

## Slide 45: Problems in FFAs
Disadvantages:
Strong focusing  Large energy acceptance
High rep. rate, fast acceleration, higher currents + intensities
Reliable due to fixed magnets (no ramping)
FFAs (in general) can be a very advantageous accelerator solution:
Large complex magnets  Large footprints
Difficulty adjusting magnets
Higher energies require stronger fields
Heavy dependence on field quality due to DA shrinkage
Might a CCT help?

## Slide 46: Could a CCT be a good fit for an FFA?
CCTs are an exciting technology, but still ‘new’
Could benefit future designs of FFAs, compact medical machines, more possibilities
Straight and curved magnet models for analysis ✓
Particle tracking through 3D gradient fields on and off-axis
Establish tolerances for multi- v.s. single pass systems
To confirm that we can apply (curved) CCTs to FFAs, we need:

## Slide 47: Next Steps
Need full 3D magnetic field representation for magnet
Track particles through these fields (using e.g. Zgoubi, Zgoubidoo) to investigate
  Beam distortion
  Fringe field extent in each layer
  DA shrinkage (needs parameterisation)
Establish design criteria for our scaled-up beamline (watch this space!)