## Slide 1: 25th Annual Accelerator Test Facility (ATF) Users' Meeting Progress on Laser Upgrades
2023-02-28
Marcus Babzien, Igor Pogorelsky, Misha Polyanskiy, William Li
Accelerator Facilities Division

## Slide 2: Outline
LWIR status and present capabilities
CO2 system upgrades
Ti:Sapphire system performance
NIR upgrades
Vacuum laser transport overview
Laser scientific productivity
Accelerator Facilities Division

## Slide 3
Accelerator Facilities Division
3

## Slide 4
Accelerator Facilities Division
Getting ready to deliver 5 TW to IP in 2023
  Vacuum compressor and photon delivery
  Polarization rotator
Reliability improvements
  Implemented shot counter
  Increased # of shots between spark-gap replacement by enforcing 1 min delay between shots
Clear roadmap from 2ps/5TW to 0.5ps/15TW and 100fs/25TW
L-WIR Highlights 2022—23

## Slide 5
Accelerator Facilities Division
Solid-state seed
High-pressure, mixed-isotope CO2 amplifiers
Chirped-pulse amplification
The L-WIR

## Slide 6
Accelerator Facilities Division
--------------------------------------------------------------------------
High-power regime High-repetition regime (two amplifiers) (pre-amplifier only)
-------------------------------------------------------------------------- Central wavelength 9.22 μm 9.22 μm Peak power 5 TW 1 GW Pulse energy 12 J 2.5 mJ Pulse duration 2 ps (FWHM) 2 ps (FWHM) Repetition rate 1 shot/min 1.5 or 3 Hz (e-beam rep-rate)
--------------------------------------------------------------------------
L-WIR Spec Sheet v.2023

## Slide 7
Accelerator Facilities Division
High-pressure, mixed-isotope gas amplifiers
CO2
CO2
Compressor
Stretcher
Present Status 5 TW
7 mJ pump 800 nm
2 μJ 140 ps
10 mJ 100 ps
20 J 70 ps
5 TW
2 ps
Post-compressor
CO2
High-pressure, mixed-isotope gas amplifier
LWIR converter
Compressor
1st Upgrade 7 TW
7 TW
500 fs
Stretcher
~200 mJ pump 800 nm [2 um]
15 TW
500 fs
14 J 100 ps
10 mJ 70 ps
NLPC
3rd Upgrade 25 TW
25 TW
100 fs
2nd Upgrade 15 TW
OPA
Active R&D
Active R&D

## Slide 8
Accelerator Facilities Division
2023: 5 TW
*isotopes, CPA, µJ seed* *vacuum beam delivery*
L-WIR Upgrade Roadmap
Polyanskiy et al., AAC ‘22
Gain
Upgrade #3: 25 TW
*post-compression*
Upgrade #2: 15 TW
*10 mJ seed*
Gain

## Slide 9
Accelerator Facilities Division
Welcome to ATF Laser Team! --- William Li

## Slide 10
Accelerator Facilities Division
NIR Performance Transitioning Phase I → II
Parameter | Units | Stage I Values | Current Values | Stage II Values
Central Wavelength | nm | 800 | 811 | 800
FWHM Bandwidth | nm | 20 | 20 | 13
Compressed FWHM Pulsewidth | fs | <55 | <70 | <75
Chirped FWHM Pulsewidth | ps | >50 | >50 | >50
Chirped Energy | mJ | >30 | 50 | 200
Compressed Energy | mJ | >14 | 32 | 100
Energy to Experiments | mJ | >10 | >30 | >80
Power to Experiments | GW | >250 | >400 | >1067

## Slide 11
Accelerator Facilities Division
Ongoing NIR Work
Diagnose and eliminate ~15% amplitude pre-pulse in Ti:Sapphire discovered during last run period
Enlarge front end vacuum aperture to enable delivery of full Phase II Ti:Sapphire energy to experiments (100 mJ) – (Spring 2023)
Integrate previously utilized optical trombone and Nd:YAG amplifier with vacuum transport to re-establish delivery of 1064 nm to BL1 for Compton scattering experiments
Continue to automate system startup/shutdown as experience is gained to enable autonomous user operation

## Slide 12
Accelerator Facilities Division
Future NIR Upgrades
Improve Ti:Sapphire diagnostics to more efficiently use run time
  Make existing instruments accessible to users online/realtime,e.g. synchronization monitoring oscilloscope
  Add diagnostics for more complete characterization and possible normalization of shot-to-shot variations in spot size, position, energy, pulsewidth, and timing
  Investigate reduction of beam profile distortion from amplifier non-uniform pumping to improve M2/Strehl ratio
  Finish optical delay line for user control of CO2 synchronization when RF engineer becomes available

## Slide 13: LWIR Vacuum Transport
Accelerator Facilities Division
 | Air (12 m) | NaCl (40 mm) | Air + NaCl
n2 | 3.0e-19 cm2/W | 3.0e-16 cm2/W | 
B-integral @ 5 TW | 1.0 | 3.3 | 4.3
Standard requirement: B < 1

## Slide 14: NIR vacuum transport
Accelerator Facilities Division

## Slide 15
Accelerator Facilities Division
NIR Vacuum Transport Upgrade
Motivated by need to deliver higher energy & power with greater stability and reliable long-term performance
Vacuum envelope extended from front end through to IP’s
Full remote actuation of mounts
Diagnostic cameras at bends
Dedicated chamber for in-vacuum compressor can be isolated from user chamber
Compressor design is modular for use at other IP’s as needs arise
First user runs validated stable day-to-day alignment
Some pumpdown flexure observed and now being mitigated
Turning Mirrors
Grating Compressor

## Slide 16
Accelerator Facilities Division
Active laser experiments and hours delivered at ATF in FY2022
Laser + e-beam Laser only *In-air transport
Expt | Title | LWIR | NIR | e-
AE087 | Hard X-ray ICS |  |  | 
AE089 | Plasma compression for terawatt long wavelength lasers | 12 | 51 | NA
AE093 | Direct measurement of fields and radiation in the self-modulated plasma wakefield regime | 220 |  | 
AE095 | Optical diagnosis of self-modulated CO2-laser driven plasma wake |  |  | 
AE098 | Probing electron Weibel instability in optical field-ionized plasmas using ultrashort electron bunches | 130 | 188 | 
AE099 | Directional X-ray radiation produced by an ultra-short period plasma magneto-static undulator |  |  | 
AE100 | The study of high-intensity laser pulse interactions with near-critical density plasmas | 94 | 92 | NA
AE101* | Optical materials for ultrahigh-power long-wave infrared lasers | 122 |  | NA
AE108* | Development of wavelength conversion techniques for generation of coherent radiation at the mid- to long-wave infrared |  | 40 | NA
AE119* | Broadband microwave emission from LWIR picosecond laser ablation | 94 |  | NA
AE122* | Remote detection of radioactivity using long-wave infrared laser-driven avalanche breakdown | 73 |  | NA

## Slide 17
Accelerator Facilities Division
Publications
JOURNALS
R. Kupfer et al., “Raman wavelength conversion in ionic liquids”, Phys. Rev. Appl. 19, 014052, 2023
C. Zhang et al., "Electron Weibel instability induced magnetic fields in optical-field ionized plasmas", Phys. Plasmas 29, 062102, 2022
Z. Chang et al., "Intense infrared lasers for strong-field science", Adv. Opt. Photonics 14, 652–782, 2022
CONFERENCES
Advanced Accelerator Concepts Workshop (AAC), Long Island, NY (USA), November 6–11, 2022
W. Li et al., “Raman-based Wavelength Conversion for Seeding and Optical Pumping of CO2 Laser Amplifiers”
I. Petrushina, et al, “Characterization of the fields inside the CO2-laser-driven wakefield accelerators using relativistic electron beams”
N. Vafaei-Najafabadi , et al, “Experimental Evidence for Suitability of Krypton as a Plasma Source for Two-Color Ionization Injection”
M. Polyanskiy et al., "9.3 microns: Toward next-generation CO2 laser for particle accelerators“
I. Pogorelsky, et al, “Fulfilling the mission of Brookhaven ATF as a DOE’s flagship user facility in Accelerator Stewardship”
64th Annual Meeting of the APS Division of Plasma Physics, Spokane, WA (USA), October 17–21, 2022
Y.-H. Chen et al., ” Proton acceleration in an overdense hydrogen plasma by intense CO2 laser pulses with nonlinear focusing effects in the underdense preplasma”
Other conferences
M. Polyanskiy, "Multi-terawatt long wave infrared lasers: Status and perspectives", 23rd International Symposium on High-Power Laser Systems and Applications, Prague (Czech Republic) June 13–16, 2022
M. N. Polyanskiy et al., "The choice of materials for post-compression of high-peak-power long-wave infrared pulses", Conference on Lasers and Electro-Optics (CLEO), San Jose, CA (USA), May 15–20 2022
Laser + e-beam
Laser

## Slide 18: Questions?
Accelerator Facilities Division

## Slide 19: Backup slides
Accelerator Facilities Division

## Slide 20
Accelerator Facilities Division
Enabling technologies
Efficient 2 μm laser
Ho:YLF
& = “mid-IR Ti:Sapphire”
Ho:YAG
2) Reliable post-compressor
Two-element bulk-material LWIR
post-compressor with spatial filter
- see AE-101 report-
15 μJ @ 9.2 µm
Ti:S
OPA
osc
7 mJ @ 0.8 µm
10 mJ @ 9.2 µm
Ho:
YLF
(*)
osc
~100 mJ @ 2.1 µm
(*) OPCPA or Raman+DFG
(see AE-108 report)

## Slide 21
Accelerator Facilities Division