## Slide 1: 25th Annual Accelerator Test Facility (ATF) Users' Meeting Facility Updates and Plans
March 2, 2023
Andrew Simmonds
Accelerator Facilities Division

## Slide 2: ATF Upgrades
  Design Process
  Configuration Control
  B820
    Laser Capability
    Capability and Safety Upgrades
    Facility Upgrades
  Summary Next Steps
Accelerator Facilities Division

## Slide 3: Design Process
  Scientific need is identified by the user community or AF staff member
  A specification document is generated
  Development of a conceptual design
  Hold design review with AF staff and relevant outside experts
  Conduct detailed design and structural analysis
  Check & approval of drawings and critical analyses
  Archival of drawings and analyses
  Utilize matrixed support from ATRO for engineering and drafting
Accelerator Facilities Division

## Slide 4: Configuration Control
  Radiation calculations are archived by the C-AD RSC
  Shielding is approved by the C-AD RSC. The drawings are reviewed and approved by a cognizant Engineer or Physicist, their supervisor, the Chief Engineer (ME or EE), Division Head, QA, Safety/RSC and the Department Chair before being archived in Windchill.
  Utilize Windchill to release and archive controlled documents
  Shift part numbering and controlled document release process fully to AF responsibility
  Store a Reference Only PDF copy of relevant drawings on SharePoint for wider accessibility
Accelerator Facilities Division

## Slide 5: Present Laser Configuration w/ FY22 upgrades
Accelerator Facilities Division
LWIR
NIR
Seed Laser Table
Final Amplifier
Shielding wall
CPA Table
Polarization Rotator
NLPC 2
NLPC 1

## Slide 6: Modified Laser Transport Systems – Plan View
Accelerator Facilities Division
NIR
LWIR
CPA Chamber
Seed Laser Table
Polarization Rotator Chamber
Final Amplifier
Shielding wall
NLPC 2
NLPC 1

## Slide 7: CPA Vacuum Chamber
  Optics mounted to concrete pedestals for thermal stability and vibration isolation
  Vacuum chamber supported by SS legs
  Bellow is only mechanical connection
Accelerator Facilities Division

## Slide 8: Improvements inside CPA Chamber
  Original CPA breadboard frame and legs were used in air
    Many opportunities for improvement were identified
  Breadboard frames were re-made from solid plate rather than welded tubes
    Produces much flatter and stiffer base for the breadboards to be supported
  Breadboard legs were re-made with solid center section
    Greatly reduces flex of the breadboard due to cantilevered weight of the periscope
  A frame clamp was developed to tie the two piece frame together once installed
    Two piece frames are required for installation into the chamber
  Redesigned leveling legs allow for adjustment and lock from topside
  Redesigned Periscope frame for improved stiffness and replacement
Accelerator Facilities Division

## Slide 9: Flexible Polarization Rotator (FPR)
  Provides infinitely adjustable beam polarization from horizontal to vertical
  6” diameter clear aperture
  FPR and chamber are being installed
Accelerator Facilities Division

## Slide 10: Future Steps…
Continue LWIR vacuum transport to BL2
LWIR
  Extend Vacuum transport to BL#2
NIR
  Front end vacuum transport upgrade
  to increase aperture and energy to experiments
  Capillary Compressor line upgrade to produce sub-10 fs pulse width
Accelerator Facilities Division

## Slide 11: B820 Capability and Safety Upgrades
Experimental Hall
  Continued in vacuum CO2 laser transport to the Compton chamber
  Upcoming Improvements to shielding
    Labyrinth at end of BL#1
    After Spectrometer Dipole at the end of BL#2
CO2 Room
  Upcoming Improvements to shielding
    Extended exclusion zone on the table at N of CO2 room
    Additional shielding of the plasma shutter
Accelerator Facilities Division

## Slide 12: EH Shielding
Accelerator Facilities Division
20° Leg of BL2
Labyrinth/Shielding
Inverse Compton Scattering
Laser Wakefield

## Slide 13: CO2 Shielding
Accelerator Facilities Division

## Slide 14: B820 Facility Upgrades
CO2 Room
  Blue steel wall separating CO2 and FEL rooms was removed
  New LED lighting throughout the CO2 room
  Cable tray system installed
  Bridge Crane installed to service water capacitor and CPA chamber
  Begin replacing drop ceiling with clean room ceiling tiles
Experimental Hall
  BL#1 Electrical reconfiguration
    Better organization of power to the BL from panel in the EH
    Power strips removed and replaced with hard mounted wiremold
  Floor level utility crossover has been eliminated
High Bay
  Moving Machine Shop. Previous location will become a dedicated utility room
  Created an assembly area for items that are larger or need cleaner environment
Accelerator Facilities Division

## Slide 15
 | FY17 |  | FY18 |  | FY19 |  | FY20 |  | FY21 |  | FY22 |  | FY23 |  | FY24 | 
ATF User Program |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
ATF CO2 Power Upgrade R&D |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
NLPC Proof-of-Principle Demonstration |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Building 820 Remedial Maintenance Program |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Ti:Sapphire Laser System (TW-Class)* |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Near-term Laser Power Upgrades (NIR/LWIR) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Electron Beam Improvements |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Non-Linear Materials R&D Program |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
LWIR Power and Rep. Rate Improvements |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Extended User Program |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Facility Reliability, Electrical Infrastructure, Environmental Systems, MPS, etc.
Approved ATF Operations
CPA Config
Isotopic Mixtures
Plasma Shutter
NLPC PoP
5TW Demonstration, Air Transport a ~2.5TW to Users w/good beam quality
Initial 0.6 ps Demo with subsequent ~2x improvement
~0.5 TW to Users
Procure, Deploy, Commission
Non-linear Materials Development & NLPC Engineering Design
5TW to Users
LINAC/eBeam Refurb.
DELAYED
Pulse Compression (a~30fs), Long. Diagnostic - DELAYED
3-year Goal: > 10TW, sub-ps LWIR to Users
ATF (B820) Upgrade Proposal
COVID Delays/ Funding Limitations
*BNL/NRL Collaboration
In-Vacuum
Transport System
TW operation for users
COVID Delays/ Funding Limitations
Upgraded
Transport
ARR Process

## Slide 16: Summary Next Steps
FY23:
  LWIR and NIR upgraded capabilities available for users
    CO2 Laser Room
    EH Beamline #1
    Plans to extend to EH Beamline #2 when funding permits
  Accelerator Readiness Review Preparations and Execution
FY24-25
  Major focus will shift to further improvements in Electron Beam Performance as strongly driven by user needs
    LINAC RF system improvements
    Pulse compression (to better match with combined e-beam/laser requests)
    Short-pulse diagnostics
  Continue facility-level corrective action plans (CAPs) as developed during ARR process
    Example: Electrical Systems CAP will continue for multiple years
  Facility Upgrade Proposal – a few identified thrusts
    Path to <500 fs & >20 TW LWIR capabilities
    Dedicated shielded research space to pursue laser-only particle source experiments
    Further development of multi-beam research capabilities
      Dedicated Ips
      Improved multi-beam timing and synchronization
    LWIR rep-rate path
    User requirements to be further explored during upcoming Science Planning Meeting (see next talk)
Accelerator Facilities Division

## Slide 17: Questions?
Accelerator Facilities Division