## Slide 1: 25th Annual Accelerator Test Facility (ATF) Users' Meeting AE108 - Development of wavelength conversion techniques for generation of coherent radiation at the XUV to LWIR
March 1st, 2023
W. Li1, R. Kupfer2, F. Wang1, J. Wishart1, M. Babzien1, M. Polyanskiy1*, I. Pogorelsky1, T. Rao1, L. Cultrera1, N. Vafaei-Najafabadi1,3, M. Palmer1
1Brookhaven National Laboratory,2Lawrence Livermore National Laboratory,
3Stony Brook University, *PI
Accelerator Facilities Division

## Slide 2: Experimental goals
Upgrading ATF CO2 laser
  9.3 μm: better LWIR seed  shorter pulse length
  4.3 μm: optical pumping  much higher repetition rate
EUV for imaging and lithography
  HHG scales with wavelength: natural fit for ATF
  With CO2 laser, potentially extend to zeptosecond hard x-rays
Seed
few mJ <500 fs 9.3 µm
10++ TW ~500 fs
Pump
100s J, < 1 µs, 4.3 µm
CO2 amplifier
Photo credit: ASML
Popmintchev, Nat. Photonics 4, 828 (2010)
CO2 laser
Accelerator Facilities Division

## Slide 3: Raman conversion
‘Cheap’ high energy laser source ωp
Raman Converter
Residual pump ωp
Converted pump ωp- ωtarget
Nonlinear crystal
Residual pump ωp
Converted pump ωp- ωtarget
ωtarget
Typical Raman shifts are on the order of 1000 cm-1
Perfect for generating LWIR!
Inelastic scattering with vibrational modes
Raman Scattering 
in
out
ΔE
ωpump
ωsignal
ωDFG
Difference-frequency generation (DFG)
Accelerator Facilities Division

## Slide 4: Seed generation in calcite (previous years)
simulated
simulated
Correct peaks
BGS suppresses TPA
Effect on CO2 laser
Red-shifts at saturation
Accelerator Facilities Division
Possibly use 2 μm pump for better DFG efficiency
Good efficiency and energy scaling

## Slide 5
LWIR Roadmap
Polyanskiy et al., AAC ‘22
Gain
Upgrade #2: 15 TW
*10 mJ seed*
Gain
Upgrade #3: 25 TW
*post-compression*
Accelerator Facilities Division
2023: 5 TW
*isotopes, CPA, µJ seed* *vacuum beam delivery*

## Slide 6: Pump generation in ionic liquids (previous years)
Artificial salts that are liquid at room temperature
Can be designed to have specific properties
Settled on EMIM DCA
  Transparent at pump and Stokes wavelengths
  Peak Raman cross section at desired shift
  High viscosity (suppressing Brillouin scattering)
  Good stability
Plots from Kupfer, Phys. Rev. Applied 19, 014052 (2023)
High efficiency
Good spectrum
Raman shifts of selected ILs
Accelerator Facilities Division

## Slide 7: Upgrades to experimental setup
Modified to run in parallel with Ti:sapphire operations instead of competing for the Nd:YAG
Switch to small glass tube for ionic liquid instead of metal container
  Drastic reduction in quantity of IL needed
Use this branch for experiment instead
~300 ml
~30 ml
Accelerator Facilities Division

## Slide 8: High harmonic generation
New component for this year
Laser field causes electron to tunnel out of atomic potential and accelerates it away from atom
Electron crashes back into atom and recombines, releasing a very high energy photon
ATF lasers compare favorably to ones used in literature
  Keldysh parameter indicates ratio of photoionization to tunnel ionization (smaller is better for HHG)
  Typical is order
  ATF Ti:sapphire: , 800 nm good for EUV
  ATF CO2: , 9.2 μm good for X-rays
Popmintchev, Nat. Photonics 4, 828 (2010)
Popmintchev, Science 336, 1287 (2012)

## Slide 9: Plans for next year
Examine other ionic liquids
  Ex: deuterated EMIM DCA to generate ~1390 nm from 1064 nm
Employ DFG to produce the seed and pump wavelengths
  DFG crystal acquired for 4.5 μm, pending delivery for 9.2 μm
Demonstrate HHG capability with Ti:sapphire (800 nm  ~30 nm)
Produce first X-rays with CO2 laser (9.2 μm  ~1 nm)
Pildschun, Opt. Mater. Express 7, 1122-1130 (2017)
Deuteration pushes absorption bands deeper into IR
Kupfer, Phys. Rev. Applied 19, 014052 (2023)
HHG gas cell chamber
Spectrum of a potentially interesting IL
Accelerator Facilities Division

## Slide 10: Products delivered
Journal Publications:
R. Kupfer, F. Wang, J. F. Wishart, M. Babzien, M. N. Polyanskiy, I. V. Pogorelsky, T. Rao, L. Cultrera, N. Vafaei-Najafabadi, M. A. Palmer. “Raman Wavelength Conversions in Ionic Liquids” – Phys. Rev. Applied 19, 014052 (2023)
Conference Presentations:
W. Li, R. Kupfer, F. Wang, J. Wishart, M. Babzien, M. Polyanskiy, I. Pogorelsky, T. Rao, L. Cultrera, N. Vafaei-Najafabadi, M. Palmer, “Raman-based Wavelength Conversion for Seeding and Optical Pumping of CO2 Laser Amplifiers”, Advanced Accelerator Concepts Workshop (AAC), Long Island, NY (USA), November 6–11, 2022
Thank you for your attention!
https://www.bnl.gov/newsroom/news.php?a=120998
Accelerator Facilities Division

## Slide 11: Backup slides
Accelerator Facilities Division

## Slide 12: EMIM DCA transmission spectrum
Problem for using Nd:YAG fundamental
Absorption peak from overtones of aliphatic C-H bonds
Deuteration should shift this peak without affecting the Stokes shift, which comes from C-N triple bonds
Accelerator Facilities Division

## Slide 13: HHG Feasibility for CO2
Simple model of HHG yield for unit interaction area and unit time given by equation
We can compare to Popmintchev, Science 336, 1287 (2012), using a 3.9 μm pump, where we target the same harmonic wavelength (~1 keV)
  Their yield was photons/shot in a bandwidth around 1 keV
goes as , but the peak power of the CO2 laser is much higher with a longer pulse length, and the optimal phase matching intensity is lower, so the interaction area is 20 times larger and the interaction time is also 20 times longer, resulting in a higher overall yield for the CO2 laser
Primary challenge will be developing a gas cell that can support the necessary pressure (several atm)
Accelerator Facilities Division

## Slide 14: Experimental goals
Commonly available high energy/ultrashort lasers are limited to specific wavelengths
Problem is exacerbated for wavelengths far outside UV-NIR
We want ways to convert from commonly available wavelengths to (ideally) arbitrary wavelengths
Primary targets: MIR-LWIR and EUV
Photo credit: Edmund Optics
Commonly available laser wavelengths
Accelerator Facilities Division

## Slide 15: Slides for Program Advisory Committee

## Slide 16
Configuration | Parameter | Units | Typical Values | Comments | Requested Values
CO2 Regenerative Amplifier Beam | Wavelength | mm | 9.2 | Wavelength determined by mixed isotope gain media | 
 | Peak Power | GW | ~3 |  | 
 | Pulse Mode | --- | Single |  | 
 | Pulse Length | ps | 2 |  | 
 | Pulse Energy | mJ | 6 |  | 
 | M2 | --- | ~1.5 |  | 
 | Repetition Rate | Hz | 1.5 | 3 Hz also available if needed | 
 | Polarization | --- | Linear | Circular polarization available at slightly reduced power | 
CO2 CPA Beam | Wavelength | mm | 9.2 | Wavelength determined by mixed isotope gain media | 9.2
Note that delivery of full power pulses to the Experimental Hall is presently limited to Beamline #1 only. | Peak Power | TW | 5 | ~5 TW operation will become available shortly into this year’s experimental run period. A 3-year development effort to achieve >10 TW and deliver to users is in progress. | 
 | Pulse Mode | --- | Single |  | 
 | Pulse Length | ps | 2 |  | 2
 | Pulse Energy | J | ~5 | Maximum pulse energies of >10 J will become available within the next year | 5
 | M2 | --- | ~2 |  | 
 | Repetition Rate | Hz | 0.05 |  | 
 | Polarization |  | Linear | Adjustable linear polarization along with circular polarization can be provided upon request | 
CO2 Laser Requirements

## Slide 17
Ti:Sapphire Laser System | Units | Stage I Values | Stage II Values | Comments | Requested Values
Central Wavelength | nm | 800 | 800 | Stage I parameters are presently available and setup to deliver Stage II parameters should be complete during FY22 | 800
FWHM Bandwidth | nm | 20 | 13 |  | 
Compressed FWHM Pulse Width | fs | <50 | <75 | Transport of compressed pulses will initially include a very limited number of experimental interaction points. Please consult with the ATF Team if you need this capability. | 75
Chirped FWHM Pulse Width | ps | 50 | 50 |  | 
Chirped Energy | mJ | 10 | 200 |  | 
Compressed Energy | mJ | 7 | ~20 | 20 mJ is presently operational with work underway this year to achieve our 100 mJ goal. | 15
Energy to Experiments | mJ | >4.9 | >80 |  | 
Power to Experiments | GW | >98 | >1067 |  | 
Other Experimental Laser Requirements
Nd:YAG Laser System | Units | Typical Values | Comments | Requested Values
Wavelength | nm | 1064 | Single pulse | 
Energy | mJ | 5 |  | 
Pulse Width | ps | 14 |  | 
Wavelength | nm | 532 | Frequency doubled | 
Energy | mJ | 0.5 |  | 
Pulse Width | ps | 10 |  | 

## Slide 18: Special Equipment Requirements and Hazards
CO2 Laser
  We will require a long focal length focusing optic in the CO2 transport line for HHG
Ti:Sapphire and Nd:YAG Lasers
  We will be running the ionic liquid conversion experiment in parallel with Ti:Sapphire operations.
Hazards & Special Installation Requirements
  We will require a vacuum chamber and associated pumping to be installed in the CO2 room for the HHG gas cell. The gas cell itself will be fed with lecture bottles.

## Slide 19: Experimental Time Request
Capability | Setup Hours | Running Hours
Electron Beam Only |  | 
Laser* Only (in Laser Areas) | 80 (1 week early in year, 1 week late in year) | 80 (1 week early in year, 1 week late in year)
Laser* + Electron Beam |  | 
CY2023 Time Request
Capability | Setup Hours | Running Hours
Electron Beam Only |  | 
Laser* Only (in Laser Areas) | 80 | 80
Laser* + Electron Beam |  | 
* Laser = Near-IR or LWIR (CO2) Laser
Total Time Request for the 3-year Experiment (including CY2023-25)