## Slide 1: 25th Annual Accelerator Test Facility (ATF) Users' Meeting NP-312796: Two-color Injection of Bright Electron Beams
March 1st, 2023
N. Vafaei-Najafabadi1,2*, W. Li1, I. Petrushina2, R. Zgadzaj3, M. Downer3, A. Gaikwad2, B. Romasky2, E. Trommer2, A. Cheng2, R. Samulyak2, A. Farrell4, C. Zhang4, Y. Wu4, C. Joshi4, M. Babzien1, M. Polyanskiy1, I. Pogorelsky1, M. Palmer1
1Brookhaven National Laboratory, 2Stony Brook University,
3University of Texas at Austin, 4UCLA, *PI
Accelerator Facilities Division
Funding Source: DOE HEP DE-SC0014043
NSF 2238840
CORI @ NERSC under contract DE-AC02-05CH11231
SEAWULF @ Stony Brook University

## Slide 2: LWIR-driven laser wakefield acceleration
A laser driver with creates fully blown out LWFA in the “bubble regime”
Strength of ponderomotive force scales with , so LWIR drivers can reach with modest intensities (at ~20 TW power)
can be reached by and LWIR laser without triggering self-injection in LWFA*
Bubble created by LWIR driver can be >100 µm, providing the ability for precise alignment of multiple beams with respect to the bubble
P. Kumar, Physics of Plasmas, 28, 013102 (2021)
,
P=20 TW,
𝜏=0.5 ps,
cm-3
* See A. Jain, Proceedings of AAC 2022
Accelerator Facilities Division

## Slide 3: Two-color ionization injection
Yu, PRL 112, 125001 (2014)
Schroeder, European Conference on Lasers and Electro-Optics (2015)
Schroeder, PRSTAB 17, 101301 (2014)
A second laser can trigger ionization injection in the wakefield driven by the LWIR laser, creating a high-quality beam
Drive laser needs large to form plasma wakefield, but we want low to avoid prematurely ionizing the gas
Injector laser needs high to ionize the gas, but low to avoid disturbing the plasma
ATF is ideally suited for this experiment:
  ATF CO2 :driver
  ATF Ti:Sapphire: injector
Low emittance
Excellent phase space
Very intense, small
Less intense, large
Accelerator Facilities Division

## Slide 4: Trapping condition for electrons
Ideal Trapping Scenario
P~20 TW ps
Current Scenario
P~5 TW ps
cm-3
mm
cm-3 : to create a bubble larger than the laser
: too small for trapping
X.L. Xu, et al., PRSTAB, 17, 061301 (2014)
A. Jain, private communication
Accelerator Facilities Division

## Slide 5: Ionization Injection with Current Laser Config
Accelerator Facilities Division

## Slide 6: Ponderomotive assistance
We can use the injector laser to help!
Ponderomotive force of injector laser at oblique angle accelerates the ionized electrons
The electrons have an initial momentum, lowering the necessary trapping potential
Zeng, New J. Phys. 22, 123003 (2020)
Note: driver is an e-beam, but the physics of injection is the same
Accelerator Facilities Division

## Slide 7: Ponderomotive assistance parameters
Trapping threshold depends strongly on angle of incidence
Optimal angle of incidence and magnitude of trapping threshold dependent on and , the laser aspect ratio
Zeng, New J. Phys. 22, 123003 (2020)
Accelerator Facilities Division
Trapping threshold as fraction of ponderomotive-free trapping threshold
Contours of constant
15 mJ
90 mJ
For ATF, f/1.5 focusing, (at 15 mJ),
At optimal angle

## Slide 8: Experimental setup (inherited from AE88)
LWIR pulse
NIR pulse
f/#1.5 focusing
f/#2 focusing
NIR focus diagnostic
Nozzle
LWIR focus diagnostic
Dipole
magnet
LANEX
Slit
Accelerator Facilities Division

## Slide 9: Experimental setup (new modifications)
LWIR pulse
NIR pulse
f/#1.5 focusing
f/#2 focusing
NIR focus diagnostic
Nozzle
LWIR focus diagnostic
Dipole
magnet
LANEX
Slit
AOI rotation
Pepperpot
Accelerator Facilities Division

## Slide 10: Experimental setup (new modifications)
LWIR pulse
NIR pulse
f/#1.5 focusing
f/#2 focusing
Nozzle
LWIR focus diagnostic
Dipole
magnet
LANEX
Slit
Pepperpot
Accelerator Facilities Division

## Slide 11: Proposed measurements
Measure dependence of yield on angle of incidence, drive laser intensity, and injector laser intensity: confirmation that ponderomotive assistance is occurring
Measure dependence of emittance on angle of incidence, drive laser intensity, and injector laser intensity: confirmation of beam quality and finding optimal beam brightness
Zeng, New J. Phys. 22, 123003 (2020)
Yu, PRL 112, 125001 (2014)
Accelerator Facilities Division

## Slide 12: Expected experimental parameters
Expected gradient >1 GeV/m = 1 MeV/mm
Expected electron energy 5-10 MeV (~5 mm gas jet)
Expected electron emittance <1 mm-mrad (number obtained in Zeng, New J. Phys. 22, 123003, 2020 simulation)
High levels of Kr ionization is expected
Ionization of Krypton
N. Vafaei-Najafabadi, Proceedings of AAC 2022

## Slide 13: Emittance measurement
Need a single-shot measurement due to shot-to-shot fluctuations
Pepperpot is well-established method used in previous LWFA experiments
Intercept beam with a grid of holes and measure the size, shape, and spacing between the transmitted beamlets to retrieve transverse phase space
Accelerator Facilities Division
Manahan, New J. Phys. 16, 103006 (2014)
Brunetti, Phys. Rev. Lett. 105, 215007 (2010)

## Slide 14: Optional: Electron Beam as Probe
Linear focusing force in a bubble: (wakefield theory suggests )
For cm-3, focal length is ~3 cm
Both lasers can drive plasma waves, allowing for precise alignment between the laser pulses

## Slide 15: Conclusion
Two-color ionization injection has been shown in simulation to produce high quality electron beams
Ponderomotively assisted injection allows us to conduct the first two-color ionization injection experiments with the potential for low-emittance beam generation
Stepping stone towards producing ultra-low emittance, high brightness beams in a colinear configuration after ATF CO2 upgrades to >15 TW
Accelerator Facilities Division

## Slide 16: Backup slides
Accelerator Facilities Division

## Slide 17: Slides for Program Advisory Committee

## Slide 18
Parameter | Units | Typical Values | Comments | Requested Values
Beam Energy | MeV | 50-65 | Full range is ~15-75 MeV with highest beam quality at nominal values | nominal
Bunch Charge | nC | 0.1-2.0 | Bunch length & emittance vary with charge | nominal
Compression | fs | Down to 100 fs (up to 1 kA peak current) | A magnetic bunch compressor available to compress bunch down to ~100 fs. Beam quality is variable depending on charge and amount of compression required. NOTE: Further compression options are being developed to provide bunch lengths down to the ~10 fs level | Max compression available
Transverse size at IP (s) | mm | 30 – 100 (dependent on IP position) | It is possible to achieve transverse sizes below 10 um with special permanent magnet optics. | 1 mm
Normalized Emittance | mm | 1 (at 0.3 nC) | Variable with bunch charge | 1 um
Rep. Rate (Hz) | Hz | 1.5 | 3 Hz also available if needed | 0.02 Hz (limited by CO2)
Trains mode | --- | Single bunch | Multi-bunch mode available. Trains of 24 or 48 ns spaced bunches. | Single Mode
Electron Beam Requirements

## Slide 19
Configuration | Parameter | Units | Typical Values | Comments | Requested Values
CO2 Regenerative Amplifier Beam | Wavelength | mm | 9.2 | Wavelength determined by mixed isotope gain media | 
 | Peak Power | GW | ~3 |  | 
 | Pulse Mode | --- | Single |  | 
 | Pulse Length | ps | 2 |  | 
 | Pulse Energy | mJ | 6 |  | 
 | M2 | --- | ~1.5 |  | 
 | Repetition Rate | Hz | 1.5 | 3 Hz also available if needed | 
 | Polarization | --- | Linear | Circular polarization available at slightly reduced power | 
CO2 CPA Beam | Wavelength | mm | 9.2 | Wavelength determined by mixed isotope gain media | 9.2
Note that delivery of full power pulses to the Experimental Hall is presently limited to Beamline #1 only. | Peak Power | TW | 5 | ~5 TW operation will become available shortly into this year’s experimental run period. A 3-year development effort to achieve >10 TW and deliver to users is in progress. | >5
 | Pulse Mode | --- | Single |  | Single
 | Pulse Length | ps | 2 |  | 2 (phase I) <1 (phase II)
 | Pulse Energy | J | ~5 | Maximum pulse energies of >10 J will become available within the next year | 5
 | M2 | --- | ~2 |  | 
 | Repetition Rate | Hz | 0.05 |  | 0.05
 | Polarization |  | Linear | Adjustable linear polarization along with circular polarization can be provided upon request | linear
CO2 Laser Requirements

## Slide 20
Ti:Sapphire Laser System | Units | Stage I Values | Stage II Values | Comments | Requested Values
Central Wavelength | nm | 800 | 800 | Stage I parameters are presently available and setup to deliver Stage II parameters should be complete during FY22 | 800
FWHM Bandwidth | nm | 20 | 13 |  | 
Compressed FWHM Pulse Width | fs | <50 | <75 | Transport of compressed pulses will initially include a very limited number of experimental interaction points. Please consult with the ATF Team if you need this capability. | 60
Chirped FWHM Pulse Width | ps | 50 | 50 |  | 
Chirped Energy | mJ | 10 | 200 |  | 
Compressed Energy | mJ | 7 | ~20 | 20 mJ is presently operational with work underway this year to achieve our 100 mJ goal. | 90
Energy to Experiments | mJ | >4.9 | >80 |  | 
Power to Experiments | GW | >98 | >1067 |  | 
Other Experimental Laser Requirements
Nd:YAG Laser System | Units | Typical Values | Comments | Requested Values
Wavelength | nm | 1064 | Single pulse | 
Energy | mJ | 5 |  | 
Pulse Width | ps | 14 |  | 
Wavelength | nm | 532 | Frequency doubled | 
Energy | mJ | 0.5 |  | 
Pulse Width | ps | 10 |  | 

## Slide 21: Special Equipment Requirements and Hazards
CO2 Laser
  No specialty configurations required.
Ti:Sapphire and Nd:YAG Lasers
  No specialty configurations required.
Hazards & Special Installation Requirements
  We will require the installation of a 3.6 kG dipole spectrometer in the experimental chamber.

## Slide 22: Experimental Time Request
Capability | Setup Hours | Running Hours
Electron Beam Only |  | 
Laser* Only (in Laser Areas) | 40 | 80
Laser* + Electron Beam |  | 
CY2023 Time Request
Capability | Setup Hours | Running Hours
Electron Beam Only |  | 
Laser* Only (in Laser Areas) | 120 | 240
Laser* + Electron Beam |  | 
* Laser = Near-IR or LWIR (CO2) Laser
Total Time Request for the 3-year Experiment (including CY2023-25)

## Slide 23: Ponderomotive assistance at ATF
mm
, , , ps, , , mm
Low density gas: CO2 laser strong enough to be in blowout regime
, not quite enough to trap electrons
Accelerator Facilities Division

## Slide 24: Higher density
, , , ps, , , mm
3x higher density: CO2 laser starts to become self-modulated
, close to the trapping threshold
Critically, there is space at the back of the bubble for the injected electrons
Current ATF laser parameters sufficient for ponderomotively assisted ionization injection
Accelerator Facilities Division

## Slide 25: Ti:sapphire parameters
(f/1.5 focusing, conservative M2 of 2)
Accelerator Facilities Division