## Slide 1: Radiofrequency emission from 9.2-micron short pulsed laser in gases and on solid targets
Erin Thornton12, Jennifer Elle2*, Andy Goers3, Brian Gibbons3
1 March 2023
Approved for public release; distribution is unlimited. Public Affairs release approval #AFRL-2023-0067
1. University of North Texas, 2. Air Force Research Laboratory, 3.Applied Physics Laboratory at Johns Hopkins University, * Principal Investigator
Funding: AFRL Program Funds and the Office of Naval Research

## Slide 2: Experimental Goals
Approved for public release; distribution is unlimited. Public Affairs release approval # AFRL-2023-0067
Ultrashort pulse lasers(USPLs) have been used to generate atmospheric filaments that are a novel source of ultra-broadband microwave generation(10s GHz)
A model has been developed describing the generation of the RF by atmospheric filaments.
Goal of the Brookhaven CO2 experiment:
  Better characterize Far IR generated plasmas and its ultra-broadband RF emission
  Use data to expand the model to include joule class, ps, far-IR driven plasma filaments
  Solid targets
BNL CO2
λ = 9.2 microns
Notes: We’ve been interested in better understanding the RF to use it as a non-interfering method of filament diagnostic as well as means of remote sensing via microwave spectroscopy.
*our model was primarily developed using fs/mj near ir pulses

## Slide 3: Current understanding of microwave generation
Approved for public release; distribution is unlimited. Public Affairs release approval # AFRL-2023-0067
  Radial current densities arise from ionized electrons gaining energy from the laser pulse, collide in electron-neutral collisions, and return due to restoring force of ions in plasma channel.
  Radial current densities drive a surface wave on plasma channel.
  Surface wave builds coherently along the length of the plasma and ejects at the end.
Hypothesis
Longer wavelengths were predicted to drive hotter electrons through greater ponderomotive heating, Up λ2.
Hotter, denser plasmas were predicted to result in much higher magnitude of RF production.
A. Englesbe et al., “Ultrabroadband microwave radiation from near- and mid-infrared laser-produced plasmas in air,” Phys. Rev. A, vol. 104, no. 1, p. 013107, Jul. 2021, doi: 10.1103/PhysRevA.104.013107.

## Slide 4: Experimental set up
Approved for public release; distribution is unlimited. Public Affairs release approval # AFRL-2023-0067
ICCD camera
Angular scans are important as RF amplitude and frequency content vary with angle of emission. For air plasmas RF is radially polarized in a forward conical direction.
Notes: For much of this talk we will be comparing again the COMET laser at LLNL. Pulse duration, energy, and focusing set up were comparable to BNL experiment

## Slide 5
Approved for public release; distribution is unlimited. Public Affairs release approval # AFRL-2023-0067
Air Plasma Characteristics
Wavelength: 9.2 microns
Pulse duration: 2 ps
Energy: 3.08 ± .875 J
Rep Rate: .05Hz (essentially single shot)
F/N = 44 (Focused with 2 4m lenses)
Actual focus: 1.97 m from lens
Unamplified beam waist: ~.5mm FWHM
Visible plasma lifetime = ~2.7ns
Horizontally polarized
Average Length(1/e2) = 17.4 ± 1.4 cm
Average Width(1/e2) = 2.89 ± .40 mm
Direction of laser propagation

## Slide 6: Signal amplitude
Approved for public release; distribution is unlimited. Public Affairs release approval # AFRL-2023-0067
Compared to COMET laser (1.053 micron, 4.75 ps, 5J) the microwave signal has increased by nearly an order of magnitude for all angles off laser axis. Since power goes as V2 this represents a 100 time increase in power

## Slide 7: Frequency resolved electric field
Approved for public release; distribution is unlimited. Public Affairs release approval # AFRL-2023-0067
Frequency resolved electric field spectrum of 1.053-micron laser at 10 degrees off the laser axis
Frequency resolved electric field spectrum of 9.2-micron laser at 10 degrees off laser axis
The magnitude increase in signal occurs across measured frequencies as well.

## Slide 8: Signal as a function of pressure
Approved for public release; distribution is unlimited. Public Affairs release approval # AFRL-2023-0067
Suggests electron-neutral collisions do not result in signal dampening for Far-IR pulses nearly to the extent it does for Near-IR.
[1] A. Englesbe et al., “Gas pressure dependence of microwave pulses generated by laser-produced filament plasmas,” Opt. Lett., vol. 43, no. 20, p. 4953, Oct. 2018, doi: 10.1364/OL.43.004953.
Notes: 9.2 micron gets 4 fold increase, 800 nm sees 40 fold increase

## Slide 9: Air vs N2
Approved for public release; distribution is unlimited. Public Affairs release approval # AFRL-2023-0067
N2 at 200 torr
Air at 200 torr
Length:
Air : 21.1 ± 4 cm
N2 : 28.3 ± 4.6 cm
Spectrum generated by plasma in dry N2 gas did not yield a significant difference in spectrum.
Pure N2 did not remove the brighter breakdown/avalanche spots within the plasma
Electric field spectrum of plasma produced in air and N2

## Slide 10
Approved for public release; distribution is unlimited. Public Affairs release approval # AFRL-2023-0067
Solid Target Plasma
Angle off normal incidence(deg) | Area as measured by light on target (cm2) | Area as measured by damage spot on plexiglass(cm2)
0 | .731 | .239
10 | .743 | .243
25 | .807 | .264
45 | 1.03 | .338
.965 cm
Plasma decay time: 14 ns (as measured by visible fluorescence)

## Slide 11: Experimental Setup
Approved for public release; distribution is unlimited. Public Affairs release approval # AFRL-2023-0067
axis
axis
axis
Angle Scan
Target
Fast Oscilloscope
1-18 GHz Horn
18-33 GHz Horn
AOI
axis
Laser
Normal

## Slide 12: Spectra of all sampled lasers
Approved for public release; distribution is unlimited. Public Affairs release approval # AFRL-2023-0067
λ (microns) | Energy (joules) | Duration (fs)
0.8 | .04 | 50
1.0 | .03 | 1300
9.2 | 3 | 2000
10.6 | .01 | 3000
Orders of magnitude improvement across all frequencies achieved with BNL laser
AAU
A.U.

## Slide 13
Approved for public release; distribution is unlimited. Public Affairs release approval # AFRL-2023-0067
axis
axis
axis
Behind
Perpendicular
Target
Fast Oscilloscope
Dual Polarization Horn
Above
AOI
axis
Laser
Normal
Ch. 3
Ch. 1
Ch. 3
Ch. 1
Perpendicular
Behind
Above
Ch. 3
Ch. 1
to laser polarization
Polarization
Position
to laser propagation
to laser polarization

## Slide 14: Sum of Frequency Content for Alumina
Approved for public release; distribution is unlimited. Public Affairs release approval # AFRL-2023-0067
AOI (°)
AOI (°)
Ratio
Results from this experiment suggest a two dipole radiation patterns (one perpendicular to target surface and one parallel to target surface) for alumina.
This has prompted new series of investigation with AFRL’s laser and have been useful insights when building a solid target model.
A.U.

## Slide 15: Moving forward
Approved for public release; distribution is unlimited. Public Affairs release approval # AFRL-2023-0067
Comparing experimental data to current model shows model underestimating resulting RF by nearly a factor of 2, likely due insufficient calculation of electron temperature. (laser heating was not a significant factor for fs scale pulses)
Work is being done currently developing a better model the heating of the electrons due to the ps scale pulse/far-IR.
Microwave modeling is underway to better capture the radiation patterns generated by the ejection and surface currents for solid target experiments.

## Slide 16: Products delivered
“Ultrashort Pulse Laser Effects Testing at JHU/APL” presentation at DEPS Systems Symposium in La Jolla, CA-November 2022
“Radio Frequency Emission from 9.2-micron Short Pulsed Laser in Gases” Abstract submitted for presentation at DEPS Science and Technology Symposium in San Antonio, TX- April 2023
“9.2 –Micron Short Pulse Laser Generated RF from Solid Target Interactions” Abstract submitted for presentation at DEPS Science and Technology Symposium in San Antonio, TX- April 2023

## Slide 17: Supercontinuum Generation
Approved for public release; distribution is unlimited. Public Affairs release approval # AFRL-2023-0067
Sneak peak for 2024 experimental campaign at BNL: supercontinuum generation study in collaboration with ARL
Visible light produced by 9.2-micron source!
Notes: First taste supercontinuum generation, currently unsure if true supercontinuum or just harmonic generation