## Slide 1: Ionization Currents and Secondary Radiation from Two-Color Pulses at Long Laser Wavelengths Proposal # 312798 Funding Status: NRL Base Program, Received
Alexander Englesbe, Jessica Peña, Michael Helle, Daniel Gordon
Plasma Physics Division, Naval Research Laboratory

## Slide 2: Controlling Tunneling Ionization of Air with Two-Color Pulses
Optical field ionization by intense laser pulses occurs in the tunneling or multiphoton regime – Keldysh theory
For ionization of atmospheric air, traditional NIR sources ionize via multiphoton
Long wavelengths are needed to drive tunneling ionization in air
The liberation of electrons constitutes an ionization current, whose time dependence can be step-like (tunneling) with each laser field maximum, or vary slowly with the laser envelope (multiphoton)
The relative phase of a two-color pulse changes the shape of the laser electric field waveform, and thus the ionization currents
Input two-color laser pulse
Air plasma
Terahertz radiation
Microwave radiation
Brunel harmonics
Δt
Δθ = 0
Δθ = π/2
Relative phase (intra-cycle)
Envelope overlap (multiple cycles)

## Slide 3: Ionization Currents Determine Secondary Radiation
Understand how ionization physics of air changes as a function of laser wavelength
Use microwave, THz, and laser harmonics that radiate as a consequence of ionization currents (secondary radiation) to infer ionization physics
  Amplitude and frequency spectrum
Identify generation mechanism of microwave radiation with two-color pulses
Link early and late plasma lifetime by combining secondary radiation measurements with plasma diagnostics
  Interferometry and optical emission spectroscopy
Binding
potential
electron
Binding Potential
electron
Tunneling
Multiphoton
I. Babushkin, J. Mod. Opt. 64(10), 1078 (2017).
Black line = ionization rate

## Slide 4: Compare Relative Phase Dependence of Secondary Radiation
Two-color scheme is common to generate THz in air, but doing it with LWIR fundamental would be unique (no publications yet as far as we know)
  Two-color NIR is in multiphoton regime, but Keldysh theory doesn’t neatly apply. LWIR would be far into tunneling regime
Two-color microwave generation is different from single-color, but mechanism is unclear. Going to tunneling regime may clarify physics.
Input two-color laser pulse
Air plasma
Terahertz radiation
Microwave radiation
Brunel harmonics
Microwave Signal (V)
THz Signal (V)

## Slide 5: Compare Relative Phase Dependence of Secondary Radiation
Two-color scheme is common to generate THz in air, but doing it with LWIR fundamental would be unique (no publications yet as far as we know)
  Two-color NIR is in multiphoton regime, but Keldysh theory doesn’t neatly apply here. LWIR would be far into tunneling regime
Two-color microwave generation is different from single-color, but mechanism is unclear. Going to tunneling regime may clarify physics.
Input two-color laser pulse
Air plasma
Terahertz radiation
Microwave radiation
Brunel harmonics

## Slide 6: Long Wavelength Pulses Allow Additional Comparison with Brunel Harmonics
In the tunneling regime, the ionization current efficiently generates harmonics via Brunel mechanism
Brunel is not the same as recollision-driven high harmonic generation
  Two-color NIR pulses do not generate Brunel harmonics, would be strongly absorbed in air if they did
Input two-color laser pulse
Air plasma
Terahertz radiation
Microwave radiation
Brunel harmonics
I. Babushkin, J. Mod. Opt. 64(10), 1078 (2017).
Two-color field
Time
Tunneling ionization current
Tunneling
Multiphoton
Harmonic Spectrum

## Slide 7: Experimental Goals and Setup
  Complete dataset = secondary radiation + plasma diagnostics as a function of two-color relative phase for single laser pulse format
  Deploy single-shot, triggerable measurements of:
    Microwave radiation
    THz radiation
    Brunel harmonics
    Plasma interferogram
    Plasma optical emission spectrum
  Repeat experiment on NRL lasers: NIR (Ti:sapphire),
  SWIR + MWIR (OPA)
  Use relative phase dependence for quantitative points of comparison for simulations: SeaRay, CHMAIR/SPARC, and TurboWave
To folded wavefront interferometer
SHG crystal
(ZGP, AgGaSe2)
Input LWIR fundamental
Time delay
compensator
Air plasma
Plasma emission collection optics
UV-VIS and NIR-SWIR imaging spectrometers for Brunel harmonics
Microwave D-dot probe
Terahertz spectrometer
Neutral/ionic emission with UV-VIS, NIR spectrometer
NIR interferometry probe

## Slide 8: Microwave Pulse Detection
Plasma currents radiate a broadband electromagnetic pulse that extends down to sub-GHz frequencies
Detect microwaves with a high-frequency d-dot probe, sensitive to fields up to 50 GHz
D-dot probe does not have a lower cutoff frequency unlike antenna
Useful info contained in relative waveform amplitude, and the real part of the frequency spectrum
D-dot probe
Fast oscilloscope
Photodiode trigger
Microwave Receiver

## Slide 9: Modulations in Microwave Frequency Spectrum are Physical
At the relative phase that maximizes microwave generation, we see very regular modulations of the microwave frequency spectrum
Have also seen modulations with SWIR and NIR pulses
Optimized amplitude is ~10X more peak power than single-color pulse
Mechanism that explains single-color microwaves does not account for the spectral modulations
Will modulations persist with tunneling ionization from LWIR driver?
NIR, femtosecond
SWIR, picosecond

## Slide 10: Modulations in Microwave Frequency Spectrum are Physical
At the relative phase that maximizes microwave generation, we see very regular modulations of the microwave frequency spectrum
Have also seen modulations with SWIR and NIR pulses
Will modulations persist with tunneling ionization from LWIR driver?
Mechanism that explains single color microwaves does not account for the spectral modulations
NIR, femtosecond
SWIR, picosecond

## Slide 11: Implement Single-Shot THz Electro-Optic Sampling
Want to look for changes in THz spectrum due to relative phase
Echelon-based electro-optic sampling obviates delay line scanning over many laser shots
Sample ~2 ps THz field at 10’s fs resolution over ~10 ps time window
Requires synchronized NIR laser pulses
Build our own at NRL, and thoroughly test before ATF experiments
LWIR beam
Polarizer
Combining optic
THz pulse
Polarizer
NIR probe
K.-Y. Kim, Opt. Lett. 32(14), 1968 (2007).
S. Teo, Rev. Sci. Inst. 86, 051301 (2015).
Image echelon through EO crystal on to camera
Echelons generate NIR beamlets
Read out THz waveform from intensity in boxes
Subtract CCD images with and without THz field
λ/4

## Slide 12: Spectrum of Brunel Harmonics Indicates Early Electron Dynamics
Need tunneling ionization to produce Brunel harmonics – cannot be done in air with NIR laser
The relative amplitudes and linewidths of the Brunel harmonics contain valuable information about electron behavior within laser field
Linewidths related to number of jumps in ionization current. Look for changes in linewidth with relative phase, and also look for trends with fundamental laser wavelength
Primarily use NIR-SWIR spectrometer in ATF experiments, but will also look at higher order harmonics in visible range
Harmonic Order | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14
Wavelength (μm) | 4.6 | 3.1 | 2.3 | 1.8 | 1.5 | 1.3 | 1.1 | 1.0 | 0.92 | 0.84 | 0.77 | 0.71 | 0.66
Number of “step-ups” in ionization current

## Slide 13: Spectrum of Brunel Harmonics Indicates Early Electron Dynamics
Relative phase relationship between THz and Brunel harmonics can be simulated using carrier-resolving solver – SeaRay
Difficult to discriminate low-order bound electron harmonics and Brunel harmonics
Focus of year 2 experiments will be comparing Brunel and recollision-driven harmonic generation in air
1.9 + 3.9 μm pulse Brunel harmonics vs. relative phase, Experiment
D. Jang, Optica 6(10), 1338 (2019).
1.9 μm
0.43 μm

## Slide 14: Plasma Diagnostics: Interferometry and Optical Emission Spectroscopy
Optical emission spectroscopy over large spectral range (e.g. 350-1100 nm) can give rough idea of electron kinetics
  Compare emission lines to two-color pulses at other fundamental wavelengths
  Population and decay of many excited states takes time period much longer than laser pulse, ionization currents
  Benchmark air chemistry using CHMAIR/SPARC
Interferometry to measure nominal plasma density and size:
  Input an accurate electron density into simulations
  If two-color field perturbs ionization rate in space and time, this may appear in interferogram fringes
  Transverse probing
NIR Plasma Emission Spectra

## Slide 15: Summary
Use the secondary radiation (microwaves, THz, and Brunel harmonics) to understand the role of ionization currents, and other potential collisional and collective charged particle dynamics excited by the two-color laser field.
Link early and late plasma characteristics with concurrent measurements of the plasma size, density, and optical emission spectrum.
Field single-shot diagnostics. Cameras for spectroscopy, interferometry, and oscilloscope for microwave receiver are triggerable. Need to build up echelon-based THz receiver.
Integrate LWIR results in comparison study with NIR, SWIR, MWIR wavelengths

## Slide 16
Configuration | Parameter | Units | Typical Values | Comments | Requested Values
CO2 Regenerative Amplifier Beam | Wavelength | mm | 9.2 | Wavelength determined by mixed isotope gain media | 
 | Peak Power | GW | ~3 |  | 
 | Pulse Mode | --- | Single |  | 
 | Pulse Length | ps | 2 |  | 
 | Pulse Energy | mJ | 6 |  | 
 | M2 | --- | ~1.5 |  | 
 | Repetition Rate | Hz | 1.5 | 3 Hz also available if needed | 
 | Polarization | --- | Linear | Circular polarization available at slightly reduced power | 
CO2 CPA Beam | Wavelength | mm | 9.2 | Wavelength determined by mixed isotope gain media | 9.2 microns
Note that delivery of full power pulses to the Experimental Hall is presently limited to Beamline #1 only. | Peak Power | TW | 5 | ~5 TW operation will become available shortly into this year’s experimental run period. A 3-year development effort to achieve >10 TW and deliver to users is in progress. | < 100 GW
 | Pulse Mode | --- | Single |  | Single
 | Pulse Length | ps | 2 |  | 2 ps
 | Pulse Energy | J | ~5 | Maximum pulse energies of >10 J will become available within the next year | ~ 100-150 mJ
 | M2 | --- | ~2 |  | 
 | Repetition Rate | Hz | 0.05 |  | 0.05
 | Polarization |  | Linear | Adjustable linear polarization along with circular polarization can be provided upon request | Linear
CO2 Laser Requirements

## Slide 17
Ti:Sapphire Laser System | Units | Stage I Values | Stage II Values | Comments | Requested Values
Central Wavelength | nm | 800 | 800 | Stage I parameters are presently available and setup to deliver Stage II parameters should be complete during FY22 | 800 nm
FWHM Bandwidth | nm | 20 | 13 |  | 
Compressed FWHM Pulse Width | fs | <50 | <75 | Transport of compressed pulses will initially include a very limited number of experimental interaction points. Please consult with the ATF Team if you need this capability. | ~ 50 fs
Chirped FWHM Pulse Width | ps | 50 | 50 |  | 
Chirped Energy | mJ | 10 | 200 |  | 
Compressed Energy | mJ | 7 | ~20 | 20 mJ is presently operational with work underway this year to achieve our 100 mJ goal. | < 7 mJ
Energy to Experiments | mJ | >4.9 | >80 |  | < 4 mJ
Power to Experiments | GW | >98 | >1067 |  | << 100 GW
Other Experimental Laser Requirements
Nd:YAG Laser System | Units | Typical Values | Comments | Requested Values
Wavelength | nm | 1064 | Single pulse | 
Energy | mJ | 5 |  | 
Pulse Width | ps | 14 |  | 
Wavelength | nm | 532 | Frequency doubled | 
Energy | mJ | 0.5 |  | 
Pulse Width | ps | 10 |  | 

## Slide 18
Parameter | Units | Typical Values | Comments | Requested Values
Beam Energy | MeV | 50-65 | Full range is ~15-75 MeV with highest beam quality at nominal values | 
Bunch Charge | nC | 0.1-2.0 | Bunch length & emittance vary with charge | 
Compression | fs | Down to 100 fs (up to 1 kA peak current) | A magnetic bunch compressor available to compress bunch down to ~100 fs. Beam quality is variable depending on charge and amount of compression required. NOTE: Further compression options are being developed to provide bunch lengths down to the ~10 fs level | 
Transverse size at IP (s) | mm | 30 – 100 (dependent on IP position) | It is possible to achieve transverse sizes below 10 um with special permanent magnet optics. | 
Normalized Emittance | mm | 1 (at 0.3 nC) | Variable with bunch charge | 
Rep. Rate (Hz) | Hz | 1.5 | 3 Hz also available if needed | 
Trains mode | --- | Single bunch | Multi-bunch mode available. Trains of 24 or 48 ns spaced bunches. | 
Electron Beam Requirements – Not Applicable

## Slide 19: Special Equipment Requirements and Hazards
Introduction of transmissive optics into LWIR beam:
  Second harmonic crystal
  Time delay compensator
  Half waveplate to co-polarize harmonics (needed if using Type 1 SHG)

## Slide 20: Experimental Time Request
Capability | Setup Hours | Running Hours
Electron Beam Only | N/A | 
Laser* Only (in Laser Areas) | 40 | 80
Laser* + Electron Beam |  | 
CY2023 Time Request
Capability | Setup Hours | Running Hours
Electron Beam Only |  | 
Laser* Only (in Laser Areas) | 80 | 160
Laser* + Electron Beam |  | 
* Laser = Near-IR or LWIR (CO2) Laser
Total Time Request for the 3-year Experiment (including CY2023-25)