## Slide 1: SLAC RPG Measurement of Ionizing Radiation from CO2 laser interactions at ATF
ATF User Meeting 3/1/2023
SLAC Team: S. Rokni, J. Liu, A. Rosenstrom, M. Santana, H. Tran
ATF Team: M. Palmer, K. Kusche, A. Simmonds, K. Roy, C. Schaefer, S. Harling, A. Emrick, L. Hammons, K. Yip

## Slide 2: Motivation
Increasing intensity of lasers will continue to push their operation into regimes where ionizing radiation can be generated
Current state of the art models rely on coupling Particle in Cell codes with Monte Carlo Radiation Transport Codes
In order to be sure models are producing reasonable estimate of ionizing radiation from the laser plasma interaction experimental benchmarks with a variety of laser parameters are needed.

## Slide 3: Laser-Induced Ionizing Radiation from Solid Targets
  Particle-in-Cell Code (EPOCH)
  Radiation Particle Transport Code (FLUKA)
  Calculate dose at ATF parameters (irradiance, energy/shot, number of shots, shielding geometry)
  Measurements of dose yields outside MEC & Titan target chambers
  Calculate dose yield (mSv/J at 1 m) outside 1 inch thick Al target chamber
  Additional sources for liquid targets and thin solid targets:
  High energy protons/ions (hazard of secondary neutrons)
  Calculated source term for solid target:
  spectrum (Maxwellian) and direction of electrons for given irradiance

## Slide 4: Previous Work and Publications: Laser-Induced Ionizing Radiation from Solid Targets
Previous Publications and SLAC Radiation Physics Notes:
T. Liang, PhD dissertation, Georgia Institute of Technology & SLAC, 2017
Liang, T., Bauer, J., Blaha, J., Cimeno, M., Ferrari, A., Liu, J., Rokni, S., and Woods, M., “Ionizing Radiation Measurements from Interaction of MEC Laser (0.7 J, 1019 W/cm2) with Cu and Ni Targets,” SLAC Radiation Physics Note, no. RP–14–23, pp. 1–22, 2014.
Liang, T., Bauer, J., Cimeno, M., Ferrari, A., Galtier, E., Granados, E., Lee, H. J., Liu, J., Nagler, B., Prinz, A., Rokni, S., Tran, H., and Woods, M., “Radiation Dose Measurements for High-Intensity Laser Interactions with Solid Targets at SLAC,” Radiation Protection Dosimetry, vol. 172, no. 4, pp. 346–355, 2016.
Liang, T., Bauer, J., Cimeno, M., Ferrari, A., Galtier, E., Granados, E., Liu, J., Nagler, B., Prinz, A., Rokni, S., Tran, H., and Woods, M., “Measurements of High-Intensity Laser Induced Ionizing Radiation at SLAC,” SLAC Publication, no. SLAC-PUB-15973, pp. 1–18, 2014.
Liang, T., Bauer, J., Liu, J., and Rokni, S., “Bremsstrahlung Dose Yield for High-Intensity Short-Pulse Laser-Solid Experiments,” Radiation Protection Dosimetry, 2016.
Liang, T., Bauer, J., Liu, J., and Rokni, S., “Development of a Photon Dose Yield Model for Laser-Solid Interaction by Coupling EPOCH and FLUKA,” SLAC Radiation Physics Note, no. RP–16–14, pp. 1–28, 2016.
Experimental Configuration of MEC Hutch at SLAC
Dose Measurements inside of the MEC Hutch at SLAC

## Slide 5: Applying Previous Work to ATF
T. Liang, J. Bauer, J. Liu & S. Rokni, Bremsstrahlung Dose Yield for High-Intensity Short-Pulse Laser-Solid Experiments”. In: Radiation Protection Dosimetry 175 (3 2017), pp. 304–312. doi: 10.1093/rpd/ncw325.
Calculated and measured dose yields agree
ATF Operational Range :
Upgrade: 2 ps pulse and 20 J
Good agreement between model and experimental measurements for 800 nm and 1053 nm lasers

## Slide 6: Previous Work: Motivation
Goals:
  Directly measure the x-ray source field within the vacuum chamber
  Apply a thin Al filter (thickness of 3.35 mm) to distinguish low energy (< few 10s of keV) x-ray dose from high energy dose
  Obtain measurements near likely ultimate parameters for B820 operation to aid future analysis of upgrades [extrapolate to lower fluences for radiation safety analysis]
6
OAP
target
sphere
lens
IR camera
Plasma Shutter
Optical transport
Interaction Chamber
TLDs
Test sphere 6” diam.; windows are for placing TLDs around a target
laser
TLD
TLD
TLD
TLD
Slide adapted from M. Palmer and ATF team

## Slide 7: Previous Work: Experimental Study Parameters
Relevant laser parameters for test dose rate estimate:
Laser pulse length 2.3 ps
Laser pulse energy 5 J
Laser pulse rep rate 0.03 Hz
Energy fluence @ 5 J 6.25E5 J/cm2
Laser intensity @5J and 2.3 ps 2.7E17 W/cm2
Plasma kTH (Ref 1) 976 keV
Hard X-ray energy / laser energy (Ref 1) 0.011 (range is 0.00737 to 0.0165)
Ref 1: Physical Review A Volume 32, Number 6 December 1985, Superhot-X-Ray and -Electron Transport in High- Intensity CO2-Laser-Plasma Interactions, G. D. Enright and N. H. Burnett.
Designed to significantly exceed the present and potential upgrades to operational configuration of the plasma shutter!!
Slide adapted from M. Palmer and ATF team

## Slide 8: Previous Work: Results
Nanodot Serial # | Rad in an hour (108 laser pulses in an hour) | Location
DB08650715G | 1.042 | 1a
DB086529564 | 1.241 | 2a
DB08653362M | 2.978 | 3a
DB08652850I | 16.03 | 4a
DB08630542R | 492.2 | 1
DB08630517K | 860.1 | 2
DB08652923D | 927.6 | 3
DB08650691I | 2,768 | 4
Slide adapted from M. Palmer and ATF team

## Slide 9: Proposed Experiments
Conduct passive and active spectral and dose rate measurements of the radiation that is produced from a solid target interaction at several intensities and angles
  This will enable a comparison of the model produced using 800 nm to a very different wavelength (10600) to show the wide range of applicability for the model and scaling for use in radiation protection assessments
Stacked dosimeters used for passive spectral measurements
Ambient dose Ion chamber for active dose measurements

## Slide 10: Application at the ATF
This work would support analysis of fault conditions in the ATF plasma shutter
mrem/laser shot
Plan View
The maximum dose rate at the exclusion barrier would result in 200 shots before the 100 mrem limit is reached
0.5 mrem/laser shot
0.5 mrem/laser shot
0.5 mrem/laser shot

## Slide 11: Conclusion
Coupled PIC and Monte Carlo Radiation Transport codes are useful tools in developing mitigations for ionizing radiations produced by high intensity laser interactions
In order to reliably predict the dose to personnel using state of art models, benchmarking of the angular distribution, radiation spectra, and dose rate are needed over a wide range of laser conditions