## Slide 1: EIC Far-Backward Component Radiation Damage Study
A. Kowalewska1, J. Nam2, K. Piotrzkowski1, B. Surrow2
1. AGH University of Science and Technology, Krawkow
2. Temple University, Philadelphia

## Slide 2: SR Study
Recap
  SR study based on SynRad+
  https://indico.bnl.gov/event/17867/
  Beam/Field info
    H. Witte et al., DOI: 10.18429/JACoW-IPAC2021-WEPAB003
    Available in the EIC standard platform
    Latest electron beam lattice info, courtesy of Charles Hetzel (EIC/BNL).
  Geometry ready for use with high flexibility on EIC platform.
    Enables studies of optimal filter specifications.
    Tests of various detector configurations.

## Slide 3: Relevant Far Backward Geometry
Geometry from November
2 X Focusing/defocusing Quad Poles (Q1eR, Q2eR).
2 X Dipoles (B2AeR, B2BeR) further separate the outgoing electrons from the incoming hadrons.
Low- taggers
calorimeters with a separating dipole and 2 electron trackers.
Additional luminosity monitor with direct photons.
  Not implemented in EIC platform, although relevant parameters exist.
Q1eR
Q2eR
B2AeR
B2BeR
Taggers
Exit
window
SPEC
Direct
Photon

## Slide 4: Beam/Field
Electron beam
  18 GeV electron beam at 250 mA current.
  Further beam properties need to be implemented (emittance, energy spread, tail info, etc.)
Magnetic Field
  B2AeR/B2BeR
    0.192/0.238T dipoles.
    Located at 10.5/13.275m downstream.
  Q1eR/Q2eR
    -13.3/12.1(T/m) focusing/defocusing quad poles.
    At 6.2/8.3m.

## Slide 5: Update (WIP)
Photon distribution on exit window
Power/Flux spectrum
Flux along vertical direction
Power along vertical direction
Preliminary sanity study in progress.
  SR at the photon exit window
  Only the two dipoles included with ideal beam condition.
  Resulting power/flux seems not too far off from previous studies (). (https://indico.bnl.gov/event/12197/)
SR generated with
at
through the two dipoles

## Slide 6: Update (WIP)
Power/Flux spectrum
Flux along vertical direction
Power along vertical direction
Wishlist before Jan meeting
  Realistic beam info
  Geometry properties (naïve scattering)
  Direct Photon Calorimeter (at least two specifications)
  SR in the low- taggers.
Feedback from community always welcome.
Photon distribution on exit window
SR generated with
at
through the two dipoles