## Slide 1: EIC Accelerator Physics/Technology
Todd Satogata, Jefferson Lab
For the EIC Project and EIC Collaboration
CFNS/CTEQ School Lecture 2
9 June 2023
EIC:
www.toddsatogata.net
satogata@jlab.org
Notes: Kierkegaard book, but Descartes!

## Slide 2: Outline (Hour 2)
EIC interaction region(s)
  Digression into accelerator R&D
Luminosity revisited
Lumi optimization and limitations
  Superconducting magnets
  Crab cavities, crossing angle
  Beam sizes and cooling
  Space charge
  Synchrotron radiation
  Cooling
Luminosity ramp-up
Primary
Detector
Location
Future
Detector
Location
Primary
Detector
Location
Future 2nd
Detector
Location
(Some may look familiar from 2022 Gordon Conference talk)

## Slide 3: Differences in IR6/8
IR6 (Primary) and IR8 (Future) are fundamentally different
  Different halls
  IR6: Primary
    Both beams “inner” to “outer”
    Crossing angle “natural”
    Secondary focus ”unnatural”
    Less ESR synch radiation
  IR8: Future
    Both beams “outer” to “inner”
    Crossing angle extra bending
    Secondary focus looks feasible
    More ESR synch radiation
Primary
Detector
Location
Future
Detector
Location
Primary
Detector
Location
Future 2nd
Detector
Location

## Slide 4: EIC Primary Interaction Region
Different
axis scales!
Existing tunnel and
experiment halls
Focusing (quads)
as close to IP as
possible (~+/-5m!)
Tensions in magnet
requirements:
high field
large apertures
e/p magnet proximity near IP
Chromaticity:
focusing dependence
on particle energy
25 mrad crab crossing
A. Parker (SULI) D. Higinbotham
”Rear side”
”Forward side”

## Slide 5: EIC Primary Interaction Region (HSR forward)
HSR forward region most constrained
  Close path to arc
  b* 5.5cm for lumi
  Maximize acceptance (pt=1.23 GeV/c)
  Minimize fringe fields on ESR
  Support crab cavity and spin rotator requirements
B: Dipoles
Q: Quadrupoles
https://www.ipac23.org/preproc/pdf/MOPL158.pdf
0
20
40
60
80
100
120
140
160
180
Crab
cavities
“Match”
Spin Rotator,
Snake
Match and
arc FODO lattice
No space for usable secondary focus
b 1200m
to 5.5cm
in 10m!

## Slide 6: EIC Primary Interaction Region: Forward
197 MHz crab cavities/cryostats transverse dimension constraints
HSR snake angle geometric constraint
Alex Jentsch excellent far-forward physics slides at 2022 CFNS school
ESR
HSR
Rotator
Rotator
https://www.ipac23.org/preproc/pdf/MOPL158.pdf

## Slide 7: EIC Accelerator Technology Challenges, R&D
ESR Cavity
Prototype
Proton Injection
Fast Kicker
IR Design and Magnet Prototyping
Cooler Electron Source
Polarized e- Source
ESR
Vacuum R&D
ESR RF 500kW FPC
HSR Vacuum Upgrade
Hadron Polarimetry
ESR RF HOM Damper
Crab Cavity
Prototype
Electron Injection
Fast Kicker
IR Vacuum Chamber
ePIC
2nd IR
Existing tunnel and
experiment halls

## Slide 8: EIC R&D: IR Superconducting Magnets
Forward superconducting magnet integration
Multiple function spectrometer magnet at the forward hadron side

## Slide 9: EIC R&D: Crab Cavities
Stiffeners
Preliminary Cryomodule Design
(2 cavities per HSR cryomodule)
RF Design
Higher Order Mode (HOM) damping schemes
Hadron collider crabbing unprecedented
  Collaborating with HL-LHC
    Beam dynamics, RF control stability
    SPS tests: Phys. Rev. Accel. Beams 24, 062001 (2021)
  Electron crabbing was performed at KEKB (arXiv:1410.4036)
Superconducting “RF dipole” cavity
  ODU design
  High electric field and overall field quality requirements
197 MHz HSR crab cavity being prototyped
  Jefferson Lab/ODU/(BNL) collaboration
  Two possible HOM damping schemes: Waveguide loaded and coaxial couplers
  Stress analysis near completion, with stiffeners
Recent IPAC’23 invited talk

## Slide 10: EIC 197 MHz Crab Dimensions
Electromagnetic design requires to achieve:
  Cavity peak surface fields of Ep < 45 MV/m and Bp < 80 mT at 11.5 MV
  Bare cavity dimensions:
    Cavity length ≤ 1.5 m
    Cavity diameter (without couplers) ≤ 0.6 m
RF Property | Value | 
Vt [MV] | 8.5 | 11.5
Ep [MV/m] | 32.3 | 43.7
Bp [mT] | 58.1 | 78.6
Total Vt [MV] | 34 | 
No. of cavities | 4 | 3
Operating Temp. [K] | 2.05 | 
Stored Energy [J] | 50.3 | 92
Rs [Ω] (RBCS = 0.4 nΩ) | 15 | 
Pdiss [W] | 9.6 | 17.6
Q0 (G = 97.2 Ω) | 6.48×109 | 
Dimension | Value
Cavity Length [mm] (iris-to-iris) | 921.9
Cavity Length [mm] (flange-to-flange) | 1435
Cavity Diameter [mm] | 587.2
Pole Length [mm] | 524
Angle [deg] | 20
Reasonable surface fields at nominal voltage of 8.5 MV
0.59 m
1.44 m
Recent IPAC’23 invited talk

## Slide 11: Prototype Crab Fabrication
Majority of the cavity body is deep drawn from 4.17 mm Nb sheets
  A full Cu cavity will be fabricated to understand and verify the fabrication process
  Also, to perform room temp measurements
Flanges:
  Dogbone flanges – Nb with Indium seals
  All other flanges – 316 LN SS CF flanges with Cu gaskets
All material procurements are placed and most of the material have been received
Recent IPAC’23 invited talk

## Slide 12: ESR Polarization: Continuous Injection
~1Hz injection of new highly polarized (~85%) electron bunches
  Will have to learn how to minimize backgrounds
Initial polarization decays towards P∞ < ~50%
  Equilibrium of self-polarization and synchrotron radiation stochastic excitation
  At 18 GeV, every bunch replaced in a few minutes
  Need both polarization directions present at the same time
Pav=80%
Pav=80%
Re-injection
Re-injections
B P
Refilled every 1.2 minutes
B P
Refilled every 3.2 minutes
Asymmetric polarizations P
with respect to dipole field B

## Slide 13: IR8 Preliminary Layout
Hadrons
Electrons
First EIC 2nd Detector Workshop (May 2023)
IR8 Accelerator Talk (R. Gamage)
35 mrad crossing angle
(Investigating 25 mrad)

## Slide 14: IR8 Preliminary Optics (including 2nd focus)
Parameters at the 2nd focus for different energies
First EIC 2nd Detector Workshop (May 2023)
IR8 Accelerator Talk (R. Gamage)

## Slide 15: Luminosity (Lumi) Limits In One Slide™
Maximize collision frequency (~90 MHz)
  Limited by kicker rise times
  Limited by parasitic collisions (crabbing)
Maximize particles per bunch (~1011)
  Limited by sources, space charge
  Limited by collective effects
    Interaction of beam with impedances
    Also total currents: I1,2=q1,2N1,2fcoll ~1-3A
Minimize beam sizes at IP (~250/25 um)
  Limited by IR focusing, magnets
  Limited by chromatic dynamic aperture
  Limited by emittance growth (IBS)
Every parameter optimized
separately and collectively in the
EIC design
Try multiplying out the given numbers –
should be very close to 1034 cm-2s-1

## Slide 16: EIC Primary Interaction Region
Different
axis scales!
Existing tunnel and
experiment halls
Focusing (quads)
as close to IP as
possible (~5m!)
Tensions in magnet
requirements:
high field
large apertures
e/p magnet proximity near IP
Chromaticity:
focusing dependence
on particle energy
25 mrad crab crossing
A. Parker (SULI) D. Higinbotham
”Rear side”
”Forward side”

## Slide 17: Electrons and Hadrons in Synchrotrons (EIC)
Electrons
  Larger charge/mass ratio
    Smaller B to bend/focus (E, crab)
    Normal conducting magnets
    Polarization time dependence
  Synchrotron radiation
    Photonic backgrounds
    Damping
    Dynamic aperture: Touschek
    Large RF power needs
    Flat beam aspect ratio
  Harder collimation (multi-stage)
Hadrons
  Smaller charge/mass ratio
    Larger B to bend/focus (E, crab)
    Superconducting magnets
    No depolarization (in principle)
  No synchrotron radiation
    Hadronic backgrounds
    Negligible damping (EIC energies)
    Dynamic aperture: “Diffusion”
    Modest RF power needs
    Round beam aspect ratio
  Easier collimation (single-stage)

## Slide 18: Lumi Limits In (more than) One SlideNoTM
Maximize collision frequency (~90 MHz)
  Limited by kicker rise times
  Limited by parasitic collisions (crabbing)
Maximize particles per bunch (~1011)
  Limited by sources, space charge
  Limited by collective effects
    Interaction of beam with impedances
    Also total currents: I1,2=q1,2N1,2fcoll ~1-3A
Minimize beam sizes at IP (~250/25 um)
  Limited by IR focusing, magnets
  Limited by chromatic dynamic aperture
  Limited by emittance growth (IBS)
Challenge: colliding asymmetric beams
electrons: flat
hadrons: round
SuperKEKB: 10 um x 50 nm, 200:1!
EIC collision point: 11:1 transverse aspect ratio

## Slide 19: EIC CDR (CD-1) Parameters for Ecm and Luminosity
e [GeV]
18
10
10
5
5
p [GeV]
275
275
100
100
41
10 MW SR limited
Beam-beam limited
Space charge limited
beam size lumi scaling

## Slide 20: Lumi Limitations: Space-Charge (low Ecm)
Dense charged particle bunches electrostatically repel in rest frame
Creates nonlinear space charge force and equation of motion in lab frame
Fortunately scales with 1/g3 so worst at low energies
  Great example of time dilation
  Limits high-intensity injector emittances
  Force applies continuously within beam
Tolerable linear “space charge tune spread” of 0.05 limits total current of 41 GeV proton beam to ~0.4A.
(IBS: intra-beam hard scattering also contributes)

## Slide 21: Lumi Limitations: Beam-Beam (mid Ecm)
Colliding beams see each other’s collective charge distributions
Creates nonlinear beam-beam force and equation of motion similar to space charge
  BUT now the fields and force are in the lab frame already
  NO benefit of relativistic scaling
  Force applies only once per turn
Tolerable “beam-beam tune spead” of 0.015 limits highest EIC luminosity

## Slide 22: Lumi Limitations: Electron SR Power (high ECM)
Accelerated charged particles emit photons
  Electrons in synchrotron: radially accelerated
  Synchrotron radiation emitted in forward cone
    Cone opening angle
    Radiated power
  scaling much worse for electrons
    18 GeV e: =3.5x104 vs 255 GeV p: =3x102
Design: 9 MW @ 18 GeV (facility limit 10 MW)
Expensive: Power must be provided by SRF
Raise electron energy last (e current limit)
Dipole Radiation
Perpendicular to charge acceleration
Synchrotron Radiation
Relativistically boosted dipole radiation
Relativistic Boost
Radial
acceleration

## Slide 23: Collider Luminosity Ramp-Up
Luminosity ramp-up to design takes years
  Useful paper: arxiv 1202.3950 (V. Shiltsev)
  Contextualizes Tevatron Run-II and early LHC
  Luminosity ramp-up parameter C: complexity
    C: time (years) to increase lumi by e
    C=2: factor of e luminosity increase in 2 years
  Early commissioning can make quick strides
    C<1 (or <<1) but do not get too exuberant
  Long-term commissioning usually C~2-3
EIC will very likely take years to reach design luminosities
  But we will get there!
Tevatron Run-II: design 275x1030
HERA: design 15x1030

## Slide 24: Summary
EIC design meets all design requirements
EIC luminosity is highly optimized
  Balances several individual parameter optimizations
EIC R&D progressing
  Focus: challenging technical components
e/p beam differences drive EIC choices
  e.g. luminosity vs Ecm, IP aspect ratio
Luminosity ramp-up will take time
  will last substantially beyond project end
  project provides excellent basis to get there!
July 28-30, 2022 (BNL)

## Slide 25: Backup and assorted discussion slides

## Slide 26
Notes: LHC design 0.58A p (HL up to 1A), beam-beam parameter 3.4e-4 (3-5—3 HL-LHC)

## Slide 27: Beware of Doug (Higinbotham, JLab)
Doug knows when I am on Teams.
Doug is inquisitive and asks good questions about EIC luminosity.
I made the tactical error of sharing this paper with Doug.
  So here I am sharing it with you in the context of EIC luminosity ramp-up.
https://arxiv.org/pdf/1202.3950.pdf

## Slide 28: Paper Context
Paper originally presented at 2011 Chamonix LHC Performance workshop
Considerable excitement about exponential improvements in LHC lumi during 2010 commissioning
  Factor of >104 in 6.5 months!
  Ended “only” factor 30 from design
C: exponential “complexity” of collider lumi improvement
  C=0.06 means it was “easy” to make LHC lumi progress in this era

## Slide 29: Lesson from the Tevatron
Tevatron Run-II experience over about a decade
  Three distinct phases
  Reflects increasing challenges of luminosity limitations
No silver bullets
  No sudden exponential jumps or reductions in complexity
  Instead many incremental improvements (~30) across many systems
Initial tuneup still “easy”
  But gets harder as low-hanging fruit are plucked
C: Time (y) to increase lumi by factor e
C=2: factor of e increase in lumi over 2y

## Slide 30: Lesson from the Tevatron
Tevatron Run-II experience over about a decade
  Three distinct phases
  Reflects increasing challenges of luminosity limitations
No silver bullets
  No sudden exponential jumps or reductions in complexity
  Instead many incremental improvements (~30) across many systems
Initial tuneup still “easy”
  But gets harder as low-hanging fruit are plucked
C: Time (y) to increase lumi by factor e
C=2: factor of e increase in lumi over 2y

## Slide 31: Lessons from HERA
HERA-2
HERA experience over more than a decade
  C~3 over multiple phases
Major upgrade after ~10y (HERA-2)
  Nearly a new machine
  Addressed known facility luminosity limitations
  Even then, C~3 over years
Fewer low-hanging fruit
  Less time in C<1 regime
  A product of new type of collider or truly complex facility
  EIC also highly complex
“Silver bullet” was a machine upgrade

## Slide 32: Tabulated Complexities
Luminosity evolution of many colliders suggests expecting a long evolution
Note that these complexities are for single colliding species types
  Usually built on top of existing, well-established injector complexes
RHIC and LHC have had decadal success colliding multiple species
  Edge effects of changing species are order of weeks (RHIC) or runs (LHC)

## Slide 33: Tabulated Complexities
Luminosity evolution of many colliders suggests expecting a long evolution
Note that these complexities are for single colliding species types
  Usually built on top of existing, well-established injector complexes
RHIC and LHC have had decadal success colliding multiple species
  Edge effects of changing species are order of weeks (RHIC) or runs (LHC)

## Slide 34: Paper Conclusions

## Slide 35: LHC Experience: 2015-2018
sqrt(s)=13 TeV
After 5y of lower-energy operations
Luminosity ramp-up C<1
Then saturated to C>>1 quickly
2e34 vs Shiltsev ~5e34 => HL-LHC
“same” vert scales

## Slide 36: IR8 Status
Randika Gamage
May 18th, 2023
First EIC 2nd Detector Workshop (May 2023)
IR8 Accelerator Talk (R. Gamage)

## Slide 37: IR comparison
 | 1st IR |  | 2nd IR | 
 | proton | electron | proton | electron
Detector occupied region | -4.5 m +5.0 m Beam elements < 1.5o in main detector |  | -4.5 m +5.0 m Beam elements < 1.5o in main detector | 
Polarimetry | Yes (IR4) | local | Yes (IR4) | local
2nd focus | No |  | yes | 
* @ 275 GeV (h), 10 GeV (e) | *x = 80 cm *y = 7.2 cm | *x = 45 cm *y = 5.6 cm | *x = 80 cm *y = 7.2 cm | *x = 45 cm *y = 5.6 cm
ZDC | 0.6m x 0.6m x 2m @ s30m 4 mrad |  | 0.6m x 0.6m x 2m @ s0m 4 mrad | 
Roman Pots | 1-5 mrad, @s30m |  | 0-5 mrad, @s30-45m | 
Scattered particle acceptance | p: 0.18 GeV/c < pT < 1.3 GeV/c |  | p: 0 GeV/c < pT < 1.3 GeV/c | 
Q2 tagger |  | Q2< 0.1 GeV |  | 
Crossing angle | 25 mrad |  | 35 mrad | 
 | 1st IR |  | 2nd IR | 
 | proton | electron | proton | electron
Detector occupied region | -4.5 m +5.0 m Beam elements < 1.5o in main detector |  | -4.5 m +5.0 m Beam elements < 1.5o in main detector | 
Polarimetry | Yes (IR4) | local | Yes (IR4) | local
2nd focus | No |  | yes | 
ZDC |  |  |  | 
Roman Pots |  |  |  | 
Scattered particle acceptance | p: 0.18 GeV/c < pT < 1.3 GeV/c |  | p: 0 GeV/c < pT < 1.3 GeV/c | 
Q2 tagger |  | Q2< 0.1 GeV |  | 
Crossing angle | 25 mrad |  | 35 mrad | 

## Slide 38: Requirements/Constraints
Fit into the existing RHIC IR8 experimental hall between arcs 7 and 9.
Preference for a secondary focus.
Same accelerator equipment as in IR6 (spin rotators, snake and crab cavities).
Second colliding IR and detector not in project, but the ability to have one is in the project scope.
Rear
Forward

## Slide 39: IR6 layout
25 mrad crossing angle

## Slide 40: IR8 full layout (colliding)
35 mrad crossing angle (driven by accelerator geometry).
Second focus point at ~45m.
Space for similar accelerator equipment as IR6.

## Slide 41: IR8 near IR layout
Space available for luminosity monitor, low Q2 tagger etc..
All ancillary detectors in outgoing hadron beam side (Forward) integrated

## Slide 42: Acceptance as a function of and
- fraction of the longitudinal momentum relative to hadron beam
- fraction of the transverse momentum relative to hadron beam ( )
acceptance at
acceptance at
Secondary focus allow for
Can reach the fundamental limit

## Slide 43
Neutrons mrad
Protons mrad
Protons mrad
This is using NbTi magnets.
Final focusing quads and the dipoles properties (apertures, lengths etc..) was optimized for forward scattering neutron and proton acceptance.
IR8 forward acceptance
100GeV
41GeV
275GeV

## Slide 44: IR8 second focus
Optimal
For the current design, 0
Limit of for the given momentum spread is at 275GeV
Parameters at the 2nd focus for different energies

## Slide 45: IR8 hadron optics
Limited matching space requires some high gradient magnets (quadrupoles) than what is available from existing RHIC magnets.
Near IR magnet include 7 FFQs, 2 Dipoles, 1 corrector and B0.
All magnets are assumed to be NbTi
Magnets | RHIC | New
Quadrupoles | 11 | 11
Dipoles | 5 | 0
275GeV
100GeV
41GeV

## Slide 46: IR8 electron optics
Optics and design similar to IR6
Rear
Forward

## Slide 47: Constraints
Space for magnets.
Geometry of the experimental hall.
Optics requirements for specific regions (eg: crab cavities)

## Slide 48: Summary 2nd IR (IR8)
Second colliding IR and detector not in project, but the ability to have one is in the project scope.
This is a Pre-conceptual design.
The IR8 with the second focus adds complementarity to IR6.
Work to be done includes,
  Crab cavity space requirement for the 35 mrad crossing angle.
  Clearance check for the RCS (Rapid Cycling Synchrotron) bypass.
  Account for luminosity sharing by moving the IP by 0.2975m away from IR6.
  Low energy lattices (41,100 for protons and 5,10 for electrons)
  Further study needed for the feasibility of the IR magnets.
  Nb3Sn magnets are being evaluated as an option.
  Chromaticity compensation with two IR’s
IR8 information