## Slide 1: EIC Project Update
Elke Aschenauer and Rolf Ent
Co-Associate Directors for the Experimental Program
ePIC Convener Meeting
December 16th 2022

## Slide 2: Background Taskforce
Need info on is the current machine design for vacuum and SR good enough to operate ePIC  questions during technical reviews
  need SR rate in detectors
  beam gas background rates
  total hadronic and electromagnetic radiation load
  neutron fluence  SIPMs, Silicon, ….
  impact on track seeding and finding
  overall rates as fct. of h and F
  …………
formed a taskforce of people working on these talks at the project and ePIC
Jarda, Zhengqiao, Alex, Kolja, Joe, Jae, Wouter, David L., Rey, Elke
welcome everybody who wants to do concrete work
have met twice till now Friday 2nd of December 9:30 am, and Friday 16th of December
will report results to ePIC GDI and respective detector WGs and Project Accelerator WG
Wiki: https://wiki.bnl.gov/EPIC/index.php?title=Background
Indigo: https://indico.bnl.gov/category/461/
email-list coming

## Slide 3: ePIC Readout Chain
Name
Sharing
Function
Attributes
Adapter
Detector Specific
-HV/Bias distribution
-HV divider
-Interconnect routing
-Sensor Specific
-Passive
Sensor
Detector Specific
-Multi-Channel
Sensor
-MAPS
-AC-LGAD
-MCP-PMT
-SiPM
-LAPPD
Front End Board
(FEB)
Detector Specific
-Amplification
-Shaping
-Digitization
-Zero Suppression
-ASIC/ADC
-Discrete
-Serial Link
Readout Board
(RDO)
Shared / (potential variations)
-Communication
-Aggregation
-Formatting
-Data Readout
-Config & Control
-Clock &Timing
-FPGA
-Fiber Link
Data Aggregation Module (DAM)
Shared / (FELIX)
-Computing Interface
-Aggregation
-Software Trigger
-Clock & Timing
-Config & Control
-Large FPGA
-PCIe
-Potentially Ethernet
Computing
COTS / Ethernet
-Data buffering and sinking
-Run Control
-Calibration Support
-QA / Scalers
-Collider Feedback
-Event ID/Building?
-Software Trigger
-Monitoring
Global Timing Unit (GTU)
-Interface between collider, Run Control, & DAM
-Config & Control
-Clock & Timing

## Slide 4: Next “ePIC – Project” Project: Subdetector Readout Chains
Have integrate read-out chain questionnaire for all subdetectors following this example to be filled by experts in the service excel-sheet
FEB:
detector specific
Sensor
detector specific
RDO:
hopefully one board
common to many
subdetectors
FEB
RDO
All linked to:
https://wiki.bnl.gov/EPIC/index.php?title=Project_Information#Documents%3A
Deadline: 9th of January 2023