## Slide 1: Readout for Calorimeter Insert Prototype and Calibration with Cosmic Rays
JiaJun Huang

## Slide 2: Prototype Preparation
Ten PCB Boards
  Four SiPMs
  Four Square/Hexagon Tiles
  Reflective Foils
  3D Printed Frames
CAEN DT5202
  Unit to bias and readout 64 SiPMs
Notes: Release date of CAEN

## Slide 3: CAEN Configuration
Bias
Gain: LG and HG
Threshold
Triggering Logic
Output: ASCII Files
  Timestamp & ADC counts
Notes: Reads out in both gains

## Slide 4: CAEN Readout
Threshold Scan
  Four cells must trigger to record counts
Run for each gain setting
Noise
Cosmics

## Slide 5: 1D & 2D Visualization
Collection of minimum ionizing particle Muons that triggers at least four SiPM channels.

## Slide 6: Signal Channel Readout
Fit pedestal to Gaussian
Fit data to Landau
  Extract peak value as MIP value
Subtract Gaussian from Landau

## Slide 7: Cosmic Ray Events

## Slide 8: Single MIP per ADC Channels
Difference in tile shape (square/hexagon) yields different MIP values
If not accounted for channel to channel variation, it can degrade the resolution of the calorimeter system

## Slide 9: 2D Cosmic Ray Event

## Slide 10: Hall D Prototype
Data collection of detector in horizontal position in progress.

## Slide 11: Conclusion
Capable of collecting beam data
MIP value for individual cells
  Used to calibrate the energy measurement of the detector for each cell independently