## Slide 1: Modular RICH Detector Simulation – Rayleigh Scattering
Cheuk-Ping Wong
Georgia State University
03-25-2016

## Slide 2: Last Update
No Rayleigh Scattering was observed in the simulation

## Slide 3: This week
Updated GEMC to version 2.3
Simulation results using material definitions of aerogel from both Hubert and Marco

## Slide 4: 100 Optical Photon w/ 2-4 eV
Hubert’s Agel
Marco’s Agel
More Rayleigh Scattering occurs when Hubert’s agel is used (see slide 7,13-16)
-- optical photon

## Slide 5: Simulation Setup
100 k optical photons
Momentum = 1.7-6.2 eV (i.e. λ=200-730 nm)
Launching at (x,y,z)=(0,0,64.585) mm, i.e. right at the front of aerogel
Fresnel lens is removed from the detector
Aerogel
  Hubert -- the one we always used
  Marco – RichAerogel3 which is predefined

## Slide 6: Analysis Setting
Unscattered photon
  Hits on the sensor, and
  Moves forward (pz>=0), and hits at (x,y)=(0,0)mm
Scattered photon
  Hits inside agel, and
  Not moves forward or not hits at (x,y)==(0,0)mm

## Slide 7: Photon Spectrum from Diff. Agel
Divide blue and red histograms by black histogram  normalized photon spectra (next slide)
Absorption? (see slide 15)

## Slide 8: Normalized Photon Spectrum from Diff. Agel
Clarity of Marco’s agel is less than ½ of Hubert’s Marco’s agel gives less scattering photons (see slide 9-10)
The shorter wavelength hits (shade region) will be filtered out by the Fresnel Lens

## Slide 9: Photon Spectrum
Due to absorption?
Marco’s agel has higher transmission if Rayleigh Scattering is implemented

## Slide 10: Normalized Photon Spectrum
Marco’s agel has higher transmission if Rayleigh Scattering is implemented

## Slide 11: Only Consider Photons that Hit on the Sensor
Only count the (both scattered and unscattered) photons that hit on the sensor
Less scattered photons are counted
More details on slide 16 to 20

## Slide 12: Summary
Fig. 1 (slide 8) and Fig. 2 (slide 7) on Hubert’s agel notes are reproduced
Marco’s agel has lower clarity (<1/2 of Hubert’s)
Marco’s agel has higher transmission than Hubert’s if Rayleigh Scattering is implemented

## Slide 13: Next
Rescale Scattering length of Marco’s agel as suggested by Marco
Shift the Rayleigh Scattering array
Put Fresnel lens back in the simulation
Simulation w/ incident pion- and w/ Rayleigh Scattering on
Likelihood Analysis

## Slide 14
Back Up

## Slide 15: Absorption Length vs Photon Wavelength
Hubert’s agel has longer absorption length
 better transmission if there’s no Rayleigh Scattering
In log scale

## Slide 16: Simulation Setup
100 k optical photons
Momentum = 2-4 eV (i.e. λ=200-730 nm)
Launching at (x,y,z)=(0,0,64.585) mm, i.e. right at the front of aerogel
Fresnel lens is removed from the detector

## Slide 17: Analysis Setting
Only count the (scattered and unscattered) photon that hits on the sensor
Unscattered photon
  Moves forward (pz>=0), and
  Hits at (x,y)=(0,0)mm
Scattered photon
  Not moves forward, or
  not hits at (x,y)==(0,0)mm

## Slide 18: Normalized Photon Spectrum of Different Aerogels
Agel from Marco has higher transmission (Lower Clarity, higher transmission, see slide 20)

## Slide 19: Photon Spectrum (before normalization)

## Slide 20: Normalized Photon Spectrum
R.S. Off
R.S. On
Rayleigh Scattering decreases transmission of aerogel
Agel from Marco has higher transmission if Rayleigh Scattering is implemented
R.S. On

## Slide 21: Scattered and Unscatterd photon spectrum in Hubert’s notes
Count of Scattered (black line) photon is much higher than unscattered photon (yellow shade) in shorter wavelength region
Preferred Aerogel : lower clarity, higher transmission in longer wavelength region
The NA44 Aerogel Cherenkov Trigger, Hubert van Hecke and Douglas E. Fields.