## Slide 1: GridPIX Mini-TPC
Klaus Dehmelt1,2, ∗∗P. Garg5, ∗Thomas Hemmick1,2, Jochen Kaminski3, Peter Kluit4, Nikolai Smirnov5
1Department of Physics and Astronomy, Stony Brook University, USA
2Center for Frontiers in Nuclear Science at Stony Brook University, USA
3Institute of Physics, University of Bonn, Germany
4Nikhef, The Netherlands
5Department of Physics, Yale University, USA

## Slide 2: Brief Introduction
Originally as “upgrade path” for ATHENA.
Not discussed in current EPIC baseline.
Ideally suited for Detector 2.
Provides:
  PID (pi-K-p) from 100 MeV/c to 800 MeV/c
  ROBUST tracking (enormous number of hits per track)
  Virtually immune to synchrotron background.
ATHENA’s Vision
Gas Volume
Readout
High Voltage (-10kV)
Low radiation Length
T2K gas (low diffusion)
Silicon Pixel Readout
4% radiation length
(dominated by cooling)
Field Cage
1% radiation length, entrance and exit

## Slide 3: PID ~ Velocity
p = mgb E = mg velocity(b) measurement yields mass.
Direct measurement:
  Record signal time at multiple locations, calculate v.
  “Fast” detector = low transit time spread (most easily achieved at small transit time)
Velocity-dependent interaction(s) with detector:
  Specific Ionization (aka )
  Cherenkov Radiation:
    qC measured wrt track direction.
    Thus dependent upon deliverables from tracking
  Bremsstrahlung:
  Transition Radiation:
eID mechanisms

## Slide 4: Physics Motivation
At the lowest momenta particle identification by dE/dx is advantageous.
Promising technology for EIC detector 2
Near h=0, soft particles dominate
TOF-PID has competition between pmin and resolving power
dE/dx in ATHENA upgrade promised lowest PID reach
Many envision a Detector 2 with 3T or higher field.

## Slide 5: GridPIX Overview
Ultimate dE/dx device.
  Avalanche grid in front of 55 x 55 mm2 pixels.
  >90% efficiency for single electrons.
  Goals:
    Enough diffusion to get every electron into a different hole.
    Count electrons one-by-one.
  Three generations of development and continuing.
Small area is not particularly expensive.
  1800 chips (order/produce/test 3600) = $716k
  Careful: 1.2-5.4 kW of power (occupancy dependent).
Pros:
Known/Proven Technology
Active further development (Bonn)
Best possible (~count each electron)
Affordable for a small area
High resolution tracking
Low mass in electron arm
Continuous (aka streaming) readout
Cons:
~3 kW of power:
Must find a low mass way to handle.
Services “bulky” (compared to just Si)
  Gas
  HV membrane
  Cooling
  DC power lines (3kV goes in too)
3D e-by-e tracking

## Slide 7
Overview:
Segmentation:
  70% active area  3150 “rows”
2400 primaries in 25 cm for a MIP.
  Thousands of hits per track.
Extremely robust patterns.
June 2021

## Slide 9
Delta Rays can be removed very often by Topology.

## Slide 10: Anticipated dE/dx Performance
Lehraus Plot
Using 5.4 as a standard TPC
  5.4*(0.25)-0.37 = 9.0
Measured for GridPIX (truncated Mean)
  4.1% at 1 meter
  4.1*(0.25)-0.37 = 6.85
Roughly 20 sigma at 0.5 GeV/c
Useful range overlaps with DIRC
9.0%
K-p
p-K
6.85%
K-p
p-K
Momentum
Momentum
#s
#s
easy
hard

## Slide 11: Overly Simplified Momentum Resolution
Figure of Merit:
Can be compared to Silicon with detailed Monte Carlo
Here is simple-minded estimate
  Gas:
    Including efficiency ~3000 electrons (minimum!) per track
    Each suffers digitization (s = 55 mm/sqrt(12) = 16 mm)
    Diffusion(Length) =
      D(2cm) = 35 mm  FOM = 0.70 mm
      D(25cm) = 125 mm  FOM = 2.3 mm
      D(50cm) = 176 mm  FOM = 3.2 mm
      D(100cm) = 250 mm  FOM = 4.6 mm
  Although ignoring many significant effects, initial result is on the order of the layers of silicon.
Momentum resolution is likely very good
Pattern recognition is certainly SUPERB!!!

## Slide 12: Radiation Length
sPHENIX:
45 kV & 18 layers kapton.
EIC:
10 kV & 5 layers kapton.
End Cap:
Temperature Profiles: 3 kW
Coolant above the dew point
  Conventional Cooling OK at 4%
  CO2 cooling promises ~2% ?
Barrel:

## Slide 13: Initial R&D Plan
Fermilab Test Beam
  Mixed beam at low energies
  Identified by beam line Cherenkov
Cosmic Rays at Argonne
  0-4 Tesla Field available.
  Limits diffusion, maintains “clusters”
sPHENIX TPC Prototype Field Cage
+
=
Ability to study PID
Argonne Magnet Facility
Nikhef 32-chip Module
=
Ability to study clusters

## Slide 14: 8-QUAD module with field cage
Nikhef will send to Stony Brook a 32-chip module & COMPLETE DAQ.
Timing is in the hands of the lawyers:
  SBU & J-Lab
    Show me the money!
  SBU & Nikhef
    Loan agreement, shipping payment, insurance, …

## Slide 15: Fermilab Beam Lines
MTest is the “test beam” most familiar to the community.
  Primary Beam 120 GeV protons
  Secondary Beam 8-32 GeV mixed (Cherenkov PID)
MCenter is less familiar
  Secondary Beam ala Mtest
  Tertiary Beam below 1 GeV (TOF PID)
MTest
MCenter
Hemmick & Garg will be there Monday and Tuesday next week

## Slide 16: Comment on Deltas
Are Delta Rays entirely junk?
Best Delta measurement ever
    Contributor to overall ionization rate.
    Significant contributor to relativistic rise.
    Fully distinguished Delta contribution on every track may provide PID opportunity.
Directing high momentum beams to the test can yield information.
“Long” tracks can be manufactured by multi-event overlays.

## Slide 17: Summary
A mini-TPC with GridPIX readout seems an ideal technology for Detector 2 at EIC
  Especially useful at future luminosity,
  Robust pattern recognition against synchrotron background.
  Data reduction/background suppression to tracklets possible in hardware.
Excellent PID performance at the lowest momenta.
Possibilities to study a long detector for PID in Relativistic Rise (PID  10 GeV/c)
NOTE:
Evgeny Shulga talk/measurement on complete elimination of Ion Back Flow
Nikolai Smirnov talk with more on Gridpix and other innovative ideas.

## Slide 18: Backups

## Slide 19: Homework-3
What R&D will be needed after the FNAL beam test?
  Theme: Demonstrations this far with GridPix are not yet “deployable” in an experiment.
    Water cooling is only a proof of principle; CO2 cooling should be implemented
      lower radiation budget, higher performance, more uniform temperature (important for parallel plate avalanche)
    Extending drift length over which cluster-counting PID can be effective
      Alternate gas choices (e.g. He + CF4 + iC4H10, etc…)
      Goal: Extend cluster counting to 1 meter of drift.
      Deal with cluster merging in post processing of data.
      NOTE: Second EIC detector may use 3 Tesla field, thereby minimizing cluster merging.
    Readout Plane Technology (the next generation beyond the quad):
      The chips should more directly contact a cold plate without making separate quads.
      The (expensive) flex solution to bring the readout to the back should be redesigned.
      The multiplexer (that combines the data streams of 16 chips) should be redesigned/optimized for full sector readout.
      On-board tracklet formation
        effective rejection for background synchrotron radiation at electron machine at highest luminosity.

## Slide 20: Homework-1
GridPIX post-processing to prevent discharges is not addressed. This is a critical item for the long-term use. Can you discuss any overhead and risks this might entail in an EIC detector?
  In the post processing a SixNy is deposited on the TPX3 chip. This protection layer prevents the detector from sparking and protects the chip.
  This protective layer works well and for single chip detector, the quad detector and the 8 quad module.
  All detectors were successfully tested in three test beam campaigns. No problems with discharges occurred.
  The only problem that occurred in the test beam campaign of the 8-quad module was that we had to disconnect the HV of the grid of one chip due to a short. For a large system the distribution of the HV should be changed to allow for remote disconnection of the HV of the grid.

## Slide 21: Prepared boxes
Dimensions in cm (no margin)
length depth height
45 47 81
Wooden box should be
50 x 50 x 85 cm3

## Slide 22: Overly Simplified Momentum Resolution
Figure of Merit:
Can be compared to Silicon with detailed Monte Carlo
Here is simple-minded estimate
  Gas:
    Including efficiency ~3000 electrons (minimum!) per track
    Each suffers digitization (s = 55 mm/sqrt(12) = 16 mm)
    Diffusion(Length) =
      D(2cm) = 35 mm  FOM = 0.70 mm
      D(25cm) = 125 mm  FOM = 2.3 mm
      D(50cm) = 176 mm  FOM = 3.2 mm
      D(100cm) = 250 mm  FOM = 4.6 mm
  Although ignoring many significant effects, initial result is on the order of the layers of silicon.

## Slide 23: Calibration curve ToT gas gain

## Slide 24: Remote desktop and data taking
Levaard
arawana
Si telescope
Switch
Control room
Remote hut
In hall
outside magnet
SLOW CONTROLS
Windows
DAQ TPX3
Linux
DAQ Si
Linux
Windows
Linux
HV, Gas and
run control (tunnel to arawana)
SPDR controls (2)
DAQ running
root file production

## Slide 25: Equalisation results chip 0
One has sigma noise is 7.9 counts and the tune per pixel is 2.8 counts
One trim dac unit corresponds to 12 counts . So one expects 12/sqrt(12.)
ThresholdFinalChip0.gif

## Slide 26: Budget Summary
We can only do the Fermilab in the first year.
The budget leverages existing apparatus
Two methods of realize reduced scenario:
  Limit the number of personnel
  Shorten the run
Cost Basis
Large numbers of students are realistic
We have a long tradition of respecting DEI