## Slide 1: Current state and planning for EIC light ion polarization
Haixin Huang (BNL)
on behalf of polarization design team
Workshop: Electron-Nuclei Interaction at EIC
July 7, 2023

## Slide 2: Outline
Proton polarization in EIC as Baseline
He-3 polarization in EIC and Snake upgrade
Potential for polarized deuterons
Conclusion

## Slide 3: RHIC Polarized Beam Complex
PHENIX
AGS
LINAC
BOOSTER
Pol. H- Source
200 MeV Polarimeter
Helical Partial
Siberian Snake
Spin Rotators
(longitudinal polarization)
2 Siberian Snakes/ring
Spin Rotators
(longitudinal polarization)
Strong AGS Snake
RHIC pC Polarimeters
Absolute Polarimeter (H jet)
STAR
AGS Polarimeter
Spin flipper
 | Max Energy [GeV] | Pol. At Max Energy [%] | 
Source+Linac | 0.2 | 82-84 | 
Booster | 2.5 | 82-84 | 
AGS | 23.8 | 67-70 | p-Carbon
RHIC | 255 | 55-60 | Jet, full store avg*
 | Relative Ramp Polarization Loss (Run 17, full run avg)
AGS | 17 %
RHIC | 8 %
* Includes both ramp loss and store decay
With pulsed skew quads in the AGS (they will be tested for run24), the polarization loss in the AGS will be mostly eliminated.
With precooler at injection and six snakes, it is expected that polarization will be preserved in Hadron Storage Ring (HSR) in EIC.

## Slide 4: Depolarizing Resonance Strength Comparison
Systematic resonances, located at 392+Qy, 412-Qy, 232+Qy, 250-Qy, appear weaker in HSR, compared to RHIC, the reverse occurs for non-systematic resonances, the latter effect could be an indication that the 3-periodicity of former RHIC lattice is in jeopardy in its HSR evolution.
A potential adverse configuration which results regarding resonance crossing, is the presence of wide non-systematic resonances in the direct vicinity of systematic resonances.
RHIC

## Slide 5: Snake Resonances in RHIC and EIC
Depolarization can still happen at certain vertical betatron tunes due to higher order resonances:
½ =m +/- n
Far more tune space available in six snake configuration
  Important for flexibility in the face of complicated beam dynamics (high peak currents, interaction with coolers, etc)
Sy
Sy
Qy
RHIC tune space
Snake resonance spectrum
2-snakes
6-snakes
Experimental observation of
Snake Resonances in RHIC
RHIC with 2 Snakes
EIC Hadron Ring with 6 Snakes

## Slide 6: Crossing of Strongest Spin Resonance in EIC
EIC will have pre-cooling at injection. Vertical emittance is expected to be cooled down to 0.5-1mm-mrad.
Simulations show that two snakes preserve proton polarization with cooled rms emittance of 1 mm-mrad
A 1,000 particle bunch is tracked across 393+ using ZGOUBI*
* F. Méot, H. Huang, V. Ptitsyn, V. Ranjbar, G. Robert-Demolaize, V. Schoefer, and V. Morozov, RHIC optics and spin dynamics with snakes and rotators, Phys. Rev. Accel. Beams 25, 121002 (2022).
(courtesy to Francois Meot)

## Slide 7: Crossing of Strongest Spin Resonance in EIC
EIC will have pre-cooling at injection. Vertical emittance is expected to be cooled down to 0.5-1mm-mrad.
Simulations show that six snakes in HSR lattice preserve proton polarization with cooled rms emittance of 0.5 mm-mrad
A 1,000 particle bunch is tracked across 393+ using ZGOUBI*
(courtesy to Kiel Hock)

## Slide 8: Outline
Proton polarization in EIC as Baseline
He-3 polarization in EIC and Snake upgrade
Potential for polarized deuterons
Conclusion

## Slide 9: Polarized He-3 source and Extended EBIS
He-3 is polarized using Metastability Exchange Optical Pumping (MEOP) mechanism
Ionized in the ionization cell using electron beam (up to 10A)
High magnetic field (5T solenoid)
Intensity ~ 2∙1011 3He++ ions in 10 s pulse
Maximum polarization > 80%
Polarized He3 source ready in 2025
The He3 source is being realized as a part of an extension of existing EBIS
Additional solenoid extends the trap length leading to 40-50% heavy ion intensity increase
Extended EBIS

## Slide 10
Overview of He-3 in the Booster
Extraction at |Gγ|=10.5
Crosses |Gγ|=5 through 10 imperfection resonances
Crosses |Gγ|=12-and |Gγ|=6+
Allows stronger snake settings in AGS
Minimizes optical defects from the AGS cold snake
The vertical tune can be placed inside the spin tune gap in AGS at injection
He-3 are injected into the Booster at |Gγ|=4.19
The injected intensity from EBIS is expected to be 2×1011 with a polarization of 80%.
Extraction is possible at |Gγ|=7.5 and |Gγ|=10.5

## Slide 11: Booster AC Dipole Beam Test
The Booster AC dipole design strength is 25Gm.
Using a spare power amplifier from RHIC, AC dipole can reach 15Gm which is enough for the functionality test.
The function of the Booster AC dipole has been tested with polarized protons at 0+y. Full spin flip is achieved. Simulations show good agreement with measurements.
preliminary

## Slide 12: Polarized He-3 in Booster and AGS
Two options for Booster extraction: extraction at |G|=7.5 or 10.5. |G|= 7.5 is similar to B of proton case. |G|= 10.5 requires Booster extraction and AGS injection magnets upgrades. No constraint for |G|=7.5 injection case.
Simulations show that the imperfection resonances up to |G|=10 can be corrected by existing orbit correctors (25A maximum current).
AGS will run with two partial snakes, 25%+14% (due to larger |G| value, same B field gives stronger partial snake) and both betatron tunes will be put into spin tune gap().
Tracking with 8 particles on the ellipse of 3*2.5 memittance for 25%+14% partial snakes. Polarization is good before 60-y.
With the source available in 2025, polarized He-3 development is possible in the AGS behind last RHIC run and during EIC construction.

## Slide 13: Polarized 3He in Present RHIC
Existing Siberian snakes and spin rotators for 3He in RHIC
Much stronger resonance strength requires more snakes.
The snakes and spin rotators from the 2nd RHIC ring can be reconfigured as additional snakes.
 | p | 3He+2
m, GeV | 0.938 | 2.808
G | 1.79 | -4.18
E/u, GeV | 24-275 | 16-183
¦Gg ¦ | 46.5-525.5 | 72.6-819.4

## Slide 14: Six Snakes
Number of Snakes will be increased from 2 to 6
Snake arrangement is perfectly symmetric with 60 degree bending angle between Snakes.
Additional Snakes are put in DU7 ”dummy” sections, free of magnets.
-45o
Due to the injection region constraint, the snake at IP6 can not be put into the desired place. The proposed snake locations are as following with counting starting at IP12: snake1 = 𝜙, snake2=𝜋/3 − 𝜙, snake3 = 2𝜋/3−𝜙, snake4 =𝜋+𝜙, snake5 = 4𝜋/3−𝜙, snake6= 5𝜋/3− 𝜙, where 𝜙 = 0.0435rad.

## Slide 15: 3He Simulation Results
10%/hour
Simulations through the strongest depolarizing resonances for 3He at 735−𝑄𝑦 and 717 + 𝑄𝑦 in RHIC lattice. The simulation was done for 1000 particles with Gaussian distributions in 6D phase space. The acceleration rate is about five times that of the proton acceleration rate in operation. The betatron tunes are 𝑄𝑦 = 28.685 and 𝑄𝑥 =29.673. The rms normalized emittance is 𝜀 = 1 𝜇m in both planes.
(courtesy to Francois Meot)
Simulations with HSR lattice is underway.

## Slide 16: Outline
Proton polarization in EIC as Baseline
He-3 polarization in EIC and Snake upgrade
Potential for polarized deuterons
Conclusion

## Slide 17: Polarized Deuterons in EIC
Unpolarized deuteron beam has been used in RHIC during ion physics program.
Present EIC physics program does not include polarized deuterons.
 | p | 3He+2 | d
m, GeV | 0.938 | 2.808 | 1.876
G | 1.79 | -4.18 | -0.143
E/u, GeV | 24-275 | 10-183 | 12-137
¦Gg ¦ | 45.5-525.5 | 48.5-818 | 1.6-20.9
Small deuteron G:
Much higher magnetic field required for spin rotation
(Siberian Snakes not feasible)
But:
  Weaker resonances
  Small number of resonances
  (makes it possible to deal with individual resonances)
In EIC hadron ring
H. Huang, F. Méot, V. Ptitsyn, V. Ranjbar, and T. Roser, Polarization preservation of polarized deuteron beams in the electron ion collider at Brookhaven National Laboratory, Phys. Rev. Accel. Beams 23, 021001(2020).

## Slide 18: Polarized Deuterons in EIC Hadron Ring
Gγ range: -1.6 to -20.9. 19 imperfection resonances. With rms orbit error of 0.3mm, the strongest resonance strength is less than 0.0015. From the nominal ramp rate in RHIC d-Au run, the ramp rate is about dγ/dt=90/220s=>resonance crossing rate α=1.2E-7.
A partial snake can be used to overcome these resonances. The required partial snake snake strength is 0.22%. The existing snake is not strong enough. Adding a solenoid is a solution. 15Tm warm solenoid (0.45% partial snake) should work. AGS Solenoid: 4.7Tm and 2.4m long.

## Slide 19: Resonance Strength for Deuterons in Hadron Ring (DEPOL)
From the d-Au run in 2016, the expected rms emittance of deuteron should be less than 2π. The rms orbit error should be under 0.3mm. The resonance strengths are estimated with these beam conditions with run17 pp lattice (Qy=29.673).

## Slide 20: Imperfection Resonance Strength for Three Lattices
The partial snake strength with single and two partial snakes.

## Slide 21: Intrinsic Resonance Strength for Deuterons
Intrinsic resonances with three different tunes.

## Slide 22: Modest Vertical Tune Jump
AGS tune jump system gives change of nx is 0.04 in 100 ms. If we use a similar PS for about 11 times larger rigidity, the expected tune change would be 0.04 in 1140μs or 0.013 in 380μs (30 turns). We actually will use a tune jump system with 0.04 in 50 turns. The resonance crossing speed would be 7E-5, which is 600 times faster than the regular ramp rate in RHIC. One possibility is to use γtr quads.
For an isolated resonance,
And resonance crossing rate is given by:

## Slide 23: Polarization after Each Resonance
At the strongest resonance, normal ramp is better than tune jump.

## Slide 24: Summary
Currently, RHIC proton ring can deliver 60% polarization at 255GeV for collisions with 1.8*1011 bunch intensity.
For the planned various EIC operation scenarios, AGS can deliver 67-70% polarization. Additional polarization gain would come from the newly installed pulsed skew quads system(will be tested in run24).
Polarized 3He+2 development is expected in about two years when the source is available. An AC dipole has been installed in the Booster and tested with polarized proton beam. Its success opens possibility to increase AGS injection energy so that stronger partial snake can be used and more tune space will be available for putting both betatron tunes into spin tune gap.
Polarized deuteron possibility has been explored. The imperfection resonances can be overcome by a solenoid partial snake. The intrinsic resonance can be overcome with modest tune jump. If deuteron beam is determined to be needed, source development should start.

## Slide 25: Backup Slides