## Slide 1: NNL ENDF/B-VIII.1(β2) Validation Testing – ICSBEP Suite
Linden Cotchen, Adam Ney, Jason Thompson, Tim Trumbull, Michael Zerkle

## Slide 2: NNL Validation
NNL ICSBEP benchmark suite: 108 benchmarks, 579 cases
Validation comparisons:
  Reactivity change () relative to benchmark
  Figure of merit indicating change in
    Positive FOM: 8.1βX closer to benchmark
    Negative FOM: 8.1βX further from benchmark
  Correlation of with ATLF, ATFF

## Slide 3: HEU Benchmarks
HMM005 cases 01-04 (Silicon)
HMF007 cases 32-34 (Fluorine)
HMF058 case 1 (Be reflector)
HFM057 cases 3 and 5 (Pb reflector)
HCM
HMF
HST
HMI (4), HMM (11), HMT (4)
Notes: These are the results for the entire HEU suite
B1 and B2 fluorine corrects historical bias on HMF007 Teflon cases
B2 lead leads to degraded performance for HM057 cases 3 and 5
B2 silicon addresses problems reported in B1 in HMM005 (and others)
B2 Be addresses problems reported in B1 in HMF058

## Slide 4: HEU Benchmarks FOM
HMF007 cases 32-34 (Fluorine)
HMM005 cases 01-04 (Silicon) –
resolved in β2
HMF058 case 1 (Be reflected)
resolved in β2
HST007 (Concrete reflected)
HCM
HMF
HST
HMI (4), HMM (11), HMT (4)
Notes: Reiterate updates to fluorine, beryllium, silicon
Better demonstrates improvements to HST007 (concrete reflected, likely due to updates fixes in silicon in B2)

## Slide 5: HEU Benchmarks ATLF vs. C/E – 1
Library | Slope | Intercept | R2
8.0 | -533.3 152.6 | 262.2 72.8 | 0.0393
8.1 β1 | -540.9 225.8 | 327.8 107.9 | 0.0189
8.1 β2 | -344.1 153.5 | 185.9 73.4 | 0.0166
Library | Slope | Intercept | R2
8.0 |  |  | 0.0393
8.1 β1 |  |  | 0.0189
8.1 β2 |  |  | 0.0166
Notes: Increase in mean C/E – 1 in B1, partially corrected in B2, still higher than 8.0
Decreased ATLF slope, intercept for B2

## Slide 6: HEU Benchmarks ATFF vs. C/E - 1
Library | Slope | Intercept | R2
8.0 | -56.1 82.2 | 66.1 62.0 | 0.0016
8.1 β1 | -329.8 119.0 | 309.1 89.7 | 0.0251
8.1 β2 | -156.6 81.3 | 138.8 61.3 | 0.0123
Library | Slope | Intercept | R2
8.0 |  |  | 0.0016
8.1 β1 |  |  | 0.0251
8.1 β2 |  |  | 0.0123
Notes: Increase in mean C/E – 1 in B1, partially corrected in B2, still higher than 8.0
Increased ATFF slope and intercept in B1, partially corrected in B2

## Slide 7: IEU Benchmarks
ICF004 case 1
IMF
ICT015
Notes: Results for entire IEU suite
B2 generally reduces the magnitude of for nearly all IEU benchmarks
Results for entire IEU suite
B2 generally reduces the magnitude of Δ𝑘 for nearly all IEU benchmarks

## Slide 8: IEU Benchmarks |C/E - 1|
ICT015 (various reflectors)
IMF
ICF004
case 1
Bare
Poly
Poly
Beechwood + Cd
Concrete + Cd
Beechwood
Concrete
Perspex
Notes: Unsure of what is going on with last Perspex case – planning to test heavy paraffinic oil TSL for B3

## Slide 9: IEU Benchmarks ATLF vs. C/E - 1
Library | Slope | Intercept | R2
8.0 | 403.1 947.9 | -595.3 467.4 | 0.0051
8.1 β1 | 729.2 841.4 | -628.6 414.8 | 0.0210
8.1 β2 | 738.0 835.2 | -586.1 411.7 | 0.0218
Library | Slope | Intercept | R2
8.0 |  |  | 0.0051
8.1 β1 |  |  | 0.0210
8.1 β2 |  |  | 0.0218
Notes: Incremental reduction in mean C/E – 1 in B1 and B2
Increased slope for B2, intercept roughly constant
Fit parameters have very high uncertainties

## Slide 10: IEU Benchmarks ATFF vs. C/E - 1
Library | Slope | Intercept | R2
8.0 | -106.1 276.5 | -355.7 138.6 | 0.0042
8.1 β1 | -163.7 246.4 | -206.8 123.5 | 0.0125
8.1 β2 | -132.6 245.1 | -172.9 122.9 | 0.0083
Library | Slope | Intercept | R2
8.0 |  |  | 0.0042
8.1 β1 |  |  | 0.0125
8.1 β2 |  |  | 0.0083

## Slide 11: Thermal LEU Benchmarks
LST001 case 1 (UO2F2)
LCT010 cases 1-3, 20-22 (Pb)
LCT
LST
Notes: B1 and B2 fluorine corrects historical bias on LST001 UO2F2
Significant changes in LCT010 Pb-reflected cases in B2
Mean C/E-1 increase, likely driven by LCT010 changes

## Slide 12: Thermal LEU Benchmarks FOM
LCT002
LCT010
(Pb, U, steel reflectors)
LST001 case 1 (UO2F2)
LST
LST002
LST003
LST00(4,7,8,9),
(STACY reflected by water, bare, concrete, borated concrete)
LST016
LST017
Pb reflector
Notes: Reiterate improvement in LST001 due to B1 and B2 fluorine
Reiterate degraded performance of LCT010 Pb-reflected cases

## Slide 13: Thermal LEU Benchmarks ATLF vs. C/E - 1
Library | Slope | Intercept | R2
8.0 | 291.3 269.8 | -25.8 71.7 | 0.0131
8.1 β1 | 354.6 263.4 | -90.8 70.1 | 0.0202
8.1 β2 | 764.8 278.4 | -123.5 74.0 | 0.0790
Library | Slope | Intercept | R2
8.0 |  |  | 0.0131
8.1 β1 |  |  | 0.0202
8.1 β2 |  |  | 0.0790
Notes: Mean C/E – 1 increase in B2
Trends indicating deteriorating performance – increased slope, intercept

## Slide 14: Thermal LEU Benchmarks ATFF vs. C/E - 1
Library | Slope | Intercept | R2
8.0 | 374.9 50.6 | 15.0 30.1 | 0.0063
8.1 β1 | 476.4 64.2 | -42.7 38.3 | 0.0106
8.1 β2 | 1174.4 47.7 | -31.5 28.4 | 0.0541
Library | Slope | Intercept | R2
8.0 |  |  | 0.0063
8.1 β1 |  |  | 0.0106
8.1 β2 |  |  | 0.0541
Notes: Mean C/E – 1 increase in B2
Trends indicating deteriorating performance – increased slope, intercept

## Slide 15: Pu Benchmarks
PMF
PMM002, PMM003
PST
PST:
PST001 (6)
PST002 (7)
PST003 (7)
PST004 (13)
PST005 (9)
PST006 (3)
PST018 (9)
PST022 (17)
PST023 (33)
PST038 (5)
PST039 (8)
Notes: B2 appears to trend high relative to 8.0 and B1 in PST benchmarks
Marginal increase in B2 mean C/E – 1 magnitude compared to 8.0
Sign flip indicates that 8.0 and B1 trended low, B2 trends high

## Slide 16: Pu Benchmarks |C/E – 1|
PMF
PMF042d
PST
PST023
PST039
PST038
PST:
PST001 (6)
PST002 (7)
PST003 (7)
PST004 (13)
PST005 (9)
PST006 (3)
PST018 (9)
PST022 (17)
PST023 (33)
PST038 (5)
PST039 (8)
PMM002, PMM003
Notes: B2 shows degraded performance for PMF, PST up to PST023
B2 shows improved performance for PST023/38/39 except for first case of PST039 – unclear as to cause
Marginal increase in B2 mean C/E – 1 magnitude compared to 8.0
Sign flip indicates that 8.0 and B1 trended low, B2 trends high

## Slide 17: Pu Benchmarks ATLF vs. C/E - 1
Library | Slope | Intercept | R2
8.0 | 1186.7 223.9 | -638.8 105.6 | 0.1495
8.1 β1 | 788.7 221.8 | -449.2 99.8 | 0.0792
8.1 β2 | 312.0 206.2 | 10.9 92.8 | 0.0153
Library | Slope | Intercept | R2
8.0 |  |  | 0.1495
8.1 β1 |  |  | 0.0792
8.1 β2 |  |  | 0.0153
Notes: Significant decreases in slope and intercept in B2

## Slide 18: Pu Benchmarks ATFF vs. C/E - 1
Library | Slope | Intercept | R2
8.0 | 883.9 100.4 | -339.9 40.9 | 0.3451
8.1 β1 | 614.5 100.9 | -259.5 41.2 | 0.2013
8.1 β2 | 244.1 100.1 | 86.2 40.7 | 0.0389
Library | Slope | Intercept | R2
8.0 |  |  | 0.3451
8.1 β1 |  |  | 0.2013
8.1 β2 |  |  | 0.0389
Notes: Significant decrease in slope and intercept for B2

## Slide 19: Poly and Lucite TSL – PMT004
Poly Moderator
Lucite Moderator
Notes: A format issue in ORNL C-CH2 prevented NDEX processing and testing of ORNL (H,C) - Poly

## Slide 20: Poly and Lucite TSL – HMF007
Poly Moderator
Poly Moderator and Reflector
Lucite Moderator
Notes: Similar performance for ORNL and NCSU in poly and lucite moderated configurations
Consistent with PMT004 findings that ORNL predicts higher keff in reflected configurations
A format issue in ORNL C-CH2 prevented NDEX processing and testing of ORNL (H,C) - Poly

## Slide 21: Conclusions
Updates to fluorine in β1 and β2 yield significant improvements over 8.0
Errors introduced in beryllium and silicon in β1 resolved in β2
  Be: HMF058
  Si: HMM005, HMF057
Noted increased bias in LCT010 Pb-reflected cases
Reduction in mean C/E – 1 for HEU and IEU benchmarks, increase for LEU and Pu benchmarks in β2
  Increase in LEU suite mean C/E – 1 due in part to degraded LCT010 performance
  Pu benchmark suite bias flipped from under-predication to over-prediction on average

## Slide 22: Additional Slides

## Slide 23: All Benchmarks

## Slide 24: All Benchmarks FOM

## Slide 25: All Benchmarks ATLF vs. C/E - 1
Library | Slope | Intercept | R2
8.0 | -112.0 111.8 | 4.0 49.6 | 0.0017
8.1 β1 | -103.6 140.2 | 38.7 62.2 | 0.0009
8.1 β2 | -118.3 104.1 | 97.0 46.2 | 0.0022
Library | Slope | Intercept | R2
8.0 |  |  | 0.0017
8.1 β1 |  |  | 0.0009
8.1 β2 |  |  | 0.0022

## Slide 26: All Benchmarks ATFF vs. C/E - 1
Library | Slope | Intercept | R2
8.0 | 196.7 50.6 | -127.8 30.1 | 0.0255
8.1 β1 | 82.9 64.2 | -39.6 38.3 | 0.0029
8.1 β2 | -62.6 47.7 | 76.8 28.4 | 0.0030
Library | Slope | Intercept | R2
8.0 |  |  | 0.0255
8.1 β1 |  |  | 0.0029
8.1 β2 |  |  | 0.0030

## Slide 27: HCM Benchmarks

## Slide 28: HCM Benchmarks FOM

## Slide 29: HCM Benchmarks ATLF vs. C/E - 1

## Slide 30: HCM Benchmarks ATFF vs. C/E - 1

## Slide 31: HMF Benchmarks

## Slide 32: HMF Benchmarks FOM

## Slide 33: HMF Benchmarks ATLF vs. C/E - 1

## Slide 34: HMF Benchmarks ATFF vs. C/E - 1

## Slide 35: HST Benchmarks

## Slide 36: HST Benchmarks FOM

## Slide 37: HST Benchmarks ATLF vs. C/E - 1

## Slide 38: HST Benchmarks ATFF vs. C/E - 1

## Slide 39: ICT Benchmarks

## Slide 40: ICT Benchmarks FOM

## Slide 41: ICT Benchmarks ATLF vs. C/E - 1

## Slide 42: ICT Benchmarks ATFF vs. C/E - 1

## Slide 43: LCT Benchmarks

## Slide 44: LCT Benchmarks FOM

## Slide 45: LCT Benchmarks ATLF vs. C/E - 1

## Slide 46: LCT Benchmarks ATFF vs. C/E - 1

## Slide 47: LST Benchmarks

## Slide 48: LST Benchmarks FOM

## Slide 49: LST Benchmarks ATLF vs. C/E - 1

## Slide 50: LST Benchmarks ATFF vs. C/E - 1

## Slide 51: PMF Benchmarks

## Slide 52: PMF Benchmarks FOM

## Slide 53: PMF Benchmarks ATLF vs. C/E - 1

## Slide 54: PMF Benchmarks ATFF vs. C/E - 1

## Slide 55: PST Benchmarks

## Slide 56: PST Benchmarks FOM

## Slide 57: PST Benchmarks ATLF vs. C/E - 1

## Slide 58: PST Benchmarks ATFF vs. C/E - 1