## Slide 1: Validating TSLs for ENDF/B-VIII.1
Chris W. Chapman
Oak Ridge National Laboratory
Cross Section Evaluation Working Group meeting – 16 November 2023

## Slide 2: Validation Goal
Given an ENDF file, how do I determine whether it is a faithful representation of the real world?
  Compare with and determine agreement with measured data
What is measured data?
  Neutron-induced reactions and integral quantities based on those reactions
  Purpose of this talk is to determine whether there is well-defined, publicly available data to validate TSL files

## Slide 3: Validation Goal
TSLs are a bit different compared to other forms of nuclear data
Inputs for TSLs can also be used as inputs for calculation of other thermophysical properties:
  Density, specific heat capacity, diffusion coefficient, mean square displacement, etc.
These properties can’t be directly computed from information provided in an ENDF file, so won’t be included here

## Slide 4: Validation Hierarchy
Cross section measurements
  Double differential scattering cross section
  Total cross section
Benchmarks
  Quasi-integral (e.g., pulsed neutron die away)
  Integral (e.g., ICSBEP, IRPhEP, etc.)

## Slide 5: List of ENDF/B-VIII.1 TSL Materials
Graphite
  3 different porosities, 2 different crystalline
Fuels
  UO2, UC, UN, & U-metal
    (6 enrichments each)
  PuO2
Liquids
  H2O, D2O, HF
Advanced Moderators
  SiC, FLiBe, CaH2, Be2C, 7Li{H,D}, BeO, ZrC, UH3
Metal Hydrides
  YH2, ZrH1,2,x
Accelerator/Cryogenic Applications
  {para,ortho}-{H,D}, Mesitylene-Phase 2, Toluene, Al2O3, Be-metal (2 types), Ice, Mg, Si, SiO2 (2 types)
Polymers
  Polyethylene, Lucite, Polystyrene, Teflon, Paraffinic Oil
Historic
  27Al, 56Fe, {l,s}-CH4, Benzene

## Slide 6: List of ENDF/B-VIII.1 New or Updated Materials
Graphite
  20% porous, crystalline+SD
Fuels
  UO2 (natural), UN (natural)
  UO2, UN (5 new enrichments)
  UC, & U-metal (6 enrichments)
  PuO2
Liquids
  H2O, HF
Advanced Moderators
  SiC, FLiBe, CaH2, Be2C, 7Li{H,D}, BeO, ZrC, UH3
Metal Hydrides
  ZrH2, ZrHx
Accelerator/Cryogenic Applications
  {para,ortho}-{H,D}, Mesitylene-Phase 2, Toluene, Al2O3, Be-metal, Be-metal+SD, Mg, Si, SiO2 alpha
Polymers
  Polyethylene, Lucite, Polystyrene, Teflon, Paraffinic Oil
Historic
  N/A

## Slide 7: List of Materials
A total of 70 materials* across 112 different ENDF files
  Including 57 new or updated materials across 97 different ENDF files for ENDF/B-VIII.1
How many of these 57 new or updated materials can we validate?

## Slide 8: Least challenging to validate
Multiple benchmarks and cross section measurements
  Light water, polyethylene, Lucite, polystyrene, graphite
  Be-metal, BeO, paraffinic oil, Teflon, SiO2
  ZrH2, ZrHx
  UO2 & U-metal (kind of)

## Slide 9: Slightly challenging to validate
Cross section measurements, but no integral benchmarks (or benchmarks are poorly defined)
  Al2O3, CaH2
  UC, UN (kind of)
  Mesitylene – Phase II, Toluene, Si, Mg, {para,ortho}-{H,D}
Integral benchmarks, but no cross section measurements
  HF, UH3
  PuO2 (kind of)

## Slide 10: Impossible to Validate
No cross section measurements or well-defined public benchmarks
  FLiBe
  7LiD, 7LiH
  Be2C
  SiC
  ZrC

## Slide 11: Fuel TSLs – A Quandary
Fuel TSLs pose a unique problem:
  Which to use in the thermal energy range: TSL or resonances?
  Does choosing one over the other have any unintended side effects (e.g., lack of resonance interference) that are not physical?
Additionally, uranium fuels have multiple enrichments
  Natural (0.72%), 5%, 10%, HALEU (19.75%) HEU (93%), 100%
  Magnitude of the cross section will be different, but will the inelastic spectra be noticeably different?
    If not, is this the best way to represent this data?
Underlying theory needs to be carefully scrutinized

## Slide 12: Path Forward
Of the 57 new or updated TSL files:
  14 are easy to validate
  12 are either lacking cross section or benchmarks
  6 have neither cross section nor benchmarks
  25 are fuel materials that require thorough investigation
What can be done?
  Provide DFT/MD input files for extra validation of material properties?
  Require corresponding measurement (benchmark or cross section) for all materials?
  Look towards other ENDF sub-library standards for validation?

## Slide 13: Conclusions
 | Cross Section Measurement | No Cross Section Measurement
Benchmark | UO2 & U-metal Light water, ZrH2, ZrHx, graphite, BeO, polyethylene Lucite, polystyrene, Be-metal, paraffinic oil, Teflon, SiO2 | PuO2 HF, UH3
No Benchmark | UC, UN CaH2 Mesitylene – Phase II, Toluene, Si, Mg, {para,ortho}-{H,D}, Al2O3 | FLiBe, Be2C, SiC, ZrC 7LiD, 7LiH

## Slide 14: Acknowledgements
This work was supported by the Nuclear Criticality Safety Program, funded and managed by the National Nuclear Security Administration for the Department of Energy.
The entire Nuclear Data team at ORNL (I. Al-Qasir, G. Arbanas, J. Brown, K. Guber, L. Leal, J. McDonnell, M. Pigni, K. Ramić, D. Wiarda)

## Slide 15: Questions?