## Slide 1: Covariance Testing Progress for ENDF/B-VIII.1β1 at ORNL
B.J. Marshall
CSEWG
Brookhaven National Laboratory
November 15, 2023

## Slide 2: Outline
Summary of results presented for β1 at mini-CSEWG
Detailed results for HMF-001 and PMF-001

## Slide 3: Data-induced uncertainty in VALID benchmarks
Historically a check ORNL has used to compare predicted variability with observed variability from benchmarks
TSUNAMI-IP propagates covariance data with sensitivities from benchmarks
The uncertainty is determined by reaction-nuclide pair and summed to determine the total data-induced uncertainty in keff
Examination of results highlights potential concerns with covariance data

## Slide 4: Results by benchmark category
Category | Number of Cases | Avg C/E (CE_V8.1) | Avg Exp. Unc. (pcm) | St. Dev. Of C/Es (pcm) | Avg 1σ XS Unc (pcm) |  | % of Cases Within | 
 |  |  |  |  | E8+SCALE | E8.1+SCALE | Exp. Unc. Band | E8.1+SCALE XS Band
HMF | 50 | 1.00002 | 193 | 467 | 979 | 950 | 34.0 | 96.0
HST | 52 | 0.99900 | 494 | 615 | 652 | 792 | 75.0 | 96.2
IMF | 13 | 1.00132 | 269 | 362 | 1027 | 1003 | 46.2 | 100
LCT | 140 | 0.99874 | 195 | 162 | 603 | 737 | 56.4 | 100
LST | 19 | 0.99920 | 318 | 283 | 824 | 944 | 57.9 | 100
MCT | 49 | 0.99244 | 400 | 313 | 973 | 758 | 18.4 | 51.0
MST | 10 | 0.99177 | 452 | 384 | 1323 | 1019 | 0 | 50.0
PMF | 12 | 0.99902 | 207 | 133 | 1022 | 1038 | 66.7 | 100
PST | 81 | 0.99927 | 497 | 429 | 1344 | 937 | 76.5 | 92.6
It appears that the covariance changes are generally having much larger impacts on thermal systems than on fast systems.

## Slide 5: Small changes…
HMF systems show small differences in general: ~3%
  HMF systems reflected with DU appear to have significant reductions in 235U nubar uncertainty (~400 pcm in E8.0 → ~225 pcm in E8.1)
IMF system uncertainties ~2% lower with ENDF/B-VIII.1β1
PMF systems a little less than 2% higher on average

## Slide 6: Big uranium changes
HST, LCT and LST systems see ~15-20% increases in uncertainty
Directly attributable to ~40% increase in nubar contribution to uncertainty in thermal uranium systems
  ORNL still disagrees with the 1H covariance introduced in ENDF/B-VIII.0 and its associated significant increase in data-induced uncertainty
    Neutron scatter off a proton has measured uncertainty more similar to the older data, references provided by Goran in the past
Plot on next slide shows comparison of ENDF/B-VIII.0 and ENDF/B-VIII.1β1 nubar

## Slide 7: Comparison of 235U nubar uncertainty data

## Slide 8: Big Pu changes
MST, MCT, and PST systems see ~20-30% decreases in uncertainty
All the 239Pu covariance data is totally different
  n,gamma (leading contributor in E8.0) down by 95%
  Nubar uncertainty up by 167%
  Chi down by 80%
  Fission down by >85%

## Slide 9: 239Pu fission, nubar, and n,gamma uncertainties
More than a factor of 30!
More than a factor of 10!
Only a factor of about 2.5.

## Slide 10: Questions on VALID results?

## Slide 11: Detailed results for HMF-001 (“Godiva” simple sphere)
 | ENDF/B-VIII.0 uncertainty (pcm) | ENDF/B-VIII.1β1 uncertainty (pcm)
235U Fission | 787 | 787
235U Nubar | 399 | 382
235U Chi | 33 | 33
235U Elastic† | 224 | 224
235U Inelastic | 239 | 239
235U Capture | 277 | 277
235U Sum | 982 | 975
Exp. Uncertainty | 100 | 100
C-E | 14 | 0
†Accounting for cross correlation with fission |  | 

## Slide 12: Detailed results for PMF-001S (Jezebel simple sphere)
 | ENDF/B-VIII.0 uncertainty (pcm) | ENDF/B-VIII.1β1 uncertainty (pcm)
239Pu Fission | 877 | 920
239Pu Nubar | 317 | 416
239Pu Chi | 179 | 37
239Pu Elastic | 484 | 360
239Pu Inelastic | -119* | 165
239Pu Capture | 64 | 19
Sum | 1061 | 1085
Exp. uncertainty | 130 | 130
C-E | -28 | -116
* Cross correlation between elastic and inelastic is larger than inelastic with itself
Resulting total scattering uncertainty is 469 pcm in ENDF/B-VIII.0 and 396 pcm with ENDF/B-VIII.1β1

## Slide 13: Conclusions
Data-induced uncertainty significantly increased for thermal 235U-fueled systems
Dramatic changes in 239Pu covariance changes for thermal systems are worrying
  Were these the changes that were intended?
Impact of changes on HMF-001 and PMF-001 is small

## Slide 14: Acknowledgment
This presentation was supported by the Nuclear Criticality Safety Program, funded and managed by the National Nuclear Security Administration for the Department of Energy.

## Slide 15: Questions?