## Slide 1: 234,236U Covariance Updates
Ionel Stetcu, A. Lovell, T. Kawano, M. Herman
T-2
November 15, 2023
CSEWG / Brookhaven National Laboratory
LA-UR-23-32705

## Slide 2: General evaluation procedure
Model calculation using CoH3 with Souhkoviskii 2005 potential
Fission: below 500 keV (234U) keep ENDF/B-VIII.0; above that: new fit to include Tovesson 2014 data for 234U. New fit for 236U was also made but it was not included in the evaluation (see 236U fission slide)
Calculation: fission transmission adjusted so that the calculation reproduces the fission data. Point-by-point fit to determine an energy-dependent adjustment
Capture: calculation-based evaluation that reproduces very well the latest measurement by DANCE below 100 keV (234U) and other existing data (236U) . The gamma-gamma width is consistent with the resonance analysis.
All the other channels have been taken from CoH3 calculations
LSSF flag set to 1 for MT=1,18,102. Background cross section in the replaced by full cross section in the URR.
PFNS taken from JENDL-4
PFG properties taken from BeOH calculations
Covariances have been updated based on feedback from Robert Casperson
Notes: 234U fission fit was not included, but it could be included (see the slide on Fission 236U)

## Slide 3
234U
HEU: 1% 234U
The crits are minimally impacted with fine tuning for 238U nubar to compensate for 234U changes included already in the beta2 files

## Slide 4: Uncertainties for inelastic and capture were updated based on feedback and templates of expected uncertainties
DANCE data (Jandel) are still preliminary and the normalization is not fixed. Uncertainties were updated so the magnitude is consistent with ENDF/B-VIII.0 values; covariances from Kalman.
Inelastic uncertainties are set to a minimum of 20%, based off of (n,xn) templates (Vanhoy, et al., EPJ N submitted).

## Slide 5: 234U(n,f)
Small reduction with respect to B-VIII.0 due to Tovesson data
Larger changes (7.5%-8%) around 10 and 15 MeV.

## Slide 6
236U

## Slide 7: Uncertainties for inelastic were updated based on feedback and the templates of expected uncertainties
Inelastic uncertainties are set to a minimum of 20%, based off of (n,xn) templates (Vanhoy, et al., EPJ N submitted).
Fission uncertainties lowered based on data from Tovesson, et al.
Capture uncertainties kept at the same shape and magnitude from ENDF/B-VIII.0 (but updates made to the cross section)

## Slide 8: 236U(n,f)
A new fit performed (adjustment of the transmission coefficients for fission channel has been performed using the old evaluation)
Tovesson data changes a bit the evaluation in the fast region (like for 234U) and lead to lower uncertainties in the fast region

## Slide 9: 236U(n,g)
New DANCE data included in the Kalman fit (Baramsai) but weighted less to not pull evaluation as strongly from 0.5-1 MeV
Notes: Clear outliers not included in the new fit. Fit using Kalman on model parameters. The chi2 values are for B8, B8.1beta1, New fit

## Slide 10: Reaction Rates
A. Lee (LANL) did a reanalysis of the uncertainties for RR shown here (blue, 2𝜎)
RR values for capture decreased by ~8% but are within the 2𝜎 uncertainties
RR values for fission did not change
Other criticality benchmarks do not change significantly
Notes: The X’s are with the new capture (Kalman fit)

## Slide 11: Summary
Inelastic and capture uncertainties have been updated based on feedback from mini-CSEWG and drafts of the Big Paper; covariances still from Kalman but magnitude increased based on recommendations from templates of expected experimental uncertainty
(Mostly) model-based evaluation
Special treatment of the fission channel
Capture data in good agreement with preliminary data by DANCE for 234U, and 236U; however, other data less well described for 236U, in particular above 100 keV. RR in flattop within about 8% from the experimental data.
LSSF changed from 0 to 1 for ; background cross section replaced by the full cross section in the URR

## Slide 12
Backup slides

## Slide 13: 234U(n,tot)
No data available in the fast range
Our OM calculation is larger by 50% than previous evaluation (and JENDL-5) – still investigating, but one could use the earlier Souhkoviskii OM parameters.
The same OM reproduces well the 236(238)U total cross section

## Slide 14: 234U other channels
(n,2n), (n,3n) significantly higher
Some better agreement with JENDL-4

## Slide 15: 236U(n,tot)

## Slide 16: 236U other channels
The cross sections in these channels are:
Significantly higher but seem to follow a pattern (see n,2n comparison between different isotopes)
Same increase observed for 234U