## Slide 1
R. Capote, A. Trkov
on behalf of the INDEN collaboration
https://www-nds.iaea.org/INDEN
Actinide evaluations below 100 keV:
toward ENDF/B-VIII.1

## Slide 2
Changes in the URR for U-235 and Pu-239
New information driving changes in the RRR
Changes in the RRR (see also Marco’s talk)
U-235 evaluation in the RRR
Depletion issue:
  U-238 evaluation in the RRR/URR
  Pu-239 evaluation in the RRR
Outlook

## Slide 3: U-235 URR fission (~2.25-40keV): change important for criticality
ENDF/B-VIII.0 (red)
XS do not reproduce
high-res experimental data
INDEN (gray) uses
High-res Weston 1984 data
Renormalized to STD
Better criticality!! with
similar self-shielding
ENDF/B-VIII.0 are the reference XS (broad average XS)
(n,f) URR: 2.5-5 keV

## Slide 4: Pu-239 URR fission (~2-20keV): change important for criticality
ENDF/B-VIII.0 (red)
XS do not reproduce
high-res experimental data
INDEN (green) uses
High-res Weston data
Renormalized to STD
Better criticality!! with
similar self-shielding
(n,f) URR: 5-20 keV
ext RRR
ENDF/B-VIII.0 are the reference XS (broad average XS)

## Slide 5
Resolved Resonance Region:
Thermal Neutron Constants (TNC)
new ORNL/IAEA/JSI eval.
U3- softer thermal PFNS
Pu9- softer thermal PFNS
following the IAEA CRP recommendations already adopted for U5.

## Slide 6: New integral constraints for RP fit of fissile targets
Duran et al, to be published in NDS, Jan.2024
Discussed at INDEN CMs since November 2021
*From G. Noguere (JEFF-T4 work)
Good consistency with TNC
and Duran et al indep. eval.
Derived f(th)
Duran et al TNC-2018 E812 E80
U3: 533.0(0.7) 533.0(2.2) 533.0 534.1
U5: 586.1(2.6) 587.3(1.4) 586.1 586.7
Pu9: 751.0(1.9) 752.4(2.2) 751.1 747.4
Pu1*: 1019(3) 1024(11) 1024 1012
All measured ToF
high-resolution data
(1955-2019)

## Slide 7
 |  | JEFF-3.3 | ENDF/B-VII.1 | Standards 2017 (2200 m/s) | ENDF/B-VIII.0
239Pu(nth,f) | σs | 7.8 | 7.99 | 7.8±1.0 | 8.1
 | σf | X 749.3 | X 747.91 | 752.4±2.2 | X 747.4
 | σ | 271.4 | 270.7 | 269.8±2.5 | 270.1
 | t | 2.8664 | 2.8807 | 2.878±0.013 | 2.8769
INDEN ST25 (E81b2) vs ENDF/B-VIII.0 vs TNC
U5 ST25 thermal neutron constants:
fission: 586.1 b (-0.11% decrease rel. to B8)
in excellent agreement with Duran et al
capture: 99.4 b, elastic: 14.1 b
νtot= 2.42685 (-0.13% decrease rel. to B8)
INDEN U5 ST25 thermal constants are closer to Standard
thermal neutron constants (but are in agreement with ENDF/B-VIII.0) fission cross section and nubar are slightly reduced

## Slide 8
RRR: additional work undertaken below 20eV to improve agreement with RPI data
Marginal impact on HEU solution criticality (slight increase of high-leakage solutions)
See INDC(NDS)-0810, INDEN-ACT III meeting report
ST25 RRR evaluation in better agreement with new RPI data
than B8 (capture reduced by 8% from 7.8-11eV, by 3-4% from 0.6-9.4eV)
INDEN ST25 contains new resonance
parameter set from ORNL

## Slide 9
Thermal nubar νtot= 2.42685 (-0.13% from ENDF/B-VIII.0 νtot=2.4298)
TNC value : 2.425±0.011, A.D. Carlson et al, Nucl. Data Sheets 148 (2018) 143-188
2. B8 tweak at 2eV eliminated, better description of Reed data in that region
Nubar fluctuations from ~20eV up to 500eV replaced by lin interpolation, Gwin nubar data used from 500eV up to 200 keV (nubar uncertainty significantly reduced in that region).
U-235: changes in nubar below 100 keV
nubar, En  100 eV
nubar, 20eV  En  100 keV
ST25 agrees better with Reed data below 3 eV
ST25 uses Gwin data, nubar unc. greatly reduced
(E81b2)
(E81b2)

## Slide 10
N.A. Kleedtke and A.C.(Skip) Kahler (miniCSWEG & Noah today)
confirmed by our own testing (Trkov), NNL
Validation of U-235 RRR with HST

## Slide 11
Depletion issues in ENDF/B-VIII.0 ( JEFF-3.3)
Kang-Seog Kim and William A. Wieselquist, ”Neutronic Characteristics of ENDF/B-VIII.0 Compared to ENDF/B-VII.1 for Light-Water Reactor Analysis”.
J. Nucl. Eng. 2021, 2, 318–335. https://doi.org/10.3390/jne2040026

## Slide 12
Depletion issues in ENDF/B-VIII.0 ( JEFF-3.3)
Kang-Seog Kim and William A. Wieselquist, ”Neutronic Characteristics of ENDF/B-VIII.0 Compared to ENDF/B-VII.1 for Light-Water Reactor Analysis”.
J. Nucl. Eng. 2021, 2, 318–335. https://doi.org/10.3390/jne2040026
U-238 (-400pcm)
U5, O16, Pu9
-100pcm each
JEFF-33 WG ident.
a similar but larger issue
( Keff = -1500pcm)
INDEN initial focus: U8
JEFF WG initial focus: Pu9
Overall: -500pcm

## Slide 13
INDEN e80V03i4 @ https://www-nds.iaea.org/INDEN/data/u238e80u8V03i4_ENDF.zip
The ENDF/B-VIII.0 RRR is replaced by JENDL-5 RRR evaluation
This update preserves the ENDF/B-VIII.0 BOC criticality but
eliminates the U-238 depletion trend at high burnup
(due to higher capture above 100eV -> higher Pu239 accumulation).
A new nubar evaluation was produced by LANL colleagues
(Neudecker et al). Nubar was tweaked @ IAEA to better reproduce
Jemima trend.
Summary: INDEN e80V03i4 evaluation
Update of the ENDF/B-VIII.0 evaluation (IAEA CIELO)
e80V03i4 eliminates the ENDF/B-VIII.0 trend with burnup, and preserves ENDF/B-VIII.0 criticality at BOC. Check LCT006 for nice trend in INDEN!
Improvements of IMF (e.g., Bigten) and Jemimas

## Slide 14
INDEN e80V03i4 RRR changes
e80V02 – B71
e80V03i4 – JENDL5
A revised B8 evaluation from
Kopecky done for JEFF-4

## Slide 15
U-238 nubar dependence
Convergence between JEFF & INDEN evaluations observed
INDEN latest : u238e80u8V03i4 -> B81beta2

## Slide 16
miniCSWEG-2023, A.C.(Skip) Kahler and N. A. Kleedtke
Validation of U-238 RRR - LCT
kcalc C/E (e812)=0.999530.00274
e810a: ENDF/B-VII.1 RRR (u238e80v02) -200pcm relative to B70
e811: ENDF/B-VII.1 RRR (u238e80v02) -100pcm relative to B70 ~B8
e812: JENDL-5 RRR + new U-238 (tweaked not to this benchmarks) nubar
Improvements confirmed by independent validations (LANL, ORNL, NNL, UPM)
2.6% U5, UO2 pellets, water, Al, lattice

## Slide 17
=INDEN U238 (post b1)
=U238 B8
Uses U238 from B8
Depletion studies (O. Cabellos)

## Slide 18
U-238 burnup issue seems solved,
Pu-239 issue remained
(@ mini-CSWEG 2023)
INDEN CM @ IAEA, May 2023
ORNL/CEA/IAEA collaboration
To produce new Pu239 RP
New RPs for Pu240 and Pu241 provided by G. Noguere (developed for JEFF-4)

## Slide 19
Summary: New 239Pu resonance parameters
ENDF/B-VIII.0 evaluation in the RRR represented a significant performance improvement over ENDF/B-VII.1 for Pu solution benchmark (PST) due to the use of WPEC SG34 resonance parameter set
However, IAEA thermal PFNS recommendation was not used: <EPFNS>(B8)=2.11 MeV vs recommended <EPFNS>=2.08 MeV)
The ENDF/B-VIII.0 f = 747.91 b was lower than TNC-752.4(2.2) b.
________________________________________________________________
A new resonance parameter set ORNL10 was found by Pigni et al (ORNL/IAEA/JSI) that preserves good performance for PST benchmarks (see slide 10) , while matching the TNC within uncertainties and the new softer thermal PFNS derived using a GMA fit which appears well founded.
Constraints:
Differential: TNC, PFNS
Integral: PST (ATLF), RTC (reactivity temp. coeff), burnup

## Slide 20
INDEN p53 contained new resonance
parameter set ORNL10 (B811)
INDEN p53 (E811)
B811 good for PST

## Slide 21: 239Pu RTC-MISTRAL2 experiment, CEA
239Pu ( E)
Modifications to the INDEN p10 (pu239E811) RR fit needed:
subthermal ,   till 1eV (closer to B8)
To improve RTC and  crit. @ high burnup
NOTE: In the light of latest U-238, we must solve Pu239!
Presented by G. Noguere @ INDEN meet.
B811 worse
for RTC

## Slide 22: 239Pu RTC-MISTRAL2 experiment, CEA
ENDF/B-VII.1=JEFF-311: RTC gradient = -0.8 pcm/K - REF
INDEN p10 (E811): RTC gradient = -1.5 pcm/K
E812 (INDEN TM, May 2023): RTC gradient = -0.9 pcm/K
pu239E81nu1 (INDEN): RTC gradient = -0.84 pcm/K (good!)
B813?
B812 too
high
B811 worse
for RTC

## Slide 23
pu239e81b2 (E81b2) tested by Skip
B812 bias +500pcm, reverted nice B8 perform.
Further work needed -> post-2 (nu1)
Also shown in morning talks (Noah, NNL)

## Slide 24
E81b3? (pst +200pcm)
E81b2 (pst +500pcm)
STD: 2.878 (0.013)
pu239e81b2nu1 vs E81b2 changes

## Slide 25
E81b3 (up to -0.4% below 0.25eV)
E81b2 (-0.2% from B8)
STD unc.
0.45%
pu239e81b2nu1 vs E81b2 changes

## Slide 26
INDEN pu239e81nu1 is a new solution
to improve thermal (only) criticality
pst038
pst012
WPEC SG34
Benchmarks
To check
Trend vs ATLF
Thermal
High-leakage PST
~e.g., pst001

## Slide 27
INDEN pu239e81nu1 is a new solution
to improve thermal (only) criticality
Pst034
Pu+Gd
High FEPIT
B812
B813?
X B811

## Slide 28: INDEN & E812 summary @nds.iaea.org/INDEN/
U-235 and U-238 in E81beta2 are ready/validated !
Latest Pu-239,240,241 INDEN/CEA evaluations in B812 are a compromise: better for depletion (not perfect) but worse for PST
U-233 needs improvement (UCT)
INDEN also delivered Si, F-19, Fe, Cr, Cu evals to B812
Validation talks today showed improvement over ENDF/B-VIII.0
Additional comments:
Cu testing showed improvement for HMF (Ealf) benchmarks
O-16: improvement in the evaluated total XS from 5 to 8 MeV needed to improve description of both diff. & integral data

## Slide 29
Attached are the resuts for the ORNL Broomstick experiment:
INDEN29u3 Original LANL Beta2 file (equal to “e80” up to 7.8 MeV)
INDEN29u4 INDEN file with renormalized by 0.968 Cierjacks’ total in the energy range 5.2 - 7 MeV (renormalized using Yaron’s value).
The current INDEN29u4 file performance is similar to JEFF-3.3 for this benchmark up to 7.8 MeV, and equal to LANL Beta2 above this energy. Overall, the performance of INDEN29u4 is the best.
INDEN29u3 Original LANL Beta2 file (equal to “e80” up to 7.8 MeV)
INDEN29u4 INDEN file with renormalized by 0.968 Cierjacks’ total from 5.2-7 MeV (renormalized using Yaron’s value).
O-16: ORNL Broomstick experiment
Need to decrease tot from 5 to 7 MeV
Broomstick experiment C/E problem 5-7MeV

## Slide 31
Criticality validation of INDEN Cu adopted in B81b2
LCT9, 13, 16, 42, 44
IMF020 , 022
ZEUS
ENDF/B-VIII.0 good criticality preserved (blue vs black)
Very
fast
Very sensitive to AD
from 80-300keV (RRR-URR)

## Slide 32
fast HEU (ZEUS)
INDEN Cu evaluation (E81b2):
Zeus benchmarks