## Slide 1: Nuclear Data for Fusion Meeting at the Office of Science Technology Policy
Lee Bernstein
Department of Nuclear Engineering
UC-Berkeley
Nuclear Science Division
Lawrence Berkeley National Laboratory
Nuclear Data Week 2023
November 15, 2023

## Slide 2: Nuclear Data for Fusion Energy Systems
Fusion energy has received an increasing amount of attention from the Biden Administration and due to the achievement of Lawson’s criterion1 and Ignition2 at the NIF.
DOE Fusion Energy Sciences sponsored a new FOA to accelerate fusion energy development.
Rian Bahran (now Office of Science and Technology Policy) convened a meeting to address one of the longest lead time items in advancing fusion research – Nuclear Data
1Abu-Shawareb et al PRL. 129, 075001 (2022).
2A.B. Zylstra et al Nature 601, pages 542–548 (2022)

## Slide 3: Nuclear Data for Fusion Energy Systems
Low-GHG Building Heating and Cooling, including refrigerants with low global warming potential
Net-Zero Aviation, cost-competitive with conventional aviation, including electric and hybrid aircraft and sustainable aviation fuels production
Net-Zero Power Grid and Electrification, including advanced transmission and distribution systems
Alternative Pathways and Circular Economy for Industrial Processes and Fuel Synthesis, including secure supply chains, circular economy innovation and low-carbon steel, aluminum, cement, chemicals, industrial heat, clean water, and electrofuels
Fusion Energy at Scale, cost-competitive with conventional energy
Only place where nuclear shows up

## Slide 4
Office of Science & Technology Policy
May 4, 2023
Fusion Nuclear Data Roundtable
Welcome/General Overview | Rian Bahran (White House Asst. Dir. for Nucl. Tech. & Strategy)
Fusion Technology Overview | Scott Hsu (DOE Fusion Lead)
Interagency Nuclear Data Working Group (NDWG) Overview | Keith Jankowski (DOE-NP)
Fusion and the Current State of Nuclear Data | Lee Bernstein (UCB/LBNL)
Discussion | All Participants
BREAK | 
Materials Damage in Fusion and Nuclear Data | Paul Romano (ANL)
Recent WANDA Discussion (Material Damage) | Cathy Romano (Aerospace)
Relevant International Nuclear Data CRPs | J-C. Sublet (IAEA-NDS)
Discussion | All Participants
BREAK | 
Path Forward | All Participants

## Slide 5: BLUF: Several Nuclear Data Needs have already been identified
Tritium breeding
  (n,t) cross sections
  Multiplying materials
Neutron-induced damage, gas production & activation
  Containment vessel (All)
  Magnets (MCF)
  Optics (ICF)
Electronics/Sensor damage
  Ion stopping powers (All)
TN reactions
  Polarized D+3H (Helion)
A number to keep in mind:
A 2 GWe fusion power plant will liberate 106 g of 14 MeV neutrons every day!
What new energy differential measurements are needed?
What sort of integral benchmarks are needed?
Are there significant holes in the compiled data?
Who are the domestic partners (e.g., stewardship science, fast reactors, nonproliferation)?
Who are the international partners?

## Slide 6: Tritium Breeding is one of the top issues identified by the fusion community
Goal is to produce 1.1-1.2 3H per neutron!
  Multiplication is a MUST → data for Pb, Zr…
First principles review of options for tritium breeder and neutron multiplier materials for breeding blankets in fusion reactors
F.A. Hernandez⁎, P. Pereslavtsev
6Li(n,t)a
Old Evaluation
New Evaluation
Thanks to Mike Loughlin & Paul Humrickhouse (ORNL)
Thanks to Mark Paris (LANL)
The 6Li(n,t)a evaluation is a recent success:
How well do we know these cross sections?
  Do we need measurements?
  Do we need improved compilation?

## Slide 7: Fusion displacement damage and gas production will be MUCH larger than fission and involve different (n,x) reactions
J.-Ch. Sublet et al., Eur. Phys. J. Plus (2019) 134: 350
neutron

## Slide 8: Cathy Romano reviewed the Findings and Recommendations from the WANDA 2019 Materials Damage Session
ENDF is missing data for recoils and (n,α)
      Inaccurate (n,α) data caused serious miscalculation of materials lifetimes
Need to understand how changed materials properties change the neutronics
      Transmutation, Porosity and Chemical bonds
Processing of the data in NJOY needs modernization to meet the needs of the fusion community
Current models do not determine the size of vacancies
Stopping Powers are not well understood
Radionuclides produced under transmutation might create further Primary Knock-on Atoms (PKAs) as they decay, and so the rate of these must also be quantified.
      Gilbert, Mark & Sublet, Jean-Christophe. (2016). PKA distributions: Contributions from transmutation products and from radioactive decay. Nuclear Materials and Energy. 9. https://doi.org/10.1016/j.nme.2016.02.006
Inelastic Scatter cross sections need to be improved for fast neutron transport calculations
Secondary particle production is not well known and requires measurement and theory development
GRIN

## Slide 9: WANDA 2019 stated that the goal would be an integrated model using current data to guide the design of nuclear energy systems
Sublet, J.C., Bondarenko, I.P., Bonny, G. et al. Neutron-induced damage simulations: Beyond defect production cross-section, displacement per atom and iron-based metrics. Eur. Phys. J. Plus 134, 350 (2019). https://doi.org/10.1140/epjp/i2019-12758-y
Integrated models with correct data (including nuclear data!) at different length scales together with links to neutronics and thermal properties are needed to provide an advanced modeling capability

## Slide 10: Paul Romano (ANL) described how we get from nuclear data to dpa
Thanks to Paul Romano (ANL)

## Slide 11: Paul Romano (ANL) described how we get from nuclear data to dpa
Thanks to Paul Romano (ANL)
Can we get data that includes both the nuclear and atomic data?

## Slide 12: Microcalorimeters together with DT-Associated Particle Imaging neutron source could measure sDPA and gas production measurements including stopping power info
Cryogenic µcalorimeter
Absorber
Sensor
SQUID
Multi-MeV
(n,p) & (n,a)
ejecta
10’s of keV recoils
a
DT neutron sources with Associated Particle Imaging (DT-API)
neutron
Note that sDPA has never been measured directly before...
Etcheverry Hall
Sample Irradiation
Vault (UCB)
…and these sorts of measurements would include stopping powers